## Slide 1: Designing of e- Beam Test Facility at ThomX
Andrii Pastushenko

## Slide 2
Outline
ThomX project
Re-matching of TL
ThomX upgrade: e-BThX

## Slide 3
ThomX project
ThomX is a light source based on CBS (Compton Back Scattering).
Machine is designed to fulfill two goals:
  Maximize the average X-ray flux
  Provide a compact, reliable and tunable source which can operate in museums, hospitals, etc.
Includes injector, collector ring, laser and Fabry-Perot resonator as shown on Fig.1.
Fig.1.Schematic diagram of ThomX experiment

## Slide 4
ThomX machine layout
Electron part of the machine include:
Dipole magnets to steer the beam along the beampipe.
Quadrupole magnets to control beam transverse spread.
Sextupoles to correct chromaticity
We are interested only in beam dynamic along the machine. Whole machine can be divided into 3 parts:
TL (transfer line) – we understand one that starts at the end of linac
Collector ring
Extraction line

## Slide 5
ThomX machine: elements overview
Magnet type | Dipole | Injection dipole | Septum
Number | 4 + 8 | 2 | 1
Bending angle | 45° | 9.69° | 4.59°
Bending length | 0.276 m | 0.2 m | 0.126 m
Gap | 40 mm |  | 
Pole faces rotation angles, φb/φe | 0°/0° | 0°/9,69° | 0°/4.59°
Fringe field integral | 0.348 | 0 | 0
Dipole magnets
Magnet type | Quadrupole
Number | 7 + 24 + 2
Strength | -18 ÷ 18 T/m
Length | 0.15 m
Gap | 41 mm
Quadrupole magnets
Magnet type | Quadrupole
Number | 6
Strength | -0.124*108 ÷ 0.124*108 T/m
Length | 60 mm
Gap | 42 mm
Sextupole magnets

## Slide 6
ThomX machine layout: ring
Ring parameters | value
Circumference | 16.8m
Nominal energy | 50 MeV
Betatron tunes, nx/nz | 3.17/1.74
Beta max, βx/βz | 11/11 m
Bunch storing time | 20 ns
Beam is injected and extracted using fast injection method. For this purpose 2 kickers and septum is installed in the ring.
Proper extraction is important here because of big experimental noise!

## Slide 7
Re-matching of TL
Fig.2.Twiss parameters for the ring calculated in MadX
Starting point for this calculations is injection point or middle of the septum.
IP
Inside the ring we search for a periodical solution.
Values obtained here we use as the final condition for TL as well as initial for extraction line.

## Slide 8
Re-matching of TL
From linac
TL parameters | value
Length | 13.5m
Nominal energy | 50 MeV
Phase advance, nx/nz | 4.48/0.6
Beta max, βx/βz | 39/74 m

## Slide 9
Re-matching of TL
Fig.4.Twiss parameters for the TL calculated in Madx
Initial conditions for TL is values at the exit of the linac and are following:
βx = βz = 34 m
αx = αz = - 4.2
The ring and TL are matched to have equal beta and alpha functions at septum position using Madx. This values are obtained from previous calculations and are following:
βx = 4.64
βz = 2.45
αx ~ 0
αz ~ 0

## Slide 10
ThomX machine layout: extraction

## Slide 11
ThomX machine upgrade: e-BThX
There is growing interest for use of electron beams in the energy range of few tens of MeV up to hundreds of MeVs.
e- line
Biomedical:
New radiotherapy approaches
Detector developments
Space:
multipactor
Other
This large multiplicity range requires a large flexibility of the beam parameters in this kind of Beam Test Facilities and many different diagnostics devices.
Electron Beam Test Facility at ThomX (e-BThX)

## Slide 12
ThomX upgrade: e-BThX
e-BThX is supposed to start at the end of a straight section of TL after injection from linac as shown on Fig.4
Fig.4.Red cyrcle indicate where the e-BThX starts
The beam will be transported until the halls TD3 and TD4 as shown on Fig.5.
Fig.5.Experimantal halls

## Slide 13
ThomX upgrade: e-BThX
Fig.6.The beam transfer line from exit of the linac until the entrance of experimental halls TD3 and TD4
In this case avoiding any beam losses while transferring beam through shielding walls is crucial.
Two e-beam experimental lines are being proposed, the first one will be a spectrometer line and the second one a multidisciplinary line.
We will concentrate on optics calculations after exit of the TL and before entering the experimental halls, on that part that is shown on Fig.6.

## Slide 14
ThomX upgrade: e-BThX
For this part of the line we have limits on beta function values because of the size of beam pipe. Limits are following:
βx < 70 m
βz < 30 m
The beam pipe goes through 2 walls we do not much possibilities to place focusing elements there. One of the solution is to place them before and after the walls.
We consider 3 options:
1) triplet and doublet:
1) two triplets:
1) two doublets:
Forbidden area
In the calculations we take the same quads as in ThomX machine.
Existing triplet

## Slide 15
ThomX upgrade: e-BThX
1)First option – quads triplet and doublet
Some of the Madx output plots with different final conditions
For this option, iteration over final conditions was mad to see if such configuration fulfill all requirements.

## Slide 16
ThomX upgrade: e-BThX
1) triplet and doublet
Beam envelope for the final conditions betx/bety = 15/15 m
Vertical plane
Horizontal plane

## Slide 17
ThomX upgrade: e-BThX
2) Two quadrupoles triplets
On the plots we see that this configuration is not as good as previous one but fulfills all requirements
Some MadX output for triplet-triplet configuration for different final conditions

## Slide 18
ThomX upgrade: e-BThX
2) Two quadrupoles triplets
Beam envelope sample for final betx/bety = 25/15 m:
Vertical plane
Horizontal plane
Maximum beam size is:
2.2 mm - x plane
1.8 mm - z plane

## Slide 19
ThomX upgrade: e-BThX
3)Two quadrupole doublets
As we see on this plot, 2 doublets is not enough to fulfill all constraints we defined, so we cant use it.