## Slide 1
Status: Cooling of the ILC e+ target
by thermal radiation
POSIPOL2016, LAL, Orsay
16th September 2016
Felix Dietrich, Alexander Ignatenko, Sabine Riemann (DESY),
Andriy Ushakov (Hamburg U), Peter Sievers (CERN)

## Slide 2: Outline
Status
  Radiative thermal cooling of e+ target
  temperature distribution
  Design considerations – update
Summary

## Slide 3: e+ target for Ecm = 250 … 500GeV
Ecm and luminosity determine energy deposition in target
Ø = 1m; 2000rpm, 0.4X0 Ti6Al4V (Pe+ ≤30%)
Edep ≤ 7kW  cooling by thermal radiation is an option
Polarization upgrade:
  higher peak load  higher peak temperatures
  higher average temp in target
Ebeam [GeV] | Edep [kW] | DTmax/pulse [K] | dpa | Edep [kW] | DTmax/pulse [K]
 | Nominal luminosity |  |  | High luminosity | 
120 | 5.0 | 66 | 0.035 | - | -
175 (ILC EDMS) | 3.9 | 125 | 0.06 | - | -
250 (ILC EDMS) | 2.0 | 130 |  | 4.1 | 195
250 | 2.3 | 85 | 0.05 | 4.6 | 128
A. Ushakov,
Update 2015
A. Ushakov,
2015

## Slide 4
Ti6Al4V
Radiator
Cooler (Cu)
photons
Radiative cooling model so far
e+ target located close to FC
Rotating wheel consists of Ti rim (e+ target) and Cu (radiator)
Heat path:
  thermal conduction Ti  Cu
  Thermal radiation from Cu to stationary water cooled coolers
Target, radiator and cooler are in vacuum
Radiating area is adjusted by fins
Goal:
keep target temperature
below limit for failure
of Ti6Al4V
Reliable fatigue limit at
elevated temperatures?
Felix Dietrich
Sketch, no technical drawing!

## Slide 5: Temperature development in target (+radiator)
200 400 600 800 1000 1400
T [C]
FEM to calculate temperature evolution in real model; here ‘estimation by hand’
Material parameters c, l, e depend on temperature and long-term load
Heating due to
energy deposition
Thermal conduction
through material
Radiation from
surfaces
K.C. Mills, 2002,
Recommended Values of
Thermophysical Properties
For Selected Commercial
Alloys, p. 217,
referenced by J. Yang
Specific heat [J/(kg C)]
Thermal conductivity [W/(m C)]
200 400 600 800 1000 1400
T [C]

## Slide 6: Temperature development in target (+radiator)
FEM to calculate temperature evolution in real model; here ‘estimation by hand’
Material parameters c, l, e depend on temperature and long-term load
Heating due to
energy deposition
Thermal conduction
through material
Radiation from
surfaces
Boivineau et al., Int. Journ.
of Thermophysics,
Vol. 27, No.2 March 2006

## Slide 7: Heating to equilibrium
Neglect heat conduction and thermal radiation  average T in material increases
Assume 2.3kW at target
  target rim height h = 2cm (4cm)
   Vrim ~ 924cm3 (1.8dm3)
  Average rim temperature Tave = 300C (DT=270K) reached after
    254sec (~4.2min) for h=2cm;
    497sec (~8.3min) for h=4cm
  Heating of rim+radiator takes correspondingly longer
Taking into account thermal radiation and time for heat transfer to radiator, few hours needed to achieve equilibrium (see our talks at POSIPOL14+15 and LCWS15 and Felix’ talk)

## Slide 8: Thermal radiation
So far, we concentrated in our T4 cooling models on radiation from radiator by optimizing the design towards a large area with fins, but there is also substantial thermal radiation off the rim
  low heat conductivity of Ti  high average temperature of rim
  despite small rim area substantial cooling by thermal radiation off the target rim
Taverage[°C]
Consider radiation off target rim only,
r = 0.5m, h=2cm, d=1.5cm
A ~ 0.17m2, e = 0.6
2.3kW  Ttarget (ave)~530C
e=0.6

## Slide 9: Heat transfer target to radiator
Spinning target ~6.5s between load cycles
  Heat moves ~ 0.5cm in 6.5sec
   accumulation of heat in the target
Temperature flow to radiator depends on s
  Average heat transfer through rim
  Acontact ~470cm2, l~10W/(m K)
  dQ/dt = 2.3kW: Tmax-ave (Ti) – Tcontact ~ 100K (s=1.5cm)
  ~ 150K (s=2.5cm)
  Additional cyclic temperature rise by pulse (80…200K)
Cyclic peak temperatures in target can exceed 500˚C, in particular for large s
  need design with short heat transfer path through Ti rim to keep the average Ttarget as low as possible
  for high power deposition ( high lumi) even average temperature could be >500C
Ti
Cu
s
Ti
Cu

## Slide 10: Estimated average temperature in T rim and Cu radiator
Consider thermal radiation from rim and radiator
  Case (1): rim 0.082m2 + radiator 1m2
  Case (2): rim 0.082m2 + radiator 2m2
  Case (3): Only rim, 0.16m2; no radiator
  Emissivity e=0.6
  Estimates give the principal behavior and only approximate temp values. Real temperatures need simulations, they depend on radiator design and Ti-Cu contact
Chart: 
| 1 | 2 | 4 | 6 | 8
Trim (1) | 195 | 292 | 436 | 550 | 644
Tradiator(1) | 157 | 220 | 297 | 344 | 383
Trim (2) | 150 | 235 | 370 | 483 | 580
Tradiator (2) | 111 | 160 | 222 | 262 | 293
Trim (no radiator) | 389 | 510 | 655 | 752 | 830
Edep[kW]
Tave[K]

## Slide 11: Percentage of power radiated by target rim
  Case (1): rim 0.082m2 + radiator 1m2
  Case (2): rim 0.082m2 + radiator 2m2
Depending on energy deposition, target rim size and radiator area, thermal radiation off the rim is efficient and can reach 35% of Edep
Chart: 
| 1 | 2 | 4 | 6 | 8
Prim[%](1) | 11 | 13 | 17 | 20.9 | 24.4
Prim[%](2) | 7 | 8 | 11.5 | 14.8 | 18.2
Edep[kW]
Prim-rad[%]

## Slide 12
Due to low thermal conductivity of Ti6Al4V, peak and average temperatures in target are substantially determined by target dimension (height)
Ti-Cu contact as well as radiator surface are important to remove the heat
However
  we need a heavy wheel (>100kg) to provide a radiator area of ~2m2
  A lower radiating surface of 1m2 increases the average temperature in the target by only ~70K.
  Reduction of # of fins by factor 2 reduces wheel weight by ~20kg
Idea: Are higher target rim temperatures acceptable?
  After our first target material tests we feel encouraged to accept higher target temperatures.
  Similar approach is followed by M. Breidenbach
Stress resistivity at elevated temperatures??

## Slide 13: Target studies at SLAC (M. Breidenbach, M. Oriunno)
(See also Marty’s talk at LCWS15)
Approach:
use high T material Ti-SF61
Study for P = 7.74kW
1312 pulses with 10Hz
Transient with emissivity 0.4
l (W.m-1.K-1) | e = 0.4 | e = 0.6
21 | 894 (621) | 814 (541)
8 | 984 (711) | 904 (631)
Private communication after LCWS15

## Slide 14: Stress in target and radiator
Depends on:
  design
  Load by pulse  Instantaneous and average heating
  Rotation
  Eddy current
  Imbalances (ignored so far)
Stress resistivity at elevated temperatures??
  Thermal and mechanical stress limits for target and radiator material at high temperatures, under irradiation

## Slide 15: Stress due to heating
Instantaneous heating
  Pulse  DT = 80K … 200K
  Ti rim s ~ 100…260MPa
  ILC e+ target: ~2×106 loads per year (4000h) 
  fatigue stress limit for Ti alloy ~600MPa at room temperature but considerably lower at elevated temprature
Average heating
  Depends on design
  Heated rim and radiator:
    Hoop stress in ring: sH = E a DT if expansion is prevented
      Ti rim @ 500C  sH would be ~420MPa
    Expansion of rim + radiator is not restricted  increase of rim circumference u,
    Du = 1.3cm (Dr = 2mm)
  Spatial expansion Vrim(heated) = g·V20˚C·DT
    Ti: DV ~ 1.2% for DT=500K (~ 2% for 850K)
    Cu: DV ~ 6.6% for DT=200K (~ 11.5% for 350K)

## Slide 16: Further stress load
Cu
Rotation  tangential and radial forces
  thin ring approximation for target rim: st ~ rr2w2 = 50MPa
  Assuming sliced target, (~40 pieces for nominal lumi),
  height ~2cm (3cm)  Fc=mrw2 ~2.2kN (3.3kN)
  With connecting area A~12cm2  s~2MPa (3MPa)
   no problem
 Sliced target
  minimizes stress in (non-uniformly heated) target rim and radiator
  Main stress contribution from cyclic energy deposition by photon beam
  Ti-Cu contact
  must work well for all temperatures
  Calculation of stress at the contact Ti to radiator needs FEM methods
  Possibilities considered
    Peter’s proposal: use bolts + plate springs
    Felix’ (also Marty Breidenbach’s) proposal: use multiple dovetail connection for tight connection between Ti and Cu
    Status and more details in Felix’ talk
Ti

## Slide 17
Eddy currents
  See talks at ALCW15, POSIPOl15
  no problem for 5Hz, tpulse~1ms, and 0.5T at target
  Pulsed braking power  intermittent force on the target shaft and bearings (P. Sievers: ~100N in 1ms)
     tight control of the wheel velocity, motor torque
     vibrations have to be studied

## Slide 18: Expected target load in the first years
Running scenarioH-20 start with Ecm=500GeV (500fb-1), followed by Ecm=350GeV (200fb-1); and 250GeV (500fb-1); 1326 bunches per pulse during the first years.
Average E deposition: 2.3kW (500GeV), 3.9kW (350GeV), 5kW (250GeV)
   Estimated peak temperatures for 2m2 (1m2) radiator area:
    ~400C (500C) at 500GeV
    ~450C (550C) at 350GeV
    ~470C (570C) at 200GeV, 5Hz, 230m undulator length
Cyclic load stress due to g beam ≤200MPa (nominal L, no e+ pol upgrade)
Beam test studies at microtron in Mainz show that Ti6Al4V should stand this

## Slide 19: Ti alloy parameters at high temperatures
Ti6Al4V (http://asm.matweb.com/search/SpecificMaterial.asp?bassnum=MTP642 )
Ti-SF61(Ti-5.9Al-2.7Sn-4Zr-0.45Mo-0.35Si-0.22Y), see also http://amt-advanced-materials-technology.com/materials/titanium-high-temperature/ :
  “This Titanium alloy could be used up to 620°C for long service times. …highest creep resistance … The fatigue strength is very high up to 820°C…”
 | r [g/cm3] | l [W/mK] | a [10-6/K] | Tmelt [C] | E [GPa] | UTS [MPa] | YS [MPa] | Elong [%] | Fatigue [MPa, 107] | b-trans. [C]
 |  |  |  |  |  | RoomTemp |  |  |  | 
Ti-SF61 | 4.56 | 6.7 | 8.3 | 1650 | 120 | 1068 | 1050 | 11 | 195@760C | 
 |  |  |  |  |  | 600C |  |  |  | 
 |  |  |  |  |  | 752 | 655 | 16 |  | 
 |  |  |  |  |  | Room temp |  |  |  | 
Ti6Al4V | 4.43 | 8 |  | 1604 | 113.4 | 950 | 880 | 14 | 510 unn. 240n. | 980

## Slide 20: Thoughts for improvements
Assuming radiator surface of 1m2,
  at least 20-40% of the deposited power are radiated from the target rim
  average target temperature increases less than 100K in comparison to 2m2 radiator area
Ti6Al4V seems stable up to T~700C average temperatures (see our material tests at MAMI, Alexandr’s talk)
Use Ti alloy developed for high temperature applications ? (M. Breidenbach: Ti-SF61)
High temperature Ti alloy + lower radiator area  Optimization of target shape? Increase radiating target area by factor 2 or ~1.5
(Rough sketches, no technical drawings!)
Split target in 2 parts and add a stationary cooler fin between them outside the beam area
 Lower e+ yield due to larger effective distance to
FC (but this could help to increase e+ polarization)
A. Ushakov estimate: Yield reduction by ~10% for
10mm gap between target parts
Do not touch beam path region but increase outer target
surface

## Slide 21: Summary
Radiative cooling will work
  Under study:
    Efficient contact between target rim and radiator
    Optimize target+radiator surface + material
    Mechanical issues
Polarized positrons
  Realistic undulator spectrum (see Khaled’s and Ian’s talks)
  Polarization upgrade
    PEDD and target design
    photon collimation?
    Polarization measurement at the e+source
Cyclic load tests at MAMI (see also Alexandr’s talk)
  Check target material properties at high temperatures and high load
    Target and exit window material
Photon dump
  … was not subject of this talk
  ‘Extrapolation’ of photon collimator studies (see http://arxiv.org/abs/1412.2498 ) show that a graphite dump is possible, but should be either moved (as the dump window) or consist of cooled rods

## Slide 22
Thank you!

## Slide 23: Temperature distribution at the target rim
adjust revolution frequency to distribute energy deposition almost uniformly over rim
for example:
  bunch train occupies angular range qpulse
  frev = 1922rpm instead of 2000rpm
   pattern: 1st second: 0, 144, 288, 72, 216,
  2nd second: 0 + qpulse ….,
  3rd second: 0 + 2qpulse ….
  after ~7s the rim is almost uniformly heated
  unbalances due to non-uniform heating are avoided