## Slide 1
The Extremely Brilliant Source project
Project Overview
P Raimondi
On behalf of the EBS Accelerator Project Team

## Slide 2: Outline
ESRF-EBS Project
  Storage Ring characteristics
  Project management
Main EBS accelerator components
  Girders, magnets, vacuum chambers, absorbers, FE
From Assembly to Installation
Conclusion
Notes: Simplify, complete

## Slide 3
Storage ring
6GeV, 844 m
Booster synchrotron
200 MeV  6 GeV
300m, 10 Hz
E- Linac
200 MeV
32 straight sections
DBA lattice
42 Beamlines
12 on dipoles
30 on insertion devices
72 insertion devices: 55 in-air undulators, 6 wigglers, 11 in-vacuum undulators, including 2 cryogenic
Energy | GeV | 6.04
Multibunch Current | mA | 200
Horizontal emittance | nm | 4
Vertical emittance | pm | 3.5
Accelerator and source division (ASD) mission
ESRF Today

## Slide 4: The EBS Storage Ring characteristics
reduced by
a factor of 30
 | Now | EBS
Energy (GeV) | 6.04 | 6
Multibunch current (mA) | 200 | 200
Circumference (m) | 844.39 | 843.98
Horizontal emittance (nm.rad) | 4 | 0.13
Vertical emittance (pm.rad) | 4 | 5
e- beam properties
The Extremely Brilliant Source Project aims to:
Substantially decrease the store ring equilibrium horizontal emittance
Increase the source brilliance
Increase coherent fraction of the beam
(reduce electricity consumption)

## Slide 5: EBS – Reduction of the horizontal emittance
Reduction of the horizontal emittance from 4nm.rad to 0.14nm.rad
Experiments can benefit from : an increase in brilliance
an increase of coherence
(the coherent fraction of the light in the horizontal plane)

## Slide 6: New lattice vs present ESRF lattice
Present ESRF lattice Double Bend Achromat = (2 dipoles + 15 quad. sext.) per cell ID length = 5 m (standard) / 6m / 7m
Future EBS lattice Hybrid 7 Bend Achromat = (4 dipoles + 3 dipole-quad + 24 quad., sext., oct.) per cell ID length = 5 m
31 magnets per cell instead of currently 17!
present
Dipole
Dipole-quadrupoles
future
Dipole
Dipole
Dipole
Dipole
Dipole

## Slide 7: EBS lattice – engineering challenges and constraints
Main engineering challenges:
Fit in the same tunnel. Same circumference.
Insertion devices at the same locations: keep beamlines where they are!
Little space between magnets, i.e. 3.4 m/cell instead of 8 m/cell today!!
Re-use injector complex
High precision & high stability positioning requirements
Little time for the project and in parallel to the normal operation of the facility
Dipoles-quadrupoles
EBS
Dipole
Dipole
Dipole
Dipole

## Slide 8: EBS time line (2016-2020)
10/12/2018 – Start of shutdown
11/11/2019 – Start of machine commissioning
January 2017-June 2018 – Delivery of components
May-July 2020 – Friendly Users
25/08/2020 – Start of USM
2018 is a normal year for Operation, except for shorter summer and October shutdowns
10 December 2018 Potential start of the long shutdown, dismantling starts
11 November 2019 Commissioning starts
02 March 2020 Beamline commissioning starts
25 August 2020 Back to USM
Milestone: Decision on shutdown date
Notes: Update

## Slide 9: Main EBS accelerator components

## Slide 10: Girders
Four girders per cell to install:
Magnet supports
Magnets
Vacuum equipment
Diagnostics
Bare girder weight: ~6t
Fully equipped girder: ~12-13t
129 girders in total
5100mm

## Slide 11: Girder design
There is 1 degree of hyperstaticity in the vertical direction managed by the girder “flexibility” for small displacements.
Z feet optimised for maximum stiffness
Courtesy: Filippo Cianciosi
Girder supported by 4 adjustable Z feet made of motorised wedges
Y adjustment by 2 manual jacks pushing the girder
X
Z
Y
Motorized Z adjustment resolution 5m
Manual Y adjustment resolution 5m
1st natural Eigen frequency:
- 50 Hz (design goal)
- 49 Hz measured

## Slide 12: Supports
Vertical shims
Support & Adjustable wedges for
Dipoles Quadrupoles & Quadrupoles
Moderate gradient magnets
Longitudinal gradient Dipoles
Vacuum chamber supports

## Slide 13: QF6/QF8- DQ supports – DL supports
QF6/QF8 supports
Base
support
Dipole support assembly
Top Frame
Courtesy: L Eybert

## Slide 14: Magnets
132 Dipoles
100 Dipole-quadrupoles
524 Quadrupoles
(132 HG, 392 MG)
196 Sextupoles
98 Correctors
66 Octupoles
More than 1000 Magnets to be produced

## Slide 15: ESRF EBS (2015-2022): magnets procurement
132 dipoles
99 dipole-quadrupoles
196 sextupoles
100 correctors
66 octupoles
130 high gradient quadrupoles
398 moderate gradient quadrupoles
All contracts in place, magnets in fabrication
All preseries successful, first batches of serial productions already at ESRF
More than 1000 Magnets to be procured by the end of 2018

## Slide 16: Implementation in Chartreuse Hall
PM assembly tool
Dipole assembly area
PM Dipoles have been assembled by ESRF staff
More than 650 Magnets Modules for a total of about 128+4 5-Module dipoles
All Dipoles have been already completed

## Slide 17: Vacuum chambers
Three main families of chambers:
High profile aluminium chambers (dipole magnets + other)
High profile stainless steel chambers
(quadrupoles, sextupoles, octupoles)
Low profile stainless steel chambers
(inside combined dipole-quadrupoles
& HG quadrupoles)
13mm
20mm
Low profile cross section
High profile cross section
Diagnostic chambers
Possible location
In situ bake-out

## Slide 18: Girder 1: detailed vacuum chamber & supports
BPM1 (fixed) support
Sector valve
sliding support
CH3- crotch 1
BPM2 (fixed) support
CH4 BPM3 (movable) support
Courtesy: L Eybert
(Dipole Chambers intermediate
basic support not represented)
Chamber flexible support
Bellow

## Slide 19: Vacuum chambers integration with Magnets
CH5 Dipole
Aluminium chamber
(section inside sextupole)
CH6
316LN chamber
(section inside DQ1C)
Limited space between
Magnets and chambers
Minimum thickness required
Deflection (vacuum)
Material stresses

## Slide 20: Vacuum pumps
IP & NEG Pumps |  | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH 8 | CH9 | CH11 | CH12 | CH13 | CH14
IP | 55 l/s |  |  |  |  |  |  | 2 |  |  |  | 1 |  | 
 | 75 l/s | 1 | 1 | 1 | 1 | 1 | 1 |  | 1 | 2 |  | 1 | 1 | 
NEG | GP100 |  |  |  |  |  | 1 |  |  |  |  |  |  | 
 | GP200 |  | 2 |  |  | 5 |  |  | 1 | 2 |  |  | 2 | 

## Slide 21: RF fingers
Patent pending
8 different bellows = 8 different RF Fingers
Close collaboration with the vacuum chamber designer
FEA model
Prototype tested, additional tests in progress
Design completed
P Brumund,T Brochard, L Goirand, J Pasquaud

## Slide 22: Vacuum chambers – Diagnostics
H stripline
V stripline
Shaker
Beam losses collimator
Current transformer
Procurement in progress
1
2
3
5
5
J Borrel
4

## Slide 23: EBS photon absorbers
Photon Absorbers
Synchrotron radiation
E Beam
Absorber flange mounted on the ante-chamber
~391 absorbers
Total power to be absorbed: 504.5 kW (30 x 15.795 kW + 2x 15.314) kW
Power density: 10 to 110 W/mm2
 moderate power parameters compared to current ESRF
D. Coulon, Y. Dabin, Th. Ducoing, E. Gagliardini, Ph. Marion, F. Thomas
Tight space constraints

## Slide 24: Absorber design: two families
Toothed (up to 110 W/mm2)
Frontal (up to 50 W/mm2)
ABS CH9-1-29
ABS CH4-1-1
ABS CH5-1-1
ABS CH13-1-13
Crotch 1
No welding, no brazing
D. Coulon, Y. Dabin, Th. Ducoing,
E. Gagliardini, Ph. Marion, F. Thomas

## Slide 25: Straight sections
Straight sections
5m AL chamber [1]
2 In-vacuum undulators [2]
Invac & Al chamber [3]
RF cavities [4]
[1]
[2]
[3]
[4]
B Ogier, P Ponthenier

## Slide 26: Front-ends
Courtesy of J Pasquaud
Front-end design completed for:
SR junction chambers
BM FE photon shutter unit
42 Front-Ends
28 ID FE’s
14 BM FE’s
Insertion Devices FE
Bending Magnets FE

## Slide 27: Mock-up: Magnets overview
Courtesy: L. Eybert

## Slide 28: Mock-up: vacuum system overview
Courtesy: L. Eybert

## Slide 29: Mock-up – transfer of vacuum string
Vacuum assembly table
Girder
Courtesy: L. Eybert

## Slide 30: Mock-up: Girder 1 fully assembled
Courtesy:
L. Eybert

## Slide 31: From Assembly to Installation

## Slide 32: Assembly Phase (November 2017 – October 2018)
Jean-Claude Biasci will oversee the Assembly phase
Note: The Assembly phase takes place during the Operation of the facility!
Main ESRF staff involved:
TID Vacuum group
TID ALGE group
External assembly staff (BINP)
External handling staff (ECTRA)
Aim of the Assembly Phase:
Produce 129 fully equipped girders, ready to be installed in the SRTU

## Slide 33: EBS buildings

## Slide 34: ESRF01 – Assembly Building

## Slide 35: Assembly Planning – ESRF01 layout
ESRF1-Assembly building
Assembly line C
Assembly line B
Assembly line A
Position girders
Install magnets & align
Open magnets
Install pre-assembled chambers
Align BPM’s & chambers
Close magnets
Final alignment check

## Slide 36: ESRF01 – Assembly lines

## Slide 37: ESRF02a/b – Storage Buildings
ESRF02a
ESRF02b

## Slide 38: Logistics areas
4TH MAC MEETING – 22-23 September 2016 - T Marchial - WP11
ID24 - BM24
Entrance for girders
Chartreuse
DL assembly
Girder storage
ID14
Storage and entrance for girders
BM7:Entrance for girders
ID08: RF storage and preparation area

## Slide 39: Girder transport module
Page 53
The first girder transport module has been delivered to ESRF
There will be four girder transport modules in total
The girder transport modules will be used inside our buildings

## Slide 40: Tractor and trolley between buildings

## Slide 41: Dismantling the good old existing Storage Ring

## Slide 42: Storage buildings for the dismantled machine – architect view
ESRF11
ESRF12
ESRF13

## Slide 43: Dismantling + Installation Planning

## Slide 44: Dismantling + Installation Planning
Dismantling
Civil works
Girder entry
Piping
Cabling
FE+Bakeout
PSS test
Equipment test
Alignment

## Slide 45: Storage ring commissioning

## Slide 46: Draft operation schedule 2018

## Slide 47: Conclusions
The main engineering challenges are:
Extreme compactness/lack of space which required multiple design iterations and complex vacuum chambers
System integration
Vacuum chambers tolerances
Schedule & installation in existing tunnel
The first cell (out of 32) called “MockUp” has been built
Production of the ESRF-EBS components is in full swing
Serial components contracts will be exhausted over the next 12 months
Assembly will start in November and last about 1 year
Dismantling/Installation planning and organisation charts are finalised
The project is well under way!

## Slide 48: Many thanks for your attention