## Slide 1: CDR Options for LHeC Infrastructure:
RR LHeC:
new ring in
LHC tunnel,
with bypasses
around
existing
experiments
RR LHeC
e-/e+ injector
10 GeV,
10 min. filling time
LR LHeC:
recirculating
linac with
energy
recovery,
or straight
linac
F. Zimmermann
CDR Study assumptions:
-Assume parallel operation to HL-LHC
-TeV Scale collision energy
 50-150 GeV Beam Energy
-Limit power consumption to 100 MW
 (beam & SR power < 70 MW)
 60 GeV beam energy
-Int. Luminosity > 100 * HERA
-Peak Luminosity > 1033 cm-2s-1
Higgs @ 125GeV > 1034 cm-2s-1

## Slide 2: CDR Choices:
Linac-Ring Design based on ERL:
-Installation largely decoupled from LHC operation ✔
-can accept larger beam-beam  larger bunch current ✔
Recirculating Linac with Energy Recovery Mode (ERL) ✔
  energy efficiency and luminosity reach!
New accelerator concept & SRF technology (Q0, HOM damping)
  New operation mode on a large scale facility
      requires demonstration of parameter reach!

## Slide 3: Motivation: Accelerator Technology Development
Energy Recovery Linac concept: First proposal 50 years ago
M. Tigner: “A Possible Apparatus for Electron Clashing-Beam Experiments”,
Il Nuovo Cimento Series 10, Vol. 37, issue 3, pp 1228-1231,1 Giugno 1965
First Tests: Done at SCA @ Stanford in 1986
Interesting concept for FELs and Compton photon light sources,
and high current electron cooler concepts and colliders  SRF!!!
Concept became only viable with recent advances in SC RF technology
(e.g. high gradient structures with high Q0)
Many interesting potential applications
(e.g. coherent e-cooling and eRHIC)
 World wide need for a variety of demonstrator facilities!

## Slide 4: LHeC: Baseline Linac-Ring Option
Two 1 km long SC
linacs in CW operation (Q > 1010)
requires Cryogenic
system comparable
to LHC system!
Super Conducting Linac with Energy Recovery
& high current (> 6mA)
Relatively large return arcs
ca. 9 km underground tunnel installation
total of 19 km bending arcs
same magnet design as for RR option: > 4500 magnets
1033 cm-2 s-1 Luminosity reach | PROTONS | ELECTRONS
Beam Energy [GeV] | 7000 | 60
Luminosity [1033cm-2s-1] | 1 | 1
Normalized emittance gex,y [mm] | 3.75 | 50
Beta Funtion b*x,y [m] | 0.1 | 0.12
rms Beam size s*x,y [mm] | 7 | 7
rms Beam divergence s’*x,y [mrad] | 70 | 58
Beam Current [mA] | 430 (860) | 6.6 (3.3)
Bunch Spacing [ns] | 25 (50) | 25 (50)
Bunch Population | 1.7*1011 | (1*109) 2*109
Bunch charge [nC] | 27 | (0.16) 0.32
1034 cm-2 s-1 Luminosity reach | PROTONS | ELECTRONS
Beam Energy [GeV] | 7000 | 60
Luminosity [1033cm-2s-1] | 16 | 16
Normalized emittance gex,y [mm] | 2.5 | 20
Beta Funtion b*x,y [m] | 0.05 | 0.10
rms Beam size s*x,y [mm] | 4 | 4
rms Beam divergence s’*x,y [mrad] | 80 | 40
Beam Current [mA] | 1112 | 25
Bunch Spacing [ns] | 25 | 25
Bunch Population | 2.2*1011 | 4*109
Bunch charge [nC] | 35 | 0.64

## Slide 5: Post CDR Studies: RF Frequency
Review of the SC RF frequency:
-HL-LHC bunch spacing requires bunch spacing with multiples of
25ns (40.079 MHz)
Frequency choice: h * 40.079 MHz
h=18: 721 MHz or h=33: 1.323GHz
SPL & ESS: 704.42 MHz; ILC & XFEL: 1.3 GHz
Existing technologies do not quite match that requirement (20MHz)!

## Slide 6: Post CDR Studies: ERL Beam Dynamics
Beam-Beam effects:
 Optimum choice for LHeC RF frequency?
N=3 109
Beam-beam effect included
as linear kick
Result depends on seed for frequency spread
“worst” of ten seed shown
Frms=1.135 for ILC cavity
Frms=1.002 for SPL cavity
Beam is stable but very small margin with 1.3GHz cavity  lower frequency
Daniel Schulte @ LHeC Seminar 12. March 2013

## Slide 7: Optimum RF Frequency: Power Considerations Results from F. Marhauser
Large-grain Nb:
Optimum frequency at 2K between 300 MHz and 800 MHz
Lower T shift optimum f upwards
Small-grain (normal) Nb:
Optimum frequency at 2K between 700 MHz and 1050 MHz
Lower T shift optimum f upwards
Optimum frequency between 700MHz and 800MHz
(large and small grain Nb and 1.6K and 2K)
Chose 801MHz for bucket matching in the LHC
and for
synergies with FCC
Started discussions with JLab for Cavity construction in Washington 2015
 collaboration active under the FCC umbrella

## Slide 8: CDR Choices: Technology Choices and Design:
Super Conducting RF:
-Requirements imposed by LHC beam structure (n * 40 MHz)
-Existing technologies world wide (e.g. ILC, ESS)
-Beam stability considerations (Beam-Beam & Beam Breakup)
-RF Power considerations
-Synergies with other projects (e.g. FCC)
Daresbury meeting in 2013
  800MHz SRF in synergy with FCC-eh and FCC-ee
  Further beam dynamic studies with 802MHz choice

## Slide 9
Beam Breakup Instability:
D. Pellegrini (EPFL/CERN) Draft Perle CDR
Evolution of the amplitudes of the dipole modes for two different charges per bunch

## Slide 10
Instabilities and Recombination pattern:
D. Pellegrini (EPFL/CERN) @ ERL’15

## Slide 11
Instabilities and Recombination pattern:
D. Pellegrini (EPFL/CERN) @ ERL’15
 Need for demonstrator and test facilities!

## Slide 12: ERL Facilities around the World
12
Low Energy (< 100MeV), Single turn Facilities:
500 MHz + DC Gun
5 mA, 17 MeV, 12 ps
JAERI, Tokai
10mA-40mA
400pC
Bunch: 7.7ns; 60pC
77pC
Rama Calaga
RFTech 2013, Annecy Mar 25-26, 2013
JLAB, FEL, 160 MeV, 1.5 GHz
All single turn !!!
Only 2 with high bunch charge

## Slide 13: ERL Facilities around the World
13
Multi Turn Test Facilities and Installations:
-At the moment only single loop operation
-Severe limitations in beam current
due to injector
Normal Conducting 180 MHz + DC Gun
30 mA, 11 MeV, 70-100 ps
BINP, Novosibirsk
-3-4 turn ERL
-Normal conducting RF
Only BINP achieves bunch charges comparable to LHeC (900-1500pC)!
But it is normal conducting!

## Slide 14: LHeC ERL Test Facility:
14
Validation of key LHeC Design Choices:
Three re-circulations with high beam current:
 Coherent Beam stability due to ions, and wake-fields when triggering
transverse perturbations (a la beam-beam) (Beam Breakup instability)
 Pulse stability and reproducibility of beam parameters (intensity, position
and size)
 Energy spread and beam parameter stability at end of deceleration process
 Study of transient ERL dynamics during current ramp-up
 Study of failure scenarios (e.g. cavity quench during ERL operation etc)
SC RF Design validation via operation with beam
  SC RF behavior with beam
  Coupler validation
  HOM tolerances and required HOM damping
  Beam loading and implied RF controls (LLRF!!!)

## Slide 15
15
Fundamental Goals and Motivation:
Build up expertise in the design and operation for a facility with a fundamentally new operation mode:
 ERLs are circular machines with tolerances and timing requirements
similar to linear accelerators (no ‘automatic’ longitudinal phase stability
etc.)
Proof validity of fundamental design choices:
  Multi-turn recirculation
  Implications of high current operation (6 * [6mA – 25mA]  150mA!!)
Verify and test machine and operation tolerances before designing a large scale facility
  Tolerances in terms of field quality and alignment of the arc magnets
  Required RF phase stability (RF power) and LLRF requirements
ERL Demonstrator for LHeC:

## Slide 16: LHeC ERL Test Facility:
16
Validation and tests of auxiliary ERL components:
Injector and gun
  Choice of electron sources (Superconducting RF, DC High Voltage etc)
  Injection energy and beam transfer, emittance requirements and preservation, etc.
Injection line and beam dump tests
  Momentum acceptance requirements
  Beam extraction at different beam energies and machine protection aspects; beam halo formation etc
Required beam diagnostics (CTF closure at end of 2016):
 Pulse by pulse diagnostics
 Single pass beam size measurements etc.

## Slide 17: Injector & injector R&D
DC Gun + SRF CM (JLAB-AES) /
Cornell DC gun
NC Gun (LANL-AES)
SRF Gun (FZR-AES-BNL)
SRF Gun (BNL-AES)
 | DC+SRF-CM | Cornell | NC | SRF
Energy | 2-5 MeV | 10 MeV | ? | 2 MeV
Current | 100 mA | 100 mA | 100 mA | 500 mA
Bunch charge |  | 77pC | 3000pC | 700pC
Bunch spacing |  | 0.7ns |  | 
Long. Emit | 45 keV-ps | 10-60 keV-ps | 200 keV-ps | -
Trans. Emit | 1.2 µm | 0.3-1.6 µm | 7 µm | 1.4-5 µm
Preferred options
Erk Jensen and
F. Loehl @ IPAC’10

## Slide 18: The test ERL in Cornell’s hall LOE
6 MeV
6 MeV
Cornell DC gun
100mA, 6MeV SRF injector (ICM)
600kW beam dump
100mA, 6-cavity SRF CW Linac (MLC)
+/- 36 MeV
Electron Current up to 320mA in the linac
Bunch charge Q of up to 2nC
Bunch repetition rate 1.3GHz/N
Beams of 100mA for 1 turn and 40mA for 4 turns
42, 78, 114, 150 MeV
Existing components at Cornell

## Slide 19: Key Performance Parameters and Ultimate Performance Parameters
Parameter | Unit | KPP | UPP (Stretch)
Electron beam energy | MeV |  | 150
Electron bunch charge | pC |  | 123
Gun current | mA | 1 | 40
Bunch repetition rate (gun) | MHz |  | 325
RF frequency | MHz | 1300 | 1300
Injector energy | MeV |  | 6
RF operation mode |  |  | CW
Number of ERL turns |  | 1 | 4
Energy aperture of arc |  | 2 | 4
Some of these items can be addressed @ CBETA.
But: Main focus is the demonstration of FFAG arcs!!
Different frequency; bunch spacing and HOM spectrum as for LHeC
 But strong synergies for collaboration with an LHeC ERL demonstrator!!!

## Slide 20: PERLE ERL Facility: PCDR 2015
20
Potential applications beyond an LHeC ERL Test Facility:
Magnet and cable quench facility:
 Vital for development of new cables and future high field SC
magnets (e.g. FCC hh)  energy density in recirculating linac mode
Test facility for SC RF with beam
  Very interesting for development of new SC RF components
  e.g. Crab Cavities, SC RF for FCC ee, etc.
  Unique installation world wide!!! (SPS CC installation for protons)
Test beam for detector component developments
  Beam lines with beam energies higher than 100 MeV/c [Peter Kostka]
Dedicated Physics Facility  N. Pietralla at 2015 LHeC

## Slide 21: Staged Installation
Stage 1 – 2 CMs, test installation – injector, cavities, beam dump.
Stage 2 – 2 CMs, set up for energy recovery, 2…3 passes
Stage 3 – 4 CMs, set up arcs for higher energies – reach up to 905 MeV
ARC 2 155 MeV
ARC 1 155 MeV
ARC 3 455 MeV
ARC 5 755 MeV
ARC 2 305 MeV
ARC 4 605 MeV
ARC 6 905 MeV

## Slide 22: Cavity and Cryomodule Design
Collaboration with JLAB established – work has started. Cavity designs exist with different apertures (… ), optimization ongoing
The cavity prototypes will be fabricated for PERLE by JLAB in the framework of our collaboration agreement.
JLAB equally helps us with the design of the cryomodule (alternative to the SPL design).
JLAB design (based on SNS 805 MHz)
CERN design (based on SPL 704 MHz)
R. Calaga, M. Karppinen, K. Schirm, R. Torres-Sanchez (CERN)
F. Marhauser, R. Rimmer (JLAB)
E. Jensen
LHeC Workshop 2015

## Slide 23: PERLE Footprint:
13.66 m
14.22 m
42.8 cm
98.5 cm
6.8 cm
42.46 m
13.66
A.Valloni 2/16

## Slide 24: PERLE Parameters: PCDR 2015
Parameter | Value | 
injection energy | 5MeV | 
RF frequency | 801MHz | 
acc. voltage per cavity | 15MV | 
# cells per cavity | 5 | 
total cavity length | ca. 1m | 
# cavities per cryomodule (CM) | 4 | 
RF power per cryomodule (CM) |  | 
# cryomodules | 2-4 | 
max. acceleration per CM pass | 75MV | 
bunch repetition | 25ns | 
injected beam current | 10-30mA | 
nominal bunch charge | 0.7 nC | 
number of passes | 1 | 3
top energy | 155-305Gev | 455-905GeV
duty factor | CW | 

## Slide 25: ERL Demonstrator for LHeC:
International Advisory Committee outcome 2015:
-Develop a Conceptual Design Report for a minimal test
facility @ CERN  demonstrate LHeC needs without
additional applications
Footprint, required infrastructure and parameter specification
Reduced version of PERLE Stage 2 (1 cryo module only)
Stage 2 – 2 CMs, set up for energy recovery, 2…3 passes

## Slide 26: ERL Demonstrator
A.Valloni 2/16
Demonstration of high current
(25mA), multi(3)turn ERL
Test and development of 802MHz
SCRF technology
(65-75MV / CM & 4 5-Cell cavities/CM)
Ee = 200 (400) MeV with 1(2) CMs
Parameter | Value
Dipoles per arc Dipole length Max B Field | 3/4 50 cm 1.1 T
Quadrupoles per arc Quadrupoles in straight lines | 5 4
Dipoles in Spreader/Combiner Quads in Spreader/Combiner | 1-3 3
Dipoles for Injection-Extraction | 6
A.Valloni 2/16

## Slide 27: Mini PERLE Parameters:
Parameter | Value | 
injection energy | 5MeV | 
RF frequency | 801MHz | 
acc. voltage per cavity | 15MV | 
# cells per cavity | 5 | 
total cavity length | ca. 1m | 
# cavities per cryomodule | 4 | 
RF power per cryomodule |  | 
# cryomodules | 1 / 2 | 
max. acceleration per module pass | 75MV | 
bunch repetition | 25ns | 
injected beam current | 10-30mA | 
nominal bunch charge | 0.7 nC | 
number of passes | 3 | 3
top energy | 230Gev | 455GeV
duty factor | CW | 

## Slide 28: Mini PERLE Footprint:
24 m
6m
A.Bogazs 2/17
92 dipole [1.4T] and 118 quadrupole magnets

## Slide 29: ERL Demontrator
Technical Mission Summary for LHeC:
-high current (25mA / 0.7nC) multi-turn (3) ERL operation
-Energy recovery efficiency
-SRF LLRF feedback and control
-Failure scenarios and transients in multi turn ERL operation
-Beam stability (Beam Breakup and filling schemes)
-Demonstration / specification of required HOM damping
-Transverse / longitudinal stability for bunch passage @ high energy
-Beam halo formation and dump-line acceptance
-Beam instrumentation (minimum requirements)
-Build up operational experience
-Source and injector validation

## Slide 30
Reserve Transparencies

## Slide 31: Cornell High Current Injector
F. Loehl @ IPAC’10

## Slide 32: ERL Facilities around the World
JLAB, FEL, 160 MeV, 1.5 GHz
APS-ERL Upgrade
5 GeV, 1-2 passes
1.4 GHz
APS
Cornell ERL Light Source, 5 GeV, 1.3 GHz
Beijing Advanced
Photon Complex
1.3 GHz
High Energy (> 100MeV), planned, (single turn) Facilities:
MESA
10mA
1.3GHz
5-125 MeV

## Slide 33: CDR Choices: Technology and Design
Optics:
-SRF Linac with quadrupoles between the cryo modules
-Flexible Momentum Compaction [FMC] arc optics

## Slide 34: HE ERL’s, EIC’s (election-ion) - Studies
JLab MEIC | BNL eRHIC | CERN LHeC
5-10 GeV | 20 GeV | 60 GeV
750 MHz 5 passes | 704 MHz 16 passes | 704 MHz 3-passes
3 A -> 30mA | 50 mA -> 1.6A | 15 mA -> 90mA
4 nC | 3.5 nC | 0.3 nC
7.5 mm | 2 mm | 0.3 mm
Planned | Planned | Planned
JLAB, MEIC
BNL, eRHIC
CERN, LHeC
Frequency choice!
Number of Recirculation turns!
Beam intensity / Beam current
Need for complementary ERL Facilities!

## Slide 35: Existing Demonstrator Proposals:
C-BETA: funded
Combined proposal by BNL and Cornell University
Funded by the state of New York and being build at Cornell
Main characteristics: FFAG arcs, 1.3 GHz TESLA module, 1 linac,
150 MeV, 6Mev inj;
4 turns and FFAG arcs; 4*2*40mA; 125pC; 203ns
PERLE: Main characteristics:
800MHz, 3 turns, 25mA, 650pC, 2 linacs, 1 GeV
ER@CEBAF: Not yet funded
Combined proposal by BNL and JLab
Main characteristics: 1.5 GHz CEBAF modules, 0.1mA,
2 linacs, 5 re-circulations, 1 GeV

## Slide 36: LHeC Infrastructure Baseline:
LR LHeC:
recirculating
linac with
energy
recovery,
or straight
linac
F. Zimmermann

## Slide 37
Alternative coil arrangement
keep the idea of recycling Ampere-turns
stack the apertures vertically but offset them also transversally
same vertical gap, 25 mm
simple coils / bus-bars, same powering circuit
as before, trim coils can be added for two of the apertures, to give some tuning
Attilio Milanese
Post CDR: Return Arc Dipoles optimization
×
0.264 T
60 GeV
0.176 T
40 GeV
0.088 T
20 GeV
×
×
∙
∙
∙
∙

## Slide 38: Linac 1 and 2 - Multi-pass ER Optics
A. Bogacz (JLab) @ ERL2015, Stony Brook University, June 9, 2015

## Slide 39: Vertical Separation of the Three Arcs
Arc 1 (10 GeV)
Arc 3 (30 GeV)
Arc 5 (50 GeV)
A. Bogacz (JLab) @ ERL2015, Stony Brook University, June 9, 2015

## Slide 40: Arc Optics: Emittance preserving FMC cells
52.3599
0
500
0
0.5
-0.5
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
52.3599
0
500
0
0.5
-0.5
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
52.3599
0
500
0
0.5
-0.5
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
total emittance increase in Arc 1- 5: DexN = 4.9 mm rad
Arc 1 , Arc2
TME-like Optics
DBA-like Optics
Imaginary gt Optics
Arc 3, Arc 4
Arc5, Arc 6
factor of 20 smaller than FODO
Emittance dilution due to quantum excitations:
A. Bogacz (JLab) @ ERL2015, Stony Brook University, June 9, 2015
[Double Bend Achromat]
[Theoretical Minimum Emittance]
[Flexible Momentum Compaction]

## Slide 41: Beam diagnostics application
Desired parameters:
  Beam energy if possible ( close to protons in LHC)
  CW operation
  bunch length below ps
  bunch charge ideal
Proposed BI tests:
  Test of BI based on the measurement of radiation produced by charged particles.
  Test of electronics for future BI upgrades (all machines, but especially HL-LHC era diagnostics & FCC if rep rate can be made to match)
  Test of BI for high resolution transverse & longitudinal diagnostics (making use of short bunches)
  Further interesting tests would be possible in non-ERL mode with a dedicated external test beam line.
E. Jensen
LHeC Workshop 2015

## Slide 42: Low Energy ERL’s and ERL test facilities (contd.)
IHEP ERL-TF | HZB BERLinPro | BINP | Peking FEL | BNL ERL-TF | KEK cERL | Daresbury ALICE | JAERI
35 MeV | 100 MeV | 11-40 MeV | 30 MeV | 20 MeV | 245 MeV | 10 MeV | 17 MeV
1.3 GHz 9 cell | 1.3 GHz | 180 MHz | 1.3 GHz 9-cell | 704 MHz 5-cell | 1.3 GHz 9-cell | 1.3 GHz 9-cell | 500 MHz
10 mA | 100 mA | 30 mA | 50 mA | 50-500 mA | 10-100 mA | 13 µA | 5-40 mA
60 pC | 10-77 pC | 0.9-2.2 nC | 60 pC | 0.5-5 nC | 77 pC | 80 pC | 400 pC
2-6 ps | 2 ps | 70-100ps | 1-2 ps | 18-31 ps | 1-3 ps | ~10 ps | 12 ps
1 pass | 1-2 pass | 4 passes | 1 pass | 1 pass | 2-passes | 1-pass | 1-pass
Under construction | Planned / construction | operating |  | Under construction | Under construction | No longer operating | operating
Rama Calaga, RFTech 2013, Mar 25-26, 2013

## Slide 43: High Energy ERL’s, EIC’s (election-ion)
JLab MEIC | BNL eRHIC | CERN LHeC
5-10 GeV | 20 GeV | 60 GeV
750 MHz ? passes | 704 MHz 6 passes | 800 MHz 3-passes
3 A | 50 mA | 25 mA
4 nC | 3.5 nC | 0.64 nC
7.5 mm | 2 mm | 0.3 mm
Study | Study | Study
JLAB, MEIC
BNL, eRHIC
CERN, LHeC
Rama Calaga, RFTech 2013, Mar 25-26, 2013

## Slide 44: High Energy ERL’s, Light sources, FEL
7GeV
Double Acc.
3GeV ERL
First Stage
XFEL-O 2nd Phase
JLAB, FEL, 160 MeV
KEK-JAEA
APS-ERL Upgrade
5 GeV, 1-2 passes
APS
Cornell ERL Light Source, 5 GeV
Beijing Advanced
Photon Complex
Rama Calaga, RFTech 2013, Mar 25-26, 2013

## Slide 45: High Energy ERL’s, Light sources, FEL’s
JLab FEL (IR, UV) | Argonne Light Source | Cornell Light source | Mainz, MESA ERL | KEK-JAEA Light Source | Beijing Photon Source
160 GeV | 7 GeV | 5 GeV | 100-200 MeV | 3 GeV | 5 GeV
1.5 GHz | 1.4 GHz 1-2 passes | 1.3 GHz | ? 2 passes | 1.3 GHz | 1.3 GHz 9 cell
10 mA | 25-100 mA | 100 mA | 0.15-10 mA | 0.01-100 mA | 10 mA
135 pC | 77 pC | 77pC | 7.7 pC | 7.7-77 pC | 77 pC
0.045-0.15 mm |  | 0.6 mm | - ps | 2 ps | 2 ps
Operating | Planned | Planned | ? | Planned | Planned
CEBAF not in the list since it is not normally operated in ER mode.
(Is this so? – Please correct me if wrong! – and help fill my other blanks!)
Rama Calaga, RFTech 2013, Mar 25-26, 2013