## Slide 1: The CLIC Accelerator Project Status and Plans
Higgs Hunting, Paris, July 2018
Daniel Schulte
For the CLIC collaboration

## Slide 2: CLIC Introduction
2012 CDR:
Shows feasibility of 3 TeV design
CLIC: Compact LInear Collider
CLIC aims to provide multi-TeV electron-positron collisions with high luminosity at affordable cost and power consumption

## Slide 3: CLIC Collaboration

## Slide 4: CLIC Staged Scenario
Plenty of physics at low centre-of-mass energies
Energy and luminosity targets from Physics Study Group
Implementation in stages
Study top at threshold
Top above threshold
Higgs via Zh and WW fusion
To be updated with more input from LHC and stage 1

## Slide 5: CLIC Staged Scenario
Plenty of physics at low centre-of-mass energies
Energy and luminosity targets from Physics Study Group
Implementation in stages
Study top at threshold
Top above threshold
Higgs via Zh and WW fusion
To be updated with more input from LHC and stage 1
This is being reviewed
Review of effective operation time for luminosity per year showed increase from 1.08 x 107 s to 1.2 x 107
Consider some extra years at full luminosity
  Likely increases integrated luminosities
  Could further improve physics results

## Slide 6: CLIC at 380 GeV
Developed optimised first energy stage
Upgrade to higher energies included

## Slide 7: Key Parameters
Gradient is optimised for luminosity and cost
Installed modules can be reused at higher energies

## Slide 8
Drive beam linac
Combiner ring
Reminder: CLIC Test Facility (CTF3)
Delay loop
CLEX
TBL
Two Beam Module
CTF3 programme 2013-2016

## Slide 9: Reminder: Drive Beam Scheme Performance
CTF3 measurements:
RF to drive beam efficiency > 95%
Current multiplication factor 8
Most of beam quality
145 MV/m X-band acceleration
Arrival time with feedback
Parameter | CLIC goal | CTF3 measured
Arrival time | 50 fs | 50 fs
Current after linac | 0.75 x 10-3 | 0.2-0.4 x 10-3
Energy | 1.0 x 10-3 | 0.7 x 10-3
Measured 145 MV/m gradient
Current stability affected by very low CTF3 energy, 3 x larger beam
and delay loop design different from CLIC
Detailed simulations of drive beam performance in CLIC

## Slide 10: Reminder: Drive Beam Scheme Performance
CTF3 measurements:
RF to drive beam efficiency > 95%
Current multiplication factor 8
Most of beam quality
145 MV/m X-band acceleration
Arrival time with feedback
Parameter | CLIC goal | CTF3 measured
Arrival time | 50 fs | 50 fs
Current after linac | 0.75 x 10-3 | 0.2-0.4 x 10-3
Energy | 1.0 x 10-3 | 0.7 x 10-3
Measured 145 MV/m gradient
Current stability affected by very low CTF3 energy, 3 x larger beam
and delay loop design different from CLIC
Detailed simulations of drive beam performance in CLIC
CTF 3 stopped operation
New facility is online: CLEAR
CERN Linear Electron Accelerator for Research

## Slide 11: CLIC Structure Development
Further optimisation ongoing of structure production for industrialisation
40 G [MV/m] 80 100 120
Structure performance is reproducible
Several klystron-based test stands exist that test structures (X-boxes)

## Slide 12: Main Linac Module and Imperfection Mitigation
Magnets are stabilised mechanically to nm against ground motion and vibrations
Overlapping wires provide accurate position information
Wake monitors in each structure measure beam offset (3.5 μm)
Components are mounted accurately on movable girders
In addition to high accuracy optimisation for cost

## Slide 13: Klystron-based Alternative
Develop klystron-based alternative
Expect comparable cost for first energy stage
But increases faster for high energies
Novel high efficiency klystrons
Novel pulse compressors
Optimised structure
Novel distribution system
8
8

## Slide 14: Beam Quality for Luminosity
Emittance [10-5 m ]
Initial beam
3 iterations
iteration
Dispersion Free Steering Test at FACET (SLAC)
Production of low-emittance beams in damping ring
  Similar to existing light sources
ATF2 at KEK
Beam size (41 nm) is close to target (37nm)
Quality preservation in transport
  Minimisation of imperfections
  Optimised lattice design
  Sophisticated beam-based tuning
Focusing of beam in beam delivery system
  Advanced lattice design
  Advanced tuning
  Test at FFTB and ATF2

## Slide 15: CLIC Technology Development and Applications
CLIC technology for CLIC and different applications
Recent EU co-funded FEL design study
SPARC at INFN-LF
Electrons to SPS for dark matter searches?
…

## Slide 16: Note: Dark Matter Searches
3.5 GeV Linac
12 GHz CLIC technology
Acceleration to about 16 GeV in SPS
Extraction
Transfer to SPS
Basically all tunnels and infrastructure exist
Need 3.5 GeV linac with CLIC technology

## Slide 17: Comment: Increased L* for Detectors
Detailed studies show great experimental conditions
Background acceptable
Luminosity spectrum useful
New BDs design increases L* from 3.5 to 6 m
Focusing magnets now outside of detector
Better angular coverage

## Slide 18
Cost and Power
Goals bring cost and power consumption down:
“reasonable cost”: O(6 GCHF)
Reasonable power < O(200 MW)
Main beam production | 1245
Drive beam production | 974
Two-beam accelerator | 2038
Interaction region | 132
Civil engineering etc. | 2112
Control & operation | 216
TOTAL | 6690
Initial value for 380 GeV
(MCHF of Dec 2010)
Improvement of cost and power is ongoing
Detailed bottom up estimate
Already savings, seems we meet goal
Intial Estimate 252 MW

## Slide 19: CLIC Site and Upgrade to 3 TeV
Drive Beam Generation Complex
Main Beam Generation Complex
50km
Can re-use previous systems and components
Just add more linac and drive beam pulse length
At 3 TeV add one drive beam

## Slide 20: Conclusion
Important progress toward the EU strategy
Much improved technical maturity
Light sources are prototypes of damping rings
Normal conducting FELs are prototypes, e.g. Swiss FEL
Further optimising 380 GeV first energy stage
Work on further stages, including considerations of novel technologies
Writing of Project Implementation Plan is well advancing, ready by end of 2018
Many thanks to L. Evans, S. Stapnes, W. Wuensch, Ph. Burrows, I. Syratchev and the CLIC team

## Slide 21: Reserve

## Slide 22: Main Linac Imperfection Mitigation
Magnets are stabilised mechnically to nm against ground motion and vibrations
Overlapping wires provide accurate position information
Wake monitors in each structure measure beam offset (3.5 μm)
Components are mounted accurately on movable girders
Optimised lattice design
Sophisticated beam-based alignment, e.g. dispersion free steering (i.e. different energy beams)

## Slide 23: Other CLIC Technology Development
Main beam injector
e.g. halved power for positron production
Permanent magnets
Use tunable permanent magnets where possible
Drive beam quadruoles
Strongest permanent magnet developed in UK
Redesign CLIC modulators and klystrons
Aim: increase efficiency from 62% to 90%
Less power consumption
Also important cost saving
Shorter tubes, no oil in modulator, …
Important cost saving
New module design
Reduce cost of mechanical system and control