## Slide 1: ILC Accelerator overview
S. Michizono and A. Yamamoto
(LCC/ILC/KEK)
Higgs Hunting 2018, Paris
2018-7-25

## Slide 2: Outline
Introduction
ILC-250 overview
Key technologies advanced
Progress in cost-reduction R&D
Project Status
Summary

## Slide 3: ILC500 to ILC250
Technical Design Phase
ILC-GDE
2006
‘07
‘08
‘12
‘09
‘10
‘11
‘13
SC Technology
selected
RDR)
LCC
LHC
2004
TDR
1980’ ~ : Basic Study
‘14
‘15
‘16
’17,18
European XFEL
LCLS-II
TDR
Progressing 
ILC-250

## Slide 4: Machine/Physics report (October 2017)
https://arxiv.org/abs/1710.07621
https://arxiv.org/abs/1711.00568

## Slide 5: ILC250 Acc. Design Overview
e- Source
e+ Main Liinac
e+ Source
e- Main Linac
Nano-beam Technology
SRF Accelerating Technology
Key Technologies
Physics Detectors
Damping Ring
Item | Parameters
C.M. Energy | 250 GeV
Length | 20.5 km
Luminosity* | 1.35 x1034 cm-2s-1
Repetition | 5 Hz
Beam Pulse Period | 0.73 ms
Beam Current | 5.8 mA (in pulse)
Beam size (y) at FF | 7.7 nm
SRF Cavity G. Q0 | 31.5~35 MV/m Q0 = 1 ~ 1.6x10 10
AC Power | 120 ~ 130 MW
Enable to be higher (discussed in ALCW2018) | 

## Slide 6
ILC Site Candidate Location in Japan: Kitakami
Oshu
Ichinoseki
Ofunato
Kesen-numa
Sendai
Express-
Rail
High-way
IP Region
Preferred site selected by JHEP community,
Endorsed by LCC, in 2013
ILC-250n(20.5 km)
Extendability (≥ 50 km)

## Slide 7
Courtesy: S. Kanemura
ALCW2018, Fukuoka
Further references for ILC250 Physics; :
”The potential of the ILC dor Discovering New Particles”, arXiv:1798.089012
“Physics Case for the 250 GeV Stage of the ILC”, arXiv:1710.07621
“The Role of Positron Polarization for the Initial 250 GeV stage of the ILC”, arXiv:1801.02840

## Slide 8
Courtesy: S. Komamiya
ALCW-2018. Fukuoka
Ref: “Physics Case for the 250 GeV Stage of the ILC”, arXiv:1710.07621

## Slide 9: ILC-250 Status -- Highlighted
Science:
Scientific significance of the precise measurements of the Higgs Boson increasing,
ILC redefined as a Higgs Factory at the maximum HZ cross section at Ecm=250 GeV, and
Energy extend-ability in future science.
Technology:
SRF technology matured: European XFEL SRF accelerator successfully built, with functioning as the prototype for the ILC.
Nano-beam technology matured: ATF demonstrating the FF beam size (41 nm) equivalent to that (7 nm) required at the ILC.
Cost reduced down to 2/3 or less, at a half Ecm and further advances in SRF technology.
Toward Project Decision:
Progress: JP/MEXT, ILC Advisory Panel finalizing the report. Science Council (JP) to provide the recommendation to MEXT-Government to finalize the decision.
Int’l discussions in progress: ICFA/LCB, US-JP, France-JP, Germany-JP, CERN, EU, EJADE, and …
The due-date of the input for the European Strategy, Dec. 2018, well informed.

## Slide 10: Outline
Introduction
ILC-250 overview
Key technologies advanced
Progress in cost-reduction R&D
Project Status
Summary

## Slide 11: Technical Status in 2018
Key Technologies advanced!
Nano-beam Technology：
    KEK-ATF2: FF beam size (v): 41 nm at 1.3 GeV (equiv. to 7 nm at ILC）
SRF Technology ：
    European XFEL completed: <G = ~ 30 MV/m> achieved with 800 cavities
    and accelerator operation reaches the design energy.
    LCLS-II: construction in progress
    H-FEL (Shanghai): approved
    US-Japan: Cost Reduction R&Ds in progress, focusing on Nb-material and
    “N-Infusion” process for High-Q and -G
  General design updated:
  ILC 250 GeV proposal authorized by ICFA/LCB, 2017

## Slide 12: ATF/ATF2: Accelerator Test Facility
Layout of ILC
Develop the nanometer beam technologies for ILC
Key of the luminosity maintenance
7.7 nm beam at IP (ILC250)
1.3 GeV S-band Electron LINAC (~70m)
Damping Ring (~140m)
Low emittance electron beam
ATF2: Final Focus Test Beamline
  Goal 1:Establish the technique for
  small beam
  Goal 2: Stabilize beam position
 | Vertical | Horizontal
ILC500 | 5.9 nm | 474 nm
ILC250 | 7.7 nm | 516 nm

## Slide 13
Goal 1: Establish the ILC final focus method with same optics and comparable beamline tolerances
ATF2 Goal : 37 nm  6nm @ILC500GeV 7.7nm@ILC250GeV
  Achieved 41 nm (2016)
Progress in FF Beam Size and Stability at ATF2
Goal 2: Develop a few nm position stabilization for the ILC collision
FB latency 133 nsec achieved
(target: < 300 nsec)
positon jitter at IP: 410  67 nm (2015) (limited by the BPM resolution)
Nano-meter stabilization at IP
History of ATF2 small beam
Efforts continued.

## Slide 14: Worldwide SRF Collaboration
European XFEL
Asia,
PAPS@IHEP CFF/STF@KEK
Americas, LCLS-II
FNAL/ANL
Cornell
JLAB
KEK
CERN, DESY
SLAC, LCLS-II
CEA, CNS-LAL
INFN
IHEP, PKU
IUAC, RRCAT
TRIUMF
ILC-SRF technology
MSU

## Slide 15: European XFEL, SRF Linac Completed
Progress:
2013: Construction started
…
2016: E- XFEL Linac completion
2017: E-XFEL beam start
XFEL site
DESY
1 km SRF Linac
Courtesy, H. Weise
1.3 GHz / 23.6 MV/m
800+4 SRF acc. Cavities
100+3 Cryo-Modules (CM)
: ~ 1/10 scale to ILC-ML

## Slide 16: European XFEL: SRF Cavity Performance
Courtesy, D. Reschke , N. Walker, C. Pagani
>10 % (47/420, RI) cavities
exceeding 40 MV/m
After Retreatment:
E-usable: 29.8 ± 5.1 [MV/m]
(RI): E usable 31.2 ± 5.2 [MV/m]), w/ 2nd EP
(EZ): E usable 28.6 ± 4.8 [MV/m]) , w/ BCP ( instead of 2nd EP)

## Slide 17: European XFEL reaches its Design Energy
Chart: E max [GeV]
| 18.5.17 (up to CS7) | 23.6.17 (up to CS8) | 28.9.17 (during MGTF)
Max Energy | 12.7315 | 15.1907 | 16.185
Regarding AMTF tests | 18.9382 | 18.9382
17.5 | 17.5 | 17.5
Courtesy, M. Omet
17.5 GeV
17.07.18

## Slide 18: Outline
Introduction
ILC-250 overview
Key technologies advanced
Progress in cost-reduction R&D
Project Status
Summary

## Slide 19: US-Japan Discussion Group on ILC
First meeting on May 25, 2016 at Washington D.C
  Attended by Deputy Director-General, Research Promotion Bureau, MEXT, and Director, Office of Science, DOE.
  Agreed on item of discussion
Second meeting on October 18, 2016 by video
  Attended by Deputy Director-General, Research Promotion Bureau, MEXT, and Director, Office of Science, DOE.
  Agreed to begin the joint R&D from April 2017.
R&D program started in 2017

## Slide 20: US-Japan cost reduction R&D
New Nb material/process
N-Infusion
Degradation-free environment
Heat treatment
Cavity fabrication
Module (including tuner, jacket)
Vertical test
Horizontal test
Stand-alone horizontal test
Module test at stF-2
Evaluate the cavity performance from vertical test to horizontal test

## Slide 21: Direct sliced Nb material performance at KEK
Preliminary
Made from large grain Nb disks;
medium RRR Nb with high Ta content (CBMM)
- The 3-cell cavity achieved very high gradient (~42 MVm) and satisfies ILC spec.
Annealed for 800℃×3hrs
to remove stresses.
Electron beam welding of end-cell
Electron beam welding of the cavity

## Slide 22: Cavity performance progress at FNAL: “standard” vs “N infused” cavity surface treatment
FNAL recently demonstrated a new treatment, which utilizes “nitrogen infusion”, achieving
    45.6 MV/m  194 mT
    with Q ~ 2x1010
Systematic effect observed on several single cell cavities
FNAL has now successfully applied it on three nine cell cavities
Jlab, KEK have reproduced similar results on single cell cavities with Q >2e10 at 35 MV/m
R&D work towards:
  Best recipe for higher Q at high G
  Robustness of process
Increase in Q by > a factor of two
Increase in gradient ~15%
A Grassellino et al 2017 Supercond. Sci. Technol. 30 094004
A. Grassellino

## Slide 23: Outline
Introduction
ILC-250 overview
Key technologies advanced
Progress in cost-reduction R&D
Project Status
Summary

## Slide 24: ILC Study Coordination by MEXT
Physics
WG
TDR Valid.
WG
2014-15 & 2018
2014 ~ 2018
MEXT
Commissioned Survey
by NRI (2014-17)
Physics WG, and TDR Validation WG
re-organized to evaluate ILC-250GeV.
Human Res. WG
WW Research trend (FY14)
Technology issues (FY15)
Large Int’l projects (FY16)
Risk/safety issues (FY17)
Organization & Manage.WG
2014-15 & 2018
2017
2015 -16
SCJ
ILC Adv. Panel
2013 2018
SCJ, MEXT
WGs
IAP

## Slide 25: Official Discussions Progress in Japan 47 IAPs/WGs held in 2014~2018 (CY)
 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
LCC/ILC | TDR published |  |  |  |  | 
SCJ - MEXT | MEXTSCJMEXT |  |  |  |  | MEXTSCJ
MEXT-IAP |  | 1st ~ 2nd | 3rd ~ 4th | 5th | 6th ~ 8th | 9th ~ 11th
- Science WG |  | 1st ~ 5th | 6th ~ 8th |  |  | (250): 1st ~ 5th
- TDR WG |  | 1st ~ 4th | 5th ~ 6th |  |  | (250): 1st ~ 5th
- HR WG |  |  |  | 1st ~ 3rd | 4th ~ 6th | 
- Manage. WG |  |  |  |  | 1st ~ 6th | 
* Comm. Survey (w/ NRI) |  | WW Research | ILC Tech. & Issues | Int’l Project | Risk/Safety Issues | 
ILC Plan, Update | ILC-500 (TDR) |  |  |  |  | ILC-250
We are here

## Slide 26
Courtesy: M. Titov

## Slide 27
ILC-500 to ILC-250
 | Collision E. [GeV] | Tunnel Space [GeV] | Value Total (MILCU) | Value Ratio
TDR | 250/250 | 500 | 7,980 | 1
TDR update | 250/250 | 500 | 7,950 | 0.96
Option A | 125/125 | 250 | 5,260 | 0.66
Option A’ (w/ R&D) | 125/125 | 250 | 4,780 w/ R&D success | 0.60
250 GeV e-
250 GeV e+
TDR update:
125GeV e-
125GeV e+
Opt. A, A’: 250 GeV
Damping Rings
Turnaround &
Bunch compressors

## Slide 28: Official Discussions progressed in IAP
Interim Report for ILC-500 (TDR) in 2015
Share the cost internationally, and Find a clear science vision on BSM, the discovery potential of new particles.
Monitor/analyze the development of the LHC, and mitigate cost-risk.
  {Homework Revisit the physics case after LHC Run-II, and Control the cost }
Obtain general understanding by the public & science communities.
Discussions reached, for ILC-250, in 2018 (w/ my understanding)
Science justification and Technical advances well recognized,
Understanding by wide, academic/public communities to be justified. It shall be discussed in SCJ (w/ wider communities).

## Slide 29: Discussions at ICFA Meeting
Courtesy: P. Bhat
ICHEP-2018

## Slide 30
Courtesy: P. Bhat
ICHEP-2018

## Slide 31: Status and Prospect for ILC
We are here,
In 2018
ILC Progress and Prospect
Assuming (~2+) 4 year
Pre-Preparation and
Preparation Phase
(9 year)

## Slide 32: KEK-ILC Action Plan Issued, Jan. 2016 https://www.kek.jp/en/NewsRoom/Release/20160106140000/
ILC Progress and Prospect
 | Pre-Preparation Stage | Main Preparation Stage |  |  | 
 | present (we are here) | P1 | P2 | P3 | P4
ADI | Establish main parameters | Verify parameters w/ simulations |  |  | 
SRF | Beam acc. with SRF cavity string, Cost Reduction R&D (proposed) | Demonstrate mass-production technology, stability, hub-lab functioning, and global sharing |  |  | 
Nano-beam | Achieve the ILC beam-size goal | Demonstrate the nanobeam size and stabilize the beam position |  |  | 
e+ | Demonstrate technological feasibility | Demonstrate both the undulator and e-driven e+ sources |  |  | 
CFS | Pre-survey and basic design | Geology survey, engineering design, specification, and drawings |  |  | 

## Slide 33: European ILC Prep. Plan, published in 2018
Note: European Industry to be a key partner, based on its European XFEL experiences

## Slide 34
Discussions with Europe:
1st Japanese Delegation to Europe
(Parliament, Ministries, Industry, Region, Researchers)
Visited Paris and Berlin (2018.1.9～1.11), and
Germany / France side
Politicians: Hon. Becht (France), Hon. Kaufmann (Germany),
and
Hon. Trautmann (EU/Strasbourg)
Researchers: Marc Winter, Maxim Titov (France)
Rolf Heuer, Joachim Mnich (Germany),
Visited CERN, 2018.1.08 and 1.12
Courtesy: S. Yamashita
ICFA-2018, Souel
Anticipated EU-JP cooperation sharing the cost discussed

## Slide 35
Counterparts between Germany and Japan established at four levels:
Bundestag and Diet
Ministries
F. A. / Laboratories
Researchers
Dr. Schuette
Hon. Kaufmann
BMBF, Germany
Courtesy: S. Yamashita
ICHEP/ICFA-2018, Souel

## Slide 36
Hon. Olivier BECHT visit Japan in May, 2018
May 16 @ TOHOKU with Governor of Iwate prefecture, Mayors, Economy bodies
May 17 @ TOKYO with Diet members, opinion leaders, industry, researchers
May 23 @ TOKYO (MHI) with Chair of Advanced Accelerator Association (AAA)
Gave BIG and WONDERFUL IMPRESSION to Japanese VIP’s
+
Facilitate clear recognition of Urgency and Necessity of Japanese Gov’s
Clear signal in time in 2018
+
Hints on protocol and processes to realize the signal in time from Japan.
Courtesy: S. Yamashita
ICHEP/ICFA-2018, Souel

## Slide 37
JP Cabinet, Diet, AAA Members:
Discussed ILC with Prime Minister Abe
- Prime Minister Abe
- Deputy Chief Cabinet Secretary Nishimura
- Deputy Chief Cabinet Secretary Nogami
- Kawamura (Diet Budget committee chair)
- Shionoya (LDP election chair)
- Suzuki (Minister of Olympic)
- Onodera (Minister of Defense)
- Nishioka (AAA chair, MHI former CEO)
- Takahashi (Tohoku, Tohoku electric former CEO)
- Yamashita
July 5th, 2018
Courtesy: S. Yamashita
ICHEP/ICFA-2018, Souel

## Slide 38: Outline
Introduction
ILC-250 overview
Nano-beam and SRF technologies advanced
Progress in cost-reduction R&D
Summary

## Slide 39: Summary
Science:
Scientific significance of the precise measurements of the Higgs Boson increasing,
ILC redefined as a Higgs Factory at the maximum HZ cross section at Ecm=250 GeV, and
Energy extend-ability in future science.
Technology:
SRF technology matured: European XFEL SRF accelerator successfully built, with functioning as the prototype for the ILC.
Nano-beam technology matured: ATF demonstrating the FF beam size (41 nm) equivalent to that (7 nm) required at the ILC.
Cost reduced down to 2/3 or less, at a half Ecm and further advances in SRF technology.
Toward Project Decision:
Progress: JP/MEXT, ILC Advisory Panel finalizing the report. JP Science Council to provide the recommendation to MEXT-Government to finalize the decision.
Int’l discussions in progress: ICFA/LCB, US-JP, France-JP, Germany-JP, CERN, EU, EJADE, and …
The due-date of the input for the European Strategy, Dec. 2018, well informed.

## Slide 40: Backup

## Slide 41
(２０１８～)
Chair: G. Taylor

## Slide 42
https://arxiv.org/abs/1711.00568

## Slide 43: ILC Parameters, demonstrated, by 2016
Characteristics | Parameter | Unit | Demonstrated
Nano-bam: |  |  | 
ILC-FF beam size (y) KEK-ATF-FF equiv. beam size (y) | 5.9 37 (reaching 41 ) | nm nm | KEK-ATF
SRF: |  |  | 
Average accelerating gradient | 31.5 (±20%) | MV/m | DESY, FNAL, JLab, Cornell, KEK,
Cavity Q0 | 1010 |  | 
(Cavity qualification gradient | 35 (±20%) | MV/m) | 
Beam current | 5.8 | mA | DESY-FLASH), KEK-STF
Number of bunches per pulse | 1312 |  | DESY
Charge per bunch | 3.2 | nC | 
Bunch spacing | 554 | ns | 
Beam pulse length | 730 | ms | DESY, KEK
RF pulse length (incl. fill time) | 1.65 | ms | DESY, KEK, FNAL
Efficiency (RFbeam) | 0.44 |  | 
Pulse repetition rate | 5 | Hz | DESY, KEK

## Slide 44: A plan for ILC Cost-Reduction R&D in Japan and US focusing on SRF Technology, in 2~3 years
Based on recent advances in technologies;
  Nb material preparation
  - w/ optimum RRR and clean surface
  SRF cavity fabrication for high-Q and high-G
  -w/ a new baking recipe provided by Fermilab
  Power input coupler fabrication
  - w/ new (low SEE) ceramic without coating
  Cavity chemical process
  - w/ vertical EP and new chemical (non HF) solution
  Others
S. Michizono, S. Belomestnykh

## Slide 45: 1DE3 – the first 49 MV/m cavity
Cavity (fine grain) from DESY colleagues was prepared for baseline test before infusion, EP 60 microns + regular 120C bake (no nitrogen, low T oven)
Results were pretty surprising/puzzling
A. Grassellino et al, https://arxiv.org/abs/1806.09824

## Slide 46: Repeated on second cavity TE1AES009 (fine grain, AES, WC)
EP+ 75C 4 hrs+ 120C 48 hours
Regular 120C
A. Grassellino et al, https://arxiv.org/abs/1806.09824

## Slide 47: KEK-ILC Action Plan announced, Jan. 6, 2016
KEK issued an KEK-ILC action plan for how KEK should start its preparation toward the International Linear Collider when the Ministry of Education, Culture, Sports, Science and Technology (MEXT), decides to initiate negotiations with foreign countries. ,,,
The study provides the basic information required to plan the technical actions, organization, human resources, and training to realize formal approval of the ILC project, and to ensure a smooth start of the construction phase through the preparation phase from the current status.
https://www.kek.jp/en/NewsRoom/Release/20160106140000/

## Slide 48: KEK-ILC-Action Plan

## Slide 49: European ILC Preparation Plan, 2018

## Slide 51: Washington DC, May 1-3, 2017

## Slide 52
September 25, 2017
General Meeting, Federation of Diet Members for ILC

## Slide 53
France-Japan Meeting on ILC
(Tokyo, 2017 Nov 29）
Japan:
Hon. Kawamura, Hon. Shionoya, Hon. Hirano, Hon. Ito, Hon. Otsuka, Hon. Fujiwara
MEXT: Mr. Itakura et al
Members of AAA, Tohoku Economy Federation
Researchers
France:
Hon. Olivier Becht
Mr. Jean-Christophe AUFFRAY （French Embassy)
Mr. Aurelien ANTHONY（Alsace Japan Agency)
etc.
The second step