Luminosity measurement at LHCb and other LHC experiments
French-Ukrainian workshop, LAL, 26 Sep 2018
Vladislav Balagura (LLR – Ecole polytechnique)
        Outline:
Luminosity mesurement in general
LHC luminometers, comparison
Absolute calibration
- from beam-gas “photos” of colliding bunces
- van der Meer (vdM) scans
- from reaction with known cross-section (fixed-target)
Novelties in two last vdM LHCb scans
Conclusions

---
How to measure luminosity?
1) Relative luminosity measurement can use any linear detector:
where R is event rate, σvis - « visible » cross section and L – instantaneous luminosity.
Having several luminometers crucial for systematics estimation.
2) Absolute luminosity calibration, ie. σvis , from :
where N1,2 are number of protons in colliding bunches, f -frequency of collisions, Aeff – overlap integral of two bunches.
TOTEM and ALFA measurements based on optical theorem will not be covered.
color red {R = %sigma_{vis} L}
color red {L= {N_1 N_2 f} over {A_eff},} newline color red{A_eff= iint %rho_1(x,y) %rho_2(x,y) dxdy }

---
Where do we need luminosity?
Online – to optimize performance of detectors, monitor beams and for adjusting luminosity (leveling)
Offline – ultimate precision for physics analyses

---
LHCb luminometers
N muons
N vertices
N Velo tracks
(best)
N backward tracks
N upstream hits
N hits in preshower
(SPD)
Calorimetric transverse energy
Measured in ≈1 kHz random stream of « nano-events » containing only “luminometers”.
N interactions per bunch crossing: μ ~ 1-2, calculated from Poisson law, μ = -log(P(0)), P(0)=fraction of “empty” events (eg. N vertexes = 0 or N tracks < 2). Less systematics as no strict linearity required.
Small beam-gas backgrounds (≤1-3%): estimated from non-colliding bunches and subtracted
Level 0 CALO trigger (or BCM when L0CALO is OFF) for online luminosity monitoring
μ is stored per smallest data unit (~10 sec running): low level “mixing” of physics and lumi-data
 <<1 % load to DAQ in CPU, data trafic and disk space.

---
ATLAS luminometers
1. BCM (diamond sensors) from LHC – best in Run I, train dependency in Run II
2. LUCID – newly installed and best in Run II: provides offline + online luminosity
3. Inner Detector (tracks) – bunch-by-bunch, but rate limited
4. Calorimeters: bunch integrating, currents in TileCal PMT, in EMEC and FCAL LAr gaps

---
ATLAS luminometers
Fractional stability between LUCID and other ATLAS luminometers versus time,
LUCID run-to-run stability = 1.3%

---
CMS luminometers
Run II
- 3 luminometers independent of central DAQ (“always” operational):
   a) Pixel Luminosity Telescope (PLT),
   b) Fast Beam Conditions Monitor (BCM1F), with a) uses zero-counting method,
   c) dedicated readout on hadronic forward calorimeter (HF), afterglow correction, best online+offline
- 2 luminometers in main CMS DAQ:
   a) muon drift tube “track” counter (DT), integrates bunches,
   b) pixel cluster counting (PCC) with “zero-bias” trigger, after exclusion of some modules and time dependent afterglow corrections – similar precision to offline HF

---
ATLAS and CMS
- high pile-up μ ~ 40: fraction of “empty” bunch crossings is essentially zero, μ = - log(P(0)) method directly not applicable (but can be recovered by redefining “visible” event as occupying 1/40 phase space eg. in acceptance, having muon etc.)
- without μ = - log(P(0)): luminometer linearity = dominating source of systematics:
dependence on pile-up, LHC filling scheme (eg. bunch spacing) etc.
- in vdM calibration fills: μ ~ 1, large linear dynamic range required to extrapolate to physics μ ~ 40
- special emphasis (not really justified?) to have precise luminometer independent of common detector DAQ
- ageing of luminometers and other instrumental instabilities require
a) corrections and
b) vdM re-calibrations every year.
In LHCb measured visible cross-section is stable.
- CMS: beam-gas background can not be estimated from be, eb crossings and subtracted (by luminometers design), parameterized in vdM scan fits.
- CMS: a few minutes, short vdM scans (called “emittance”) in beginning / end of every fill.
Take physics time, but necessary to (approximately) re-calibrate luminometers, measure ageing effects and pile-up dependences

---
CMS luminosity in 2017

---
ATLAS and CMS overall precision
Excellent precision!

---
Extrapolating from vdM to physics

---
ALICE luminometers
- Very low μ = 0.001 - 1
- Only two detectors (no redundancy)
- In 2015 overall luminosity measurement precision = 2.3% for isolated bunches,
3.4% for bunch trains (because of non-trivial systematics in V0)

---
Absolute calibration of L
color red {L= {N_1 N_2 f} over {A_eff} = N_1 N_2 f iint %rho_1(x,y) %rho_2(x,y) dxdy }
N1,2 are measured in three steps:
total beam intensities are determined from total beam currents (slowly) measured with high accuracy by LHC direct-current current-transformers (DCCT),
background (1-2%) in nominally empty LHC bunches or buckets is determined either with LHC equipment (BSRL) and/or with beam-gas interactions in LHCb and subtracted ,
charge fraction per bunch is measured with LHC fast transformers (FBCT)
Typical N1N2 uncertainty: ~0.2-0.3%.

---
Beam-gas imaging (BGI)
color red{iint %rho_1(x,y) %rho_2(x,y) dxdy }
Main difficulty:
Only at LHCb: find ρ1,2 from beam images recorded with beam-gas interactions.
The very first L measurement at LHC in 0.9 TeV pilot run in Dec 2009
To increase statistics: switch off VELO pumps;
from Nov 2011 on: inject a tiny amount of gas using a dedicated
injection System for Measuring the Overlap with Gas (SMOG)
(~50 more interactions)
SMOG is also used as a fixed target eg. for heavy ion physics
Beam-gas allows to measure “ghost” charge in nominally empty bunches
NIM A 553 (2005) 388
PLB 693 (2010) 69
X-Z
912 urad full crossing angle
Y-Z
First 1000 vertexes in fill 2852 (Run I).
Typical x,y (z) beam widths: 0.1 (40) mm
ΔY separation to reduce pile-up

---
Beam-gas imaging
Beam profiles are unfolded with VELO spatial resolution, determined from data as a function of N tracks, z position and interaction type (beam-beam or beam-gas).
To improve precision: ρ1,2 are fit to a sum of Gaussians simultaneously with the precisely measured beam-beam profile IP(x,y) ~ ρ1ρ2.
2D fit for one bunch pair as an example. Pulls are shown by color in ±3 range in the top.
J. Instrum. 9 (2014) P12005
The best BGI luminosity calibration precision (8 TeV data): 1.43%

---
Van der Meer scan
Idea: sweep one beam across the plane.

---
Van der Meer scan
Idea: sweep one beam across the plane. This integrates its ρ out:
and
iint color red{ %rho_1(x+%DELTA x,y+%DELTA y)} %rho_2(x,y) color red{d%DELTA x d%DELTA y} dx dy = 1
%sigma = iint %mu( %DELTA x, %DELTA y) d%DELTA x d%DELTA y / N_1 / N_2
Suggested by van der Meer in 1968.
Works for any ρ1,2 and any LHC crossing angle
(relativistic correction due to transverse velocity is negligible)
If ρ1,2 factorize in x,y:
        “Crossing point” x0,y0 may be chosen arbitrarily.
Another possibility: swept beam effectively becomes broad and uniform.
Similarly to “beam gas” it provides beam-beam imaging after unfolding with VELO resolution V:
CERN ISR-PO-68-31
%sigma = {int %mu( %DELTA x, y_0) d%DELTA x cdot int %mu( x_0 , %DELTA y) d%DELTA y} over {%mu(x_0 , y_0) N_1 N_2}
x0,y0
Raster
scan
Scan along X,Y axes (done at LHC)
IP = (%rho_1 %rho_2) circ V
NIM, A 654 (2011) 634
[ %rho_2 circ V ] ( x ) ~ prop ~ int IP( x, %DELTA x) d%DELTA x
(for Δx in frame of fixed beam 2)

---
Van der Meer scan
μ in one bunch crossing in X, Y scan
%sigma = {int %mu( %DELTA x, y_0) d%DELTA x cdot int %mu( x_0 , %DELTA y) d%DELTA y} over {%mu(x_0 , y_0) N_1 N_2}
X-Y non-factorizability can give ~1% bias, not easily visible (except with BGI):
- from luminous region fits
- “offset” and “diagonal” scans
μ(Δx, y0)
μ(x0, Δy)
25(45) kHz rate of “lumi”- events in Run I (II)

---
vdM length scale calibration
        directly depends on Δx,Δy scale.
Calibration: beams move synchronously in X or Y.
IP movement (by the same amount) is precisely measured by VELO (and can be cross-checked by BGI).
%sigma prop int ... d%DELTA x int ... d%DELTA y
Measured deviation from LHC scale
Mismatch btw IP and BGI beam1,2 average gives systematics
IP movement

---
Observations in recent pp vdM scans at LHCb

---
Recent pp vdM scans at LHCb: observations
Length Scale Calibration (LSC) in fill 4269, 25 Aug’15 : LHC X- and Y-displacements were incorrectly written manually as equal. 3.5% mistake found by checking the bump magnet recordings in LHC data base. In later vdM scans the displacements were logged automatically.
FBCT measurement of N particles per bunch before 2017 :
2-in-1 device for odd / even bcid, with a few % different slopes and offsets.
To equalize : ATLAS BPTX (noisier but immune to odd-even difference). Bcid can be wrong by 1-4.
Now : much better new FBCT
odd bcid
even bcid
6 %

---
Recent pp vdM scans at LHCb: observations
Fill 6012 (Jul’17) : unexpected instabilities in 3 and, after 2 scans, in 19 out of 24 bunch crossings (current drops, width increase)
Only 5 good pairs used in all scans
Changed to non-Gaussian
current drop
vdM profile changed
Length Scale Calibration (LSC) : beam displacements set by LHC precisely verified by Velo.
LSC in fill 4269 : X- and Y-displacements were incorrectly written manually as equal. Mistake found by checking the bump magnet recordings.

---
vdM scan with beam gas imaging
SMOG during vdM scan is very attractive cross-check:
+ measures individual bunch profiles, their movements and length scale, but
- introduces huge backgrounds.
Solid points: background is not fully subtracted from Velo-based track and hit counters.
In fill 6012, Jul’17 : μ(head-on beam-beam) ~ 0.25, μ(SMOG) ~ 0.13,
    after background subtraction Δμ(SMOG) ~ 0.001 – 0.002 remains.
Therefore, final cross-section is obtained from Vertex>0 by rescaling with coefficient determined without SMOG.

---
Preliminary 13 TeV pp cross section
Preliminary: still, a few things to finalize.
Spread between 15 scans in 2015,16,17,18:
   0.5 % – excellent time stability without any corrections (!) contrary to ATLAS/CMS.
Probably, final systematics will be ~2% or less.
σ(Velo>1), mb	63.7
Early 2015 BGI measurement	63.4 ± 3.9 % (-0.6%)
preliminary BGI, fill 4937	65.8 (+3.1 %)
	Error, %
DCCT	0.16
Ghost charge, BGI+LDM	<0.1
FBCT A/B/BPTX	<0.1
LSC	<0.5
Fit model	0...0.5
statistics	<0.1
Scan-to-scan variations within one fill	0.2...0.6
Fill-to-fill variations	0.4
RZ Velo – Velo diff.	0...0.2 when SMOG off
Typical uncertainty of extrapolation from vdM to physics: ~ 0.5% (stability of luminometer ratios)

---
Other methods of luminosity calibration

---
LHCb: Luminosity of p-He sample √s =110 and 86 GeV
PAMELA + AMS-02: excess in anti-p / p fraction
– sign of dark matter or wrong model of anti-p production in interstellar medium of galactic disk?
Largest uncertainty from σ(p+He → anti-p X)
Measurable at LHCb as fixed target process: p – He (SMOG)
Critical to know SMOG pressure, but difficult to measure precisely because it is very low
Take SMOG density from p - (atomic) e elastic scattering,
using its known Rosenbluth cross-section.
Precision: 6% !
"Measurement of antiproton production in p-He collisions at √sNN=110 GeV", https://arxiv.org/abs/1808.06127, submitted to PRL.
Same approach will be used for heavy flavor production measurements in p-He.

---
Physics reaction as a luminometer
Z0 → ll counting (used in ATLAS and CMS) can be useful in relative luminosity debugging (validate corrections, long-term stability)
Example: N(Z0) / L, should be constant, from 2015 CMS report
Earlier proposal (eg. in LHCb): two-photon pp→ pp μ+μ-,
proton compositeness can be neglected, QED precise cross-section allows to calibrate luminosity;
but very low statistics and requires very forward coverage to veto backgrounds – not competitive.

---
Novelties in 2 most recent vdM scans at LHCb
Experiments typically do symmetric X,Y vdM scans with minimal variations.
From end 2015 LHC allows to define scan points arbitrarily, however.
1) Nov’17, 5 TeV pp, 1 hour: LHCb has tried for the first time two-dimensional vdM scan
2) Jun’18, 13 TeV pp, 3.5 hours: many novelties (on the next slides)

---
First ever quasi two-dimensional scan, Nov’17
Cross-section ~ integral over X-Y beam separation plane.
Standard vdM: along X, Y axes, assuming factorization : μ(∆x, ∆y) = μ(∆x, 0) μ(0, ∆y) / μ(0, 0).
Factorization cross-checks up to now: diagonal scans and scans along x=const or y=const lines.
Full two-dimensional scans are expensive (too many points). In Nov’17 LHCb scanned central region giving maximal contribution to the integral.
 contribution to cross-section

---
Mismatch btw. factorization and 2D cross-section integrals
… for 22 bunch crossings. Red : average line with expected from spread error band.
Mismatch for Velo : 0.11±0.10 % – excellent accuracy and agreement.
Full χ2 analysis of 44 scan points, ie. of 22 x 44 = 968 underdetermined factorizability equations also gives reasonable agreement (deviation at only 6σ probability in spite of excellent stat. precision).

---
Jun’18, 13 TeV pp vdM scan
- Same 2D scan as in Nov’17
- Special program to study beam orbit drifts (difficult to control during “standard” scans)
   a) multi-pass X,Y scans b) spiral 2D
4 passes (2 forward + 2 backward) instead of one, every side of the spiral allows to
each allows to find when beams are head-on and find head-on position and measure drifts
measure drifts during the scan

---
Jun’18, 13 TeV pp vdM scan
- since beams are moving not in one direction during scan, important to check the absence
of hysteresis effects in LHC magnets: forward – backward through the same points
in addition,
- more sophisticated length scale calibration
- beam-beam imaging when one beam is at rest
        Lot’s of interesting and new data to analyze!

---
Conclusions
Luminosity measurement is a technical service, but very much needed.
Eg. in LHCb used in ~15% of all publications.
Current LHCb pp luminosity precision 3.9-3.8% from early BGI measurements in 2015.
When finalized, vdM scans should give ~ twice better precision.
Run I, 8 TeV pp: 1.16% from combination of vdM and BGI, record for bunched colliders,
J. Instrum. 9 (2014) P12005, arXiv:1410.0149.
My opinion: LHCb luminosity measurement is very well designed, excellent time stability,
reference calibrations stable in 2015-2018 without need of any correction at hardware level
Lack of manpower in LHCb lumi group, only 2-3 experts and having also other duties.
Rosen Matev (convener) is now on CERN long duration contract fully on HLT.
BGI not covered, George Coombs finishes his PhD.
Many novelties in last 2 vdM scans at LHCb, data to be analyzed.
First 2D scan results are very positive.
Ideas for upgrade are welcome