## Slide 1: PRAE Dechirper for ProRad exp.
Projet Emblématique
Programme SESAME
With the support of
Sandry Wallon
2018.11.28 – réunion du groupe diagnostiques

## Slide 2: Outline 1/3
Dechirper for PRAE used to correct the beam longitudinal phase space portrait.
  Longitudinal wake field to be generated.
  Avoid (minimized) transverse wake field (dipole and quadrupole effects).
  sE/E < 5x10-4 required by final user (ProRad exp.)
Dechirper and its applications – 23 May 2014 Heung-Sik Kang
Pohang Accelerator maboratory

## Slide 3: Outline 2/3
  Corrugated structure used to generate wake fields
Wake measurements of a dechirper jaw with nonzero tilt angle - 29 May 2018
Karl Bane, Marc Guetg, Alberto Lutman, SLAC
To minimize transverse wake field, jaws need no tilt w.r. to the beam
Side talk : “Obviously”, the beam must see two corrugated surfaces symmetrical together (one of the wake field component then equals to zero)  consideration to be taken into account for the manufacture of the 2 jaws (e.g. machining during the same operation)
jaw1
jaw2

## Slide 4: Outline 3/3
Existing dechirpers / sources of inspiration :
  LCLS project at SLAC : 1 hori. + 1 vert. dechirpers (hori. model showed a 25 mm backlash issue ; vert. model intended to have no tilt issue thanks an unusual design [See May 2018 paper quoted previous page]).
  LAL collimator project at ATF2 (not a dechirper, but some affinities ; showed linear disp. statistical error within +/- 3 mm)
Jaws’ specifications :
  Not known yet (required wake depends on beam dynamics)
  First mechanical design done w/ 1 m long jaws (LCLS used 2 m long jaws… and 2 “crossed” dechirpers. Only one dechirper for PRAE.

## Slide 5: Dechirper model (1/2) (main subsystem)
Dechirper main subsystem (right pic)
Features :
Follows the KISS principle (i.e. make it simple);
Different kind of actuators can be used (step motor, piezo element stack);
Compatible with different kinematics (regular style, or latest used at LCLS)
Dechirper main subsystem mounted on an optical table
NB. Dechirper’s jaws could move in a horizontal plane or a vertical one : it does not change the longitudinal wakefield, but change the direction of transverse one.
Shown CAD model is done for a horizontal dechirper, the simplest type.

## Slide 6: Dechirper model (2/2) (main subsystem)
Dechirper main subsystem can be mounted on an optical table, giving high flexibility to installed equipment (actuators, manual positioning stages, linear position encoders)
Mechanical interfaces : DN100CF flanges non-rotatable (used also as references for alignment)
One of the two jaw enables to move in a horizontal plane (slots – i.e. corrugated pattern – are vertical)

## Slide 7: Status, budget & WBS (1/3)
Budget done (next page);
WBS done (but not a planning) (next page);
Main subsystem designed ; drawings done, but update needed (jaw and actuators specs);
Jaw need to be specified  wakefield calculations to be done be Y. Han or by B. Bowen ?
ProRad’s ANR un-successfull  project postponed for the mechancial part.

## Slide 8: Status, budget & WBS (2/2)

## Slide 9: Status, budget & WBS (2/3)
Dechirper budget & "non fine tuned" WBS |  |  |  |  |  |  |  |  |  |  |  | 
Sandry Wallon - édition 2018.11.27 |  |  |  |  |  |  |  |  |  |  |  | 
Pos. | Task | Field | Item / work | Material only (if fab.at LAL) | Min price | Max price | Qty | Tot. Price (min) € | Tot. Price (max) € | Brand / supplier / Human R. | LAL's HR - estimated work time required (wk) | Rem.
1 | 1.1 | Mec. design | Derchirper main subsystem |  |  |  | 1 |  |  | LAL | not estimated | Raphael Vilar (Trainee) - DONE
2 | 1.3 | Mec. drawing |  |  |  |  | 1 |  |  |  |  | Raphael Vilar (Trainee) - DONE
3 | 2.1 | Mec. design | Derchirper - linear actuators integration |  |  |  | 1 |  |  |  |  | Sandry Wallon, trainee
4 | 2.2 | Mec. drawing |  |  |  |  | 1 |  |  |  |  | Trainee
5 | 3.1 | Mec. design | Adjustable interface between derchirper support (table) and ground |  |  |  | 1 |  |  |  |  | See LAL's mec. Dpt : proposed interface shown at 2018 PRAE workshop (hoof style) - (final table leg specs to provide to Mec. Dpt)
6 | 3.2 | Mec. drawing |  |  |  |  | 1 |  |  |  |  | 
9 | 4 | Mec. drawing | General layout drawing |  |  |  | 1 |  |  |  |  | Trainee
10 | 5 | Manufacture (machining, welding) | Chamber (flanges quoted below) | Y | 100 | 600 | 1 | 100 | 600 |  |  | 
11 |  |  | Stems w/ flange to be welded | Y | 10 | 20 | 4 | 40 | 80 |  |  | 
12 |  |  | Misc. Parts | Y | 300 | 400 | 1 | 300 | 400 |  |  | 
13 |  |  | Jaw (1 m long) |  | 1500 | 4000 | 1 | 1500 | 4000 | KG industrie or other |  | Specs unknown on Nov. 2018
14 | 6 | General supplies | Metal bellow w/ 2 DN40CF flanges |  | 350 | 350 | 4 | 1400 | 1400 | Mewasa |  | 
15 |  |  | Optical table w/ legs (bench) |  | 2418 | 6000 |  | 0 | 0 | Micro Controi Instrument Ltd or Thorlabs |  | Solid Vibration Isolation vs pneumatic Vibration Isolation
16 |  |  | Solid aluminum breadboard probably to be machined from Al board (at LAL) or standard breadboard | Y or N | 200 | 1300 |  | 0 | 0 | LAL or Thorlabs |  | 
17 |  |  | Block for linear slide |  | 88 | 120 | 4 | 352 | 480 | Hiwin or other |  | 
18 |  |  | Rail for linear slide |  | 221 | 300 | 2 | 442 | 600 |  |  | 

## Slide 10: Status, budget & WBS (3/3)
19 |  |  | DN40CF non-rotatable flange |  | 28 | 28 | 8 | 224 | 224 | NEYCO |  | 
20 |  |  | DN100CF non-rotatable flange |  | 154 | 154 | 2 | 308 | 308 | NEYCO |  | 
21 |  |  | Special screws and washers (vented, molycoated) |  | 200 | 200 | 1 | 200 | 200 | MDC |  | 
22 |  |  | Regular screws, washers and nuts |  | 50 | 50 | 1 | 50 | 50 | LAL's warehouse |  | 
23 |  | Sensitive supplies | Linear actuator w/ electonics (e.g. linear stage based on step motor w/ brake, EGSK-26-100-2P like) |  | 1800 | 1800 | 4 | 7200 | 7200 | FESTO or other |  | Check thrust needed ; Tx and Rz coupled -> 4 same actuators ; if Tx and Rz uncoupled -> 2 types of actuators
24 |  |  | Linear position encoder (LVDT - linear variable disp. tranducer) |  | 200 | 500 | 4 | 800 | 2000 | Misc. |  | likely requested "accuracy" : 1 um ; Warning : "While most LVDTs are magnetically shielded, it is recommended that ferrous metals should not be located closer than 1/4 inch from the open end of the LVDT body."
25 | 7 | Checks | Linear actuators and linear encoder to be checked and assess the performance |  |  |  |  |  |  | LAL |  | "volunteer?" ; devices could be checked w/ LAL's interferometer -> Statistical and systematic errors to assess
26 | 8 | Checks | Parts dimensions and specs to be checked w/ CMM |  |  |  |  |  |  |  |  | Bruno Leluan
27 | 9 | Cleaning | Cleaning for vaccum app |  |  |  | 1 |  |  |  |  | LAL's vacuum group
28 | 10 | Mechanical assembly | Assembly |  |  |  | 1 |  |  |  |  | Filip Rudnyckyj (proposal)
29 | 11 | Checks | He leak test |  |  |  | 1 |  |  |  |  | LAL's vacuum group
30 | 12 | Electrical supply | Box for 2 controllers and 1 power supply |  | 106 | 150 | 2 | 212 | 300 |  |  | See Patrick Cornebise
31 |  |  | Misc. Parts for controller box |  | 101.5 | 150 | 2 | 203 | 300 |  |  | 
32 |  |  | (set) Basic cables (PC to controler : RJ45 ; 24/48VDC power supply to controler) |  | 0 | 100 | 4 | 0 | 400 |  |  | 
33 |  |  | (set) Encoder and motor cables (if longer than 8 m) |  | 0 | 100 | 4 | 0 | 400 |  |  | 
34 |  | Design & drawing | Controler box - wiring diagramm and boxe machining drawing |  |  |  | 1 |  |  |  |  | Patrick Cornebise (proposal)
35 |  | Electrical assembly | Controler box w/ power supply and controler |  |  |  | 2 |  |  |  |  | Patrick Cornebise (proposal)
36 | 13 | Checks | Test of assembly with its "power supply" (test with power on) - Adjust jaws position w/ respect of external references - final test under vacuum condition and w/ power on |  |  |  | 1 |  |  |  |  | Bruno Leluan + "volunteer?"
37 | 14 | Installation | Installation |  |  |  | 1 |  |  |  |  | Sandry Wallon + Filip Rudnyckyj (proposal)
 |  |  |  |  |  |  | Total (€) | 13331 | 18942 |  |  |