## Slide 1: PICMIC status
I.Laktineh
E. Bechetoille, H. Pham, Y. Zhao, H. Mathez, L. Zhang, I. Vallin, G. Dozière
Ch. Hu, C. Colledani, S. Callier
D. Charlet, J-P. Cachemiche, Ch. Combaret
Journées R&T, IJCLAB, October 2021

## Slide 2
MCP is considered as the best timing device with a few
picoseconds of time resolution.
Most often there are two plates with the channels oriented in a slightly tilted way (chevrons) to increase the gain and at the same time reduce the ions return impact.
1st gap
pores in
glass
with 2dry
emitter
2d gap
a few mm
200 V
1- 2kV
200 V
Anodes (1.6 x 1.6mm2 pixels)
Photo-cathode
vacuum
Courtesy: J-F. Genat

## Slide 3
X,Y
T2
T3
T4
T5
T6
T1
Grid
Pixels
MCP
  To exploit MCP and similar sensors we propose the following scheme:
  A transparent grid placed downstream, read out by sensors with excellent time resolution
  An original detection matrix with micrometric pixels to measure with great precision the position of the avalanche while requiring limited number of electronic channels.
Time + position
Position+ time
Readout scheme
Patent: PCT/2020/050058

## Slide 4
Setup structure
⍺ source

## Slide 5
Current setup: Timing sensors+1 pad position

## Slide 6
Octopus-PCB
Time Measurement

## Slide 7
8-point PCB for the time measurement.
SAMPIC: TDC ASIC allowing to reach 3 ps time resolution
Principle components for this measurement already exist.
Time Measurement

## Slide 8
DT

## Slide 9
La triangulation seems to work quite well
(4-channel configuration)
X(mm)
Y(mm)

## Slide 10
Time Measurement
A board integrating a low-jitter timing preamplifier and discriminator (LIROC-OMEGA) as well as a precise TDC (picoTDC-CERN) was conceived.
The board will allow the communication with the position electronics through a dedicated DAQ board (IDROGEN)

## Slide 11
To reach few microns resolution with a limited number of electronic channels, a genuine concept was developed, successfully tested and patented.
NXN  3N : Reduction of electronic channels, power consumption and occupancy
Connect the pixels in woven strips
Two neighboring pixels are connected to two different strips
Each strip is connected to one electronic channel
Share the charge among a few ones
Crossing the fired strip to determine the position
Position measurement
Patent:PCT/EP2018/053561

## Slide 12
Exploiting the expertise IN2P3 in µelectronics, we propose to read out the connected pixels by CMOS discriminators in TJ 180 nm (6 metal layers) technology.
Position Measurement

## Slide 13
X-talk study was performed taking into account the technology, the geometry of the circuit, and the nature of the signal and its amplitude with the expected current (0.17-1.7 mA) the X-talk < 10%
Current mirror + Current discriminator were proposed and carefully studied to check the stability and performance of such a FE electronics

## Slide 14
PICMIC Architecture
Parameters | Value
Design Flow | Cadence DoT flow
Technology | TJ CIS 180nm
Power supplies | 1.8V
Power density | >172mW/cm² (only analog static current)
Die dimension | ~7.5x7.5 mm² (6.5x7.5mm² active)
Anode dimension | ~22µ²(5µm hexagonal pitch)
Readout pixel dimension | 50µmx140µm
Readout matrix | 128x54 cells (only 2556 active)
Input clock | 40MHz
Read-out port | 13-bit parallel, 1 sync clock out, 1 marker (programmable 1clk cycle resolution)
I/O Pad | CMOS
Slow control | I2C
Max data rate (1Mhz hit rate) | 390Mbps
Priority Encoder

## Slide 15: PICMIC Layout
Only 2556 RO cells are active among the 6912
The active RO cells are placed in a way to improve heating dissipation
The 2556 RO cells allow reading out the
2 216 000 pixels

## Slide 16
VDD
GND
GND
S1
S2
S3
Idet
(Idet < 0)
Ith2 (S1,S2)
Ith1 (S3)
Current
Comparator
Current
Mirror
VDD
D1
VDD
D2
Vref_P
Vref_N
ENA_CM
ENA_CM
ENA_CM
ENA_CM1
ENA_CC
ENA_CM
Iadj
I_adj<0:2>
VBP
I_gain<0:1>
MUX
ENA_D2P
VBNadj
To DFF
Out_EN
PWR
VDD
Internal
GND
Out_EN
Pulsing
Vin
TOCHECK
VBN
ENA_D1P
Dac_P
1-200µA
8 bits
Dac_N
1-200µA
8 bits
Vref_P
Vref_N
Dac_CM
3-7µA
8 bits
VBN
A
B
Pad
VBP
Pad
Column lines
GND
VDD
ENA_IP
ENA_IPb
VDD
ENA_INb
GND
ENA_IN
ENA_CM1
ENA_D2P
VBNadj
Dac_Iadj
0-5µA
8 bits
Pad
C
D
Vin
Pad
VDac_BP
Cible 700mV
8 bits
E
F
ENA_D1P
Front End lock

## Slide 17
Interconnected by skill-script routing
Connection between the detection pixels and the 3-direction strips
Connection between the 3-direction strips and the RO cells
Connections

## Slide 18: Part of the script that generates the random interconnection
~3400 coded lines
~50 functions
for placement, visualisation, layout/schematic generation, etc.
Connections
Connection between the detection pixels and the 3-direction strips
Connection between the 3-direction strips and the RO cells

## Slide 19: PIMIC Simulation (Digital Matrix + Peripheral)
The simulation validates:
  I2C Register R & W
  Analog matrix output by different hit patterns
  Output data stream with CTS
Output data stream
Write Configuration Registers
Read Configuration Registers

## Slide 20: Development Progress
Task/Bloc | RTL/schematic | Simulation | Implementation | Validation | Task repartition
Analog FE + Metal Anode |  |  |  |  | IP2I
FE Testability |  |  |  |  | IP2I
RO Digital matrix (PE+Config+Memories) |  |  |  |  | IPHC + IP2I
Col PE Readout |  |  |  |  | IPHC
I2C+Registers |  |  |  |  | IPHC
Analog DAC |  |  |  |  | IPHC
DATA Emulation |  |  |  |  | IPHC
SEQUENCER |  |  |  |  | IPHC
Power routing & floor planning |  |  |  |  | IPHC + IP2I
Pad ring |  |  |  |  | IPHC+IP2I
Full digital data flow simulation with emulation analog input |  |  |  |  | IPHC
Full circuit integration |  |  |  |  | IPHC+IP2I
Next step: to design a DAQ board
Chip/sensor submission is foreseen for the 15/10/2021

## Slide 21
We need to associate the timing information with the position information to provide the final output.
Grid time (ps)
Pixels time (ns)
This requires a board that allows the configurations of the timing and the position electronics, their synchronization and to transmit the data to PC.
Pixel board
Time board
Det.
IDROGEN
PC
Acquisition

## Slide 22
To be able to exploit the IDROGEN board we need:
develop appropriate interface/mezzanine boards between the IDROGEN and the timing and position boards.
develop appropriate firmwares
A generic board (IDROGEN) developed within the DAQGEN of the IN2P3
does exist. We propose to use it.
Acquisition

## Slide 23
Demonstrator
The work to conceive a full demonstrator of the PICMIC has started

## Slide 24
The project to build a PICMIC demonstrator with MCP was recently selected as a laureate for the Pre-Maturation CNRS projects  150 k€
This, with IN2P3 spport, will allow the construction of a demonstrator in 18-24 months.
+6m
+6m
+6m

## Slide 25
Conclusion
A great enthusiasm
Excellent collaboration among the different actors
Great help from the DAT (many thanks Rodolphe)
We are slightly behind the schedule but we foresee to have our demonstrator and test it in 2022.
Next step is to replace the MCP by NCP and do better

## Slide 26
Backup

## Slide 27
Courtesy J.Vallegra

## Slide 28: Matrix data taking (internal signals)

## Slide 29
Current Mirror
Current Comparator
Input transistor
Gain Stage
Input Current
Output Current
Comparator stage
Shaping Stage
Mux Stage :
Same polarity in both cases
Current mirror + Current Comparator
Current Comparator Only