## Slide 1
PERLE Injection Line Design Review
Introduction
Walid Kaabi- IJCLab/CNRS
16 December 2020

## Slide 2: Introduction to PERLE
[2] J.L. Abelleira Fernandez et al, “ A Large Hadron Electron Collider at CERN: Report on the Physics and Design Concepts for Machine and Detector “, J.Phys. G39 (2012) 075001, arXiv:1206.2913
PERLE: A proposed 3 turns ERL, based on SRF technology, to serve as testbed for studying, testing and validating a broad range of accelerator phenomena & technical choices for future projects.
Target Parameter | Unit | Value
Injection energy | MeV | 7
Electron beam energy | MeV | 500
Normalised Emittance γεx,y | mm mrad | 6
Average beam current | mA | 20
Bunch charge | pC | 500
Bunch length | mm | 3
Bunch spacing | ns | 25
RF frequency | MHz | 801.58
Duty factor |  | CW

## Slide 3: Global ERL landscape
PERLE
legacy, decommissioned
Operating (SC, NC)
potential future machine
planned
cERL-KEK
legacy, decommissioned
Operating (SC, NC)
potential future machine
planned

## Slide 4: PERLE Configuration
DC = lRF/2
7 MeV
DE = 80 MeV
7 MeV
1 : 3 : 5
2 : 4 : 6
dump
injector
DE = 80 MeV
2 Linacs (Four 5-Cell 801.58 MHz SC cavities)
3 turns (160 MeV/turn)
Max. beam energy 500 MeV

## Slide 5: PERLE Timeline
The Collaboration is currently developing a detailed time schedule. Currently it is foreseen to complete the TDR by 2022, Phase 0 by 2025, Phase 1 by 2028 and Phase 2 by 2030. A scheme of milestones will be worked out and agreed upon with emphasis on the accelerator but including a timeline for future experiments.
2028
End Phase 1: PERLE @ 250MeV
2030
End Phase 2: PERLE @ 500MeV
2025
End Phase 0: Injection line
2022
PERLE TDR

## Slide 6: Lattice design optimisation of switchyards and circulating arcs
Design and prototyping of main magnets for arcs and switchyards
Courtesy to A. Bogacz and C. Vallerand

## Slide 7: R&D toward PERLE TDR
Lattice design: optimization of arcs and switchyards lattice, study of optics tolerances, magnets specifications, start to end simulation.
BBU study in high average current environment: cavity design optimization for an efficient extraction of HOMs considering PERLE parameters: bench pattern recombination, current threshold, cryogenic efficiency…
Collective effects study: effects of Coherent Synchrotron Radiation (CSR) and Longitudinal Space Charge (LSC) on beam quality, microbunching instability and ion cloud mitigation.
Particle tracking studies of halo formation and control of beam loss.
LLRF and feedback system development: RF control and stability under maximum practical QLoad, development of multi-bunch BBU feedback systems.
Beam diagnostics development

## Slide 8: PERLE SRF System development
Design and prototyping of a full dressed SRF cavity: demonstration of level of SRF performance required in CW operation, high-average current environment, adequate damping of HOM.
DQW HOM Coupler
Linac cryomodule design: study the possibility of SPL cryomodule adaptation to PERLE need, complete design of a cryomodule for PERLE later.
Design and prototyping of an input power coupler
HOM coupler study
Q0 (2k) = 3 e10 @ ~27 MV/m
Quench @ Eacc ~ 30 MV/m
Courtesy to F. Marhauser

## Slide 9: PERLE injection line
It consist of:
A DC photoemission electron gun (The ALICE DC gun to be upgraded).
A bunching and focusing section: 401 MHz normal conducting buncher cavity placed between two solenoid.
A superconducting booster with five 802 MHz cavities individually supplied and controlled on amplitudes and phases.
Merger to transport the beam into the main LINAC,
Beam diagnostics to be placed between components.
Photocathodes choice:
Sb-based photocathodes (unpolarized electrons) operated at 350 kV
GaAs photocathodes (polarized electrons) operated at 220 kV
Photocathode gun
Focusing solenoids
Light box
Buncher
SRF booster
Photocathode laser choice:
Nd:YAG laser (532 nm) or Ti:Sapphire laser (400 nm).
Courtesy to B. Militsyn & B. Hounsell

## Slide 10
Thank you for your attention!
MESA ERL simulation©