Silver ion production with RIALTO
Anahí Segovia Miranda

---
Outline
- Laser Resonance Ionization Technique
- RIALTO facility
- Silver Production
- Outlook

---
Laser Resonance Ionization
[Speaker Notes: Pure ion beams Efficient and selective way to ionize exotic isotopes]

---
Laser Resonance Ionization

---
ALTO and RIALTO facility
MLLTrap
PolarEx
BEDO
LINO
2 high power Nd:YAG (532 nm, 100W and 35W)
3 dye lasers (540–850nm) with BBO doubling units(270–425nm)

---
RIALTO « Old » layout
Nd:YAG 100W max

---
RIALTO upgraded layout
Nd:YAG 35W max
Nd:YAG 100W max
Improving non resonant step
Improving beam distribution
Stabilization system

---
RIALTO upgrade
- Improving the quality of the non resonant step
  - 2nd YAG laser and external trigger unit
- Beam Distribution System that allows changing schemes.
  - Cube beam splitters and waveplates.
- Beam Stabilization System.

---
RIALTO Upgrades. YAG laser and trigger unit
- Up to 35 W (63 A)
- Gaussian profile for ionization step
- Temporal synchronization with
  new trigger unit

---
RIALTO Upgrades. Beam Distribution
Polarazing Beam Splitter (PBS)
Waveplate

---
Beam Stabilization System
YAG position without stabilization system
Position
Angle
YAG position with stabilization system

---
Silver Ionization Scheme
Challenging Scheme
  - 3 step-3 color scheme
  with no resonant last step
  - Green laser (second step)
  - UV first step
Motivation
  - POLAREX (LTNO)
  - MLLTrap
  - LINO
  - BEDO
  - ...

---
Atomic Beam Unit (ABU)

---
Ag Test. Transversal configuration

---
Wavelength scan and saturation power
First step saturation curve. Saturation power .83 mW ± 0.12
Wavelength scan for the first excitation step.
Second step saturation curve. Saturation power 3.28 mW ± 0.81
Wavelength scan for the second excitation step.

---
YAG Delay
{1} over {A} approx 11ns
YAG Decay time ≈ 14ns
20 W
300 mW
A=8.6e+07 s-1
40mW

---
Summary
- Upgrade of RIALTO
  - New YAG with external trigger unit
  - Beam distribution
  - Stabilization System
- Ag off-line production
  - Wavelength scan
  - Saturation curves
Temporal overlap

---
Outlook
- Online Ag and Ga beams.
- Stabilization system for UV
- Tripling frequency for Sb
- Sb production in ABU
- Zn, Cu, beams...

---
Thank you !

---
Heating Cycle and YAG heating

---
Back-up

---
First step saturation curve. Saturation power 4.74 mW