## Slide 1: The EPIC proposal @ ISOLDE
G. Georgiev
A personal view and a collection of presentation from the EPIC workshops

## Slide 2: Exploiting the Potential of ISOLDE at CERN
Take advantage of LIU upgrades: proton BOOSTER energy (1.4 GeV  2 GeV) and intensity increase
  Gain a factor of 1-20 in radioactive beam intensity
Install additional target station(s): allow parallel beams
  double the beam time for an increasing amount of users (more than 80 accepted experiments, typically 30 new per year coming)
An upgrade of HIE-ISOLDE – reaching 10 MeV/u for all masses
Install a ‘Storage Ring’ for short-lived (low-energy) isotopes – unique worldwide new opportunities in atomic, nuclear and fundamental (new) physics
A new experimental hall (new experiments coming – mostly low-energy for searching new symmetries/interactions)

## Slide 3: 2 GeV energy upgrade
Beam dumps replacement
  Material not conform to standards
  Unknown condition and signs of corrosion
  Required for Energy and Intensity upgrade
Beam dump exchange will be complex process and should take place during LS3 – preparations have started in 2020
Upgrading BTY line to transfer 2 GeV protons to ISOLDE
  It is feasible and there are two potential routes
  Will require statement from ATS Sector management before studies can commence.

## Slide 4: 2 GeV and Intensity upgrade
The yield will scale with intensity
Increase the target dose and frontend dose
Peak power and shocks may impact on target lifetime.
Fluence mapping (All particles)
1.4 GeV 3.5g/cm3
2.0 GeV 1.3g/cm3
Higher beam energy combined with target development may help reduce dose and increase target and frontend lifetime at higher intensities.
Increase of p-intensity ( x2)
The possibility to maintain both energies (1.4 GeV and 2 GeV) should be kept!

## Slide 5: 2 GeV and Intensity upgrade
Largest increase for the exotic n-deficient isotopes (Zisotope = Ztarget – (10 to 30)) factors of 2 to 40 predicted
Low Z isotopes (fragmentation):
  Increase in factors of 2 to 4
For neutron induced fission there is potentially higher contamination induced by scattered protons (but they will also scatter less) requires design considerations.
DB
Increase of PS-BOOSTER energy (1.4 to 2 GeV)

## Slide 6: Higher energy - double front end?
FLUKA Simulation: Ch. Duchemin
ISOLDE Target #1
UC2 3.5 g/cm3
19.6 cm length
0.7 cm radius
ISOLDE Target #2
UC2 7.0 g/cm3
10.0 cm length
2.5 cm radius
25 cm
1.4 GeV protons
M. Lozano
Two targets installed in series in a single front-end area profiting from the full proton current simultaneously.
Significant cost reduction in civil engineering
Overall RIB production would increase significantly.

## Slide 7: Upgrade of REX-ISOLDE
Ideally 10 MeV/u for all masses (some experiments not possible at lower energies)
Priority from the users to allow A/Q to be extended to 5.5
Upgrading the EBIS:
  Higher charge states and faster breeding time.
  Reduce pressure on the accelerator
Bunched beams for TOF measurements
RFQ
Buncher
ST3
ST4
ST5
ST6
CM1
CM2
CM3
CM4
ST1
ST2
CM5
RFQ
Buncher
IHS
7GP1
7GP2
7GP3
9GP
CM1
CM2
CM3
CM4
REX/HIE-ISOLDE today:
Room temperature upgrade of REX + fifth high-beta cryomodule:

## Slide 8: A new compact storage ring
Stored radioactive beams have many advantageous
Uniqueness: injection at the required energy (fast – shorter lifetimes accessible)
Can be used multiple times in an in-ring detector (luminosity increase!)
Can be cooled to deliver excellent quality beams to external experiments for high-precision studies
10 m
Talks given by:
Manfred Grieser (a new design)
Yuri Litvinov (physics)

## Slide 9: A new ISOLDE experimental hall and target stations
E. Siesling, J.A. Rodriguez - 2020 EPIC Workshop
AD pbar facility
PS Booster
BTY proton line from PSB to ISOLDE target area
ISOLDE experimental hall 170,
control & user building 508 and cryo buildings 198, 199
ISOLDE target area, Class A lab,
MEDICIS and nano-lab
Fire Brigade
CERN goods reception
Recuperation site building 133
Potential for a new ISOLDE Low Energy Nuclear Physics facility at CERN

## Slide 10
Facility Layout (general idea):
Experimental stations
Experimental stations
Beam dump
Target
01
Proton beam
Target
02
Mass separator dipoles
Time separator kickers
Slow released isotopes
Fast released isotopes
Target
03
Target
04
Mass separator dipoles
Time separator kickers
Beam dump
Proton beam
Slow released isotopes
Fast released isotopes
Beam
switchyard
High-resolution separator
High-resolution separator
Experimental stations
Beam characterization lines
J.A. Rodriguez, E. Siesling – EPIC Workshop – 2020/11/25

## Slide 11
Cross-section of the Proposed Hall and Underground Area:
15 m ?
5 m span crane
Vertical beamlines
Surface Level 0:
Experimental Hall
Underground Level -1:
Beam distribution and purification
Underground Level -2:
HT/RILIS/CV
Underground Level -3:
Target/Separator
Rutherford road
SAS Area
Surface:
New experimental Hall
Underground:
Target zone, Services and beam preparation
Access to
beam distribution level from the 508 side
17 m
TT70 tunnel use to transfer protons from the PSB

## Slide 12
15 m ?
4 m
5 m
1-3 m thick concrete shielding floor
Elevator/stairs shaft
Shaft to lower equipment
Separator areas
5 m span crane
Vertical beamlines
90 deg. separator magnets
Surface Level 0:
Experimental Hall
Underground Level -1:
Beam distribution and purification
Underground Level -2:
HT/RILIS/CV
Underground Level -3:
Target/Separator
6 m
Rutherford road
SAS Area
Surface:
New experimental Hall
Cross-section of the Proposed Hall and Underground Area:
Access to
beam distribution level from the 508 side

## Slide 13
25 m span, 15+ ton cranes
15 m ?
4 m
5 m
1-3 m thick concrete shielding floor
Elevator/stairs shaft
Shaft to lower equipment
Separator areas
5 m span crane
Vertical beamlines
90 deg. separator magnets
Surface Level 0:
Experimental Hall
Underground Level -1:
Beam distribution and purification
Underground Level -2:
HT/RILIS/CV
Underground Level -3:
Target/Separator
Beamline level: 1.75 m
Rutherford road
SAS Area
Cross-section of the Proposed Hall and Underground Area:
Access to
beam distribution level from the 508 side

## Slide 14
Cross-section of the Proposed Hall and Underground Area:
15 m ?
5 m span crane
Vertical beamlines
Surface Level 0:
Experimental Hall
Underground Level -1:
Beam distribution and purification
Underground Level -2:
HT/RILIS/CV
Underground Level -3:
Target/Separator
Rutherford road
SAS Area
Surface:
New experimental Hall
Underground area
Access to
beam distribution level from the 508 side
17 m
TT70 tunnel use to transfer protons from the PSB

## Slide 15: Layout of Underground Level -3: Target/Separator Zones:
Underground Level -3:
Target/Separator
30m
34m
Surface: 1020m2

## Slide 16
Boris tube
Robot rail
Double target front-ends
Robot control room
Target exchange point
Robot parking area
90 deg. separator magnets
Used target storage
Faraday cage of Target area 1
Laser injection points
Underground Level -3:
Target/Separator
Layout of Underground Level -3: Target/Separator Zones:
TT70 tunnel
Emergency exit to TT70
Faraday cage of Target area 1
Separator area 1
Separator area 2
2 GeV proton beamline
Shaft to lower equipment
Cooling and ventilation
Emergency stairs
Used target storage
Faraday cage of Target area 2
Beam dumps
Cooling, ventilation and cable trays shafts
Access lift and stairs
Bending dipoles

## Slide 17: Radiation shielding of Underground Level -3: Target/Separator Zones:
Concrete blocks (1 m thick)
Emergency exit to TT70
Separator area 1
Concrete wall (1 m thick)
Emergency stairs
Used target storage
Concrete wall (2 m thick)
Bending dipoles
Beam dumps
Concrete + iron walls (2 m thick)
Access to target area
Concrete movable door (0.75 m thick)
Concrete movable door (1 m thick)
Concrete blocks (0.75 m thick)
Concrete blocks
Concrete wall + blocks (1+1 m thick)
Concrete blocks (2 m thick)
Underground Level -3:
Target/Separator
Concrete movable door (1 m thick)
Separator area 2
Courtesy F. Pozzi
ISOLDE beam dump study preliminary nrs

## Slide 18: Target/Separator Ceiling Thickness:
~5 m thick ceiling
blocks above dump area increasing total to >7 m
2 m thickness
Standard thickness
1.0 m ?
2 m thickness
Underground Level -3:
Target/Separator
Shielding blocks behind building
Courtesy F. Pozzi
ISOLDE beam dump study preliminary nrs

## Slide 19
Cross-section of the Proposed Hall and Underground Area:
15 m ?
5 m span crane
Vertical beamlines
Surface Level 0:
Experimental Hall
Underground Level -1:
Beam distribution and purification
Underground Level -2:
HT/RILIS/CV
Underground Level -3:
Target/Separator
Rutherford road
SAS Area
Surface:
New experimental Hall
Access to
beam distribution level from the 508 side
17 m
TT70 tunnel use to transfer protons from the PSB
Underground area

## Slide 20
Underground Level -2:
HT/RILIS/CV
Layout of Underground Level -2: HT/RILIS/CV Zones:
Surface: 1020m2
30m
34m

## Slide 21
Electronic racks for equipment at the separator level
Water station for target/beam dump
Laser rooms for targets in both separators
~37m2 each
Vacuum primary pumps
Gas storage tanks
Laser injection points
High tension rooms
Boris tube
Vertical beamlines shaft
Access lift and stairs
Shaft to lower equipment
Emergency stairs to target area
Regular stairs to upper levels
Target/separator areas filtering and ventilation
Underground Level -2:
HT/RILIS/CV
Layout of Underground Level -2: HT/RILIS/CV Zones:

## Slide 22
Cross-section of the Proposed Hall and Underground Area:
15 m ?
5 m span crane
Vertical beamlines
Surface Level 0:
Experimental Hall
Underground Level -1:
Beam distribution and purification
Underground Level -2:
HT/RILIS/CV
Underground Level -3:
Target/Separator
Rutherford road
SAS Area
Surface:
New experimental Hall
Access to
beam distribution level from the 508 side
17 m
TT70 tunnel use to transfer protons from the PSB
Underground area

## Slide 23
Underground Level -1:
Beam distribution and purification
Layout of Underground Level -1: Beam Distribution and Purification:
30m
34m
Surface: 1020m2

## Slide 24
Underground Level -1:
Beam distribution and purification
Layout of Underground Level -1: Beam Distribution and Purification:
Electronic racks for equipment
Ventilation for lower levels
Beam characterization lines (triplet + BI + tape station)
Vertical beamlines shaft
Access lift and stairs
HRS purification area
Stairs to upper and lower levels
Shaft to lower equipment
Vertical beamlines to experimental hall

## Slide 25
Access lift and stairs
Side access to
beam distribution level (under Route Rutherford)
Building 508
Control room and user building
Stairs to upper and lower levels
Route Rutherford
Shaft to lower equipment
Underground Level -1:
Beam distribution and purification
Layout of Underground Level -1: Beam Distribution and Purification:

## Slide 26
Cross-section of the Proposed Hall and Underground Area:
15 m ?
5 m span crane
Vertical beamlines
Surface Level 0:
Experimental Hall
Underground Level -1:
Beam distribution and purification
Underground Level -2:
HT/RILIS/CV
Underground Level -3:
Target/Separator
Rutherford road
SAS Area
Surface:
New experimental Hall
Underground:
Target zone, Services and beam preparation
Access to
beam distribution level from the 508 side
17 m
TT70 tunnel use to transfer protons from the PSB

## Slide 27
Layout of the experimental hall:
Surface Level 0:
Experimental Hall
72m
50m
Surface: 3600m2 Low E dedicated

## Slide 28
Layout of the experimental hall:
Surface Level 0:
Experimental Hall
72m
50m
Surface: 3600m2 Low E dedicated
Surface existing hall: 1380m2
Of which half is occupied by the GPS separator zone, the REX/HIE ISOLDE post-accelerator and HEBT lines
20m
69m

## Slide 29
SAS area
Layout of the experimental hall:
5 m wide passage
1.5 m wide passage
Experimental stations (14 with high-resolution separation)
Beam distribution lines
Experimental stations (6 without high-resolution separation)
Structural pillars (crane + roof)
Vertical beamlines from lower levels
Stairs to lower levels
Shaft to lower equipment
6 m
14 m
13 m
10 m
7.7 m
Surface Level 0:
Experimental Hall

## Slide 30
SAS area
Layout of the experimental hall:
Experimental stations (14 with high-resolution separation)
Beam distribution lines
Experimental stations (6 without high-resolution separation)
Stairs to lower levels
Shaft to lower equipment
6 m
14 m
13 m
7.7 m
Surface Level 0:
Experimental Hall
Experimental areas: 9: 6x10m (each 60m2) 6: 6x14m (each 84m2) 3: 6x13m (each 78m2) 2: 6x7.7m (each 46m2) 20 stations with a total surface: 1370m2
Comfortability large areas for housing setup + possible laser setup barrack and exp. infrastructure

## Slide 31
SAS area
Layout of the experimental hall:
Beam distribution lines
6 m
14 m
13 m
10 m
7.7 m
Surface Level 0:
Experimental Hall
Experimental areas: 9: 6x10m (each 60m2) 6: 6x14m (each 84m2) 3: 6x13m (each 78m2) 2: 6x7.7m (each 46m2) 20 stations with a total surface: 1370m2
Comfortability large areas for housing setup + possible laser setup barrack and exp. Infrastructure
11+ Low E experimental stations in the existing hall:
To compare: The new GLM/GHM zone is 57m2

## Slide 32
Summary (on the proposed new building)
The concept of the building - feasible from the Civil Engineering point of view. A study and implementation has started (Eliseo Perez-Duenas (SMB/SE))
The building and underground areas will be able to house the proposed machine with all its capabilities to fulfill the (future) needs of the nuclear physics community (talk by Alberto Rodriguez) as well as 20 sufficiently large footprints for the experiments
Advantages: - construction and commissioning can take place in parallel to running physics at the existing facility, securing nuclear physics at CERN - in terms of geographical position it opens the possibility for interconnection with the AD and even n-TOF, enabling promising future physics (talks by Michael Doser and Alberto Mengoni) - the existing ISOLDE facility would become fully available for HIE physics, MEDICIS and TID development as well as a possible storage ring
Staged approach can be used for the installation of the machine, however, the building with (most of) its infrastructure should be fully build at a first stage
Further possibilities to extend over a large area towards the west (Heli-port) securing another 50 years of ISOLDE Physics at CERN

## Slide 33: Next Steps
Preliminary feasibility study of a new building (civil engineering) looks promising – more detailed study is planned with the support of the ISOLDE Collaboration.
Current designs meant to be a starting point and to trigger discussions that could help refining the concept! Nothing is set in stone (yet).
Define what we want in a conceptual design report of the project, covering:
  The key physics cases and new scientific opportunities.
  The technical conceptual details of the project with input from CERN and ISOLDE collaboration communities.
The goal is to converge to a feasible concept that could serve the current and future community of users on 10-30 years time scale

## Slide 34: More details on EPIC
For more details on EPIC please visit the web pages of the 2 workshops held in
  2019: https://indico.cern.ch/event/838820/overview
  and
  2020: https://indico.cern.ch/event/928894/overview
To finish with a question: What could be the approach of this (ISOL-France) community towards EPIC?

## Slide 36: Uniqueness of different European facilities (as seen from ISOLDE)
SPIRAL-II (d,p 40 MeV, 5 mA and stable heavy ions up to 14 MeV/u, 1 mA)
  + S3 heavy elements and n-deficient regions from fusion-evaporation
    S3/REGLIS low-energy ISOL-type studies (direct or in DESIR)
    Post-acceleration of RIB’s with CIME up to 25 MeV/u
  + Ucx/ISOL clean beams of fission fragments (p and n-induced fission)
    To DESIR or for post-acceleration with CIME or …
SPES (p at 35-70 MeV, 0.2-0.5 mA)
  UCx/ISOL clean beams of fission fragments (p and n-induced fission)
    Post-acceleration with ALPI SC-Linac up to 10 MeVu
    ISOL low energy beams for applications (isotope production)
ISOLDE (p at 2 GeV, 2-4 mA)
  Multiple targets + ISOL intense RIB’s from spallation (Ztarget – 10 to 30)
  and fragmentation
    Low-energy ISOL-type precision studies and applications
    Large variety of post-accelerated RIBs with HIE-ISOLDE up to 10 MeV/u