## Slide 1: Introduction: Irradiations at ALTO
Journée Irradiations IJC Lab 17 novembre 2021
J.N. Wilson and A. Said

## Slide 2
Bibliométrie ALTO: publications (2017-2020)
Chart: 
| Physique Nucleaire | Astrophysique Nucleaire | Instrumentation/R&D | Interdisciplinaire
Thematiques | 28 | 8 | 15 | 5

## Slide 3
ALTO High Energy stable Beams (HEB)
Faisceaux standards du Tandem :
- H, 3He, 4He, ..., 14C, ... up to 127I
- Tension au terminal entre < 1 MV et 14.5 MV
- Faisceaux pulsés : largeur d’impulsion 1 - 2 ns; taux de répétition : 100 ns - 100 μs
- Nouvelle source d’ion  intensité x5  faisceaux difficiles (Mg, Ca)
ALTO - HEB
Tandem

## Slide 4
ALTO Neutron production/beams
ALTO - HEB
LICORNE
LICORNE: Unique, naturally directional quasi-monoenergetic neutron source neutron source:
Low background
High Flux: 108 n/s/steradian
En=0.5 – 4 MeV
Permits participation in European TNA Network
n
n
n
n
γ
γ
Sample
H gas target
0.5 µA 7Li
13-18 MeV
High complementarity with NFS@GANIL

## Slide 5: Energy Applications: Irradiations of nuclear materials
Xenon migration in UO2 under irradiation studied by SIMS profilometry
B.Marchand et al. Journal of Nuclear Materials 440, p562-567 (2013)
Xe and Kr represent 25% of total fission product yield. Gaseous fission products deform the fuel pellets and cladding. Limit the lifetime of fuel bundles in reactors
Understanding of the (implanted) Xe diffusion as a function of temperature and irradiation conditions

## Slide 6: Energy Applications: Irradiations of nuclear materials
Ion irradiation to simulate neutron irradiation in model graphites: Consequences for nuclear graphite N.Galy et al. Nucl. Instrum. and Meth. B: 409, p235-240 (2017)
Ion irradiation of 37Cl implanted nuclear graphite: Effect of the energy deposition on the chlorine behavior and consequences for the mobility of 36Cl in irradiated graphite
N.Toulhoat et al. Journal of Nuclear Materials 464, 405-410 (2015)
Structural modifications induced by ion irradiation and temperature in boron carbide B4C
G. Victor et al. Nucl. Instrum. Meth. B365 p30-34 (2015)
Irradiations at ALTO with 127I to induce accelerated material damage
B4C control rods
Graphite is used as a core moderator material
(some reactor designs)

## Slide 7: ARIS: Dark Matter Search, Liquid Argon TPC irradiation
Measurement of the liquid argon energy response to nuclear and electronic recoils
P. Agnes, et al. Phys. Rev. D 97, 112005 (2018)
Dark matter search liquid Argon detector prototype
Neutrons used as a proxy for WIMPS
Characterisation of the detection properties
via nuclear recoils and sensitivity limits

## Slide 8: Geochronology: Measurement of 39K(n,p)39Ar cross section
Boutique neutrons advance 40Ar/39Ar geochronology D. Rutte et al. Science Advances, Vol5. No.9 (2019)
Accelerator based neutron irradiations broaden the applicability of the dating method to fine-grained materials
T1/2 (40K) = 1.25 x 109 years
Geochronological dating method for old rocks -> build up of 40Ar daughter