## Slide 1: PERLE Collaboration Meeting 11-12/01/2022
PERLE: a Powerful Energy Recovery Linac @ Orsay
Footprint & Infrastructure

## Slide 2: PERLE Collaboration Meeting 11-12/01/2022
Toward the footprint
Part 1
  List of the main components
  Associated equipment & infrastructure
Part 2
  Choice of building
Short term goals

## Slide 3: PERLE Collaboration Meeting 11-12/01/2022
Why a footprint ?
Define and find an area @ IJCLab for the PERLE facilities

## Slide 4: PERLE Collaboration Meeting 11-12/01/2022
Part 1 : The list of the components
DC = lRF/2
7 MeV
DE = 82.2 MeV
7 MeV
1 : 3 : 5
2 : 4 : 6
dump
injector
2 Linacs (Four 5-Cell 801.58 MHz SC cavities)
3 turns (164 MeV/turn)
Max. beam energy 500 MeV
Footprint: 29 m × 5.5 m × 0.9 m
DE = 82.2 MeV
Top view
29 m
5.5 m
10 m
10 m
DE = 82.2 MeV
7 MeV
7 MeV
9 m
2 : 4 : 6
1 : 3 : 5
DE = 82.2 MeV
Side view
DC = lRF/2
45 cm
IP
45 cm
Notes: puis le treillis
et les deux en même temps.

## Slide 5: PERLE Collaboration Meeting 11-12/01/2022
The list of the main components (PBS)
With the support of the expert
Notes: merci d’avance à tous les contributeurs

## Slide 6: PERLE Collaboration Meeting 11-12/01/2022
Then list “precisely” the main components
Photocathode gun
Focusing solenoids
Light box
Buncher
SRF booster
Injection line
Cryomodules
Magnets, diagnostics chambers and supports
Beam dump
Experimental site
Area around IP

## Slide 7: PERLE Collaboration Meeting 11-12/01/2022
List the equipment & infrastructure linked to the components
Power Supply
Cooling water
SF6 & Vacuum
RF supply
Cryoplant + Storage
Air conditioner
Shielding
etc…
+ Radioactive nuclear beam source
+ Equipped control room, living infrastructure, etc…

## Slide 8: PERLE Collaboration Meeting 11-12/01/2022
Surface, volume & Mass status
Financial budget estimate
Find an area
and
potentially a building

## Slide 9: PERLE Collaboration Meeting 11-12/01/2022
Choice of building
HALL SUPER ACO
IGLOO
« CHAPEAU DE GENDARME »
FREE
FREE
FREE
      Meet the needs of scientists
      Have convenient access
      Become a large accelerator platform

## Slide 10: PERLE Collaboration Meeting 11-12/01/2022
Pros :
  A lot of space
  Radioprotected area « Chapeau de gendarme »
  Proximity to Thomx and Andromede facilities
Cons :
  Old building requiring major rehabilitation work
Choice of building
FREE
FREE
FREE
ThomX
Andromede

## Slide 11: PERLE Collaboration Meeting 11-12/01/2022
Before final installation:
Assembly,
test and qualification
of the DC Gun
in the Igloo
(radioprotected and
equiped area)
(Extended scale)
ThomX
Super ACO

## Slide 12: PERLE Collaboration Meeting 11-12/01/2022
DRAFT
Work in progress :
Level one footprint
of Perle
Top view
29 m
5.5 m
10 m
10 m
DE = 82.2 MeV
7 MeV
7 MeV
9 m
2 : 4 : 6
1 : 3 : 5
DE = 82.2 MeV
ASAP :
Realistic footprint of Perle @ Super ACO
  « Chapeau de gendarme »

## Slide 13: PERLE Collaboration Meeting 11-12/01/2022
Thank you for your attention
!
Thank you in advance for your advice
!
Thank you for 3D models and drawings that can help us
!
11/01/2022