## Slide 1: CBETA: 4 Pass Energy Recovery Challenges Adam Bartnik

## Slide 2: Quick CBETA Overview
Multi-pass ERL, with single return loop
7 beams of 4 energies in 1 pipe: 42, 78, 114, 150 MeV
Uses the wide energy acceptance of Fixed Field Alternating-gradient (FFA) permanent magnets
FFA Return Loop
“R” Splitter
“S” Splitter

## Slide 3: 4 Pass Commissioning Timeline
Primary goal:
4 pass ERL operation at the commissioning current of 1 nA (FFA radiation limit)
12 weeks of operation, ending Dec. 31st 2019
Progress was not steady, often determined by problem solving

## Slide 4: Talk Organization
Expected challenges
Microphonics
BPMs for many beams
Multi-beam orbit correction
Stray fields
Dispersion/R56 correction
Laser leakage current
Machine reproducibility, degaussing
Unexpected challenges
Component failures
Magnet power supply instability
Path length adjustment
MLC slow energy drift
Beam arrival phase drift
Matching lattice optics
Microbunching instability
Problems & Solutions
What types of challenges did we face?
What types of solutions did we try?
Were we successful?
Results
example data from 4-pass operation
strikethrough = Included in extra slides

## Slide 5: BPMs for Many Beams
One of the biggest challenges is the ability to measure up to 8 different beams at a single location, and to do it reliably when there is only ~1 nA of current.
Two kinds of BPMs
“Time domain BPMs”: Position only
“RF BPMs”: Position and phase (arrival time)
= RF BPM

## Slide 6: Time domain BPMs
Bunch spacing = 23.8 ns
Round-trip time = 264 ns
8 bunches passing by BPM twice
Single bunch response
= ADC sampled points
Digitize BPM response
Single bunch response: ~3 ns
ADC rate: 2.5 ns
Original plan: Synchronize BPMs to (every other) peak
Problems:
Time-consuming to set up
Each pass has different timing
Laser hiccups cause timing to be lost (extra slides)

## Slide 7: Time domain BPMs
Solution: Asynchronous timing : Sample random part of a bunch response
Synchronous BPM ADC: (1300/31)x(76/2)/4 = 398.4 MHz
Asynchronous BPM ADC: (1300/31)x(73/2)/4 = 382.6 MHz
Synchronous
Asynchronous
Bad: Lose about a factor of 5 in signal
Good: Simple, stable, details of timing no longer matter

## Slide 8: Phase (RF) BPMs
Original plan: Two frequency mixing (f0 and 2 f0) to measure 2 simultaneous beams
Commissioning plan: Use trains of ≤8 bunches, so that passes do not overlap in time
Good: single frequency (f0) , same as injector BPMs (well understood)
Good: can use locations with more than 2 beams (e.g. linac entrance/exit)
Bad: cannot be used with long bunch trains, e.g. high current
1st pass
2nd pass

## Slide 9: Stray fields
Splitter magnet density was expected to be a significant problem
Largest expected problems: septa magnets
  Field clamps from detailed modeling, engineering
  Reduced stray field effect by factor of 40
No time for engineering, nor space for clamps around other magnets…

## Slide 10: Stray fields
Splitter magnet density was expected to be a significant problem
Use linear combinations of magnets in other lines to best cancel stray fields
“Real” : actual magnet controls
“Corrected” : stray-field corrected
“VM” : online simulation (virtual machine)
e.g. this magnet is felt in adjacent (prior) beamline. Fix automatically using other nearby magnets.

## Slide 11: Power supply instability
15V/220A Genesys power supplies had an instability above ~120 A
  Up to ±10% oscillations!
  Initially beam was moving purely from oscillating field in adjacent beamline
Two hallmarks to distinguish from other sources of jitter
  18 Hz, sinusoidal
  Does not follow trend of dispersion
Solved by adding one (or two) 3 mF capacitors in parallel with magnet
S1, R1 have roughly equal dispersion (h~1 m)
FFA has h < 0.02 m

## Slide 12: Power supply instability
Proved difficult to fully solve in one access
  Single capacitor on each power supply wasn’t enough
    Cannot directly measure residual problem field pickups / ammeter
  Difficult to notice until well after bad supply (cannot pinpoint to single magnet)
  Stray fields complicate diagnosis (possibly due to magnets in other beamlines)
Not a coincidence that new passes achieved after capacitor additions (green, above)

## Slide 13: Path length adjustment
Some bellows would not reliably change their path length
Vibrations during bellows movement sometimes cause MLC to quench
  Must turn off MLC to adjust path length, then wait for MLC to stabilize.
  Very time-consuming!
No work-around. We tried to adjust phase as few times as possible.
25 minute duration
Two bellows,
Must move synchronously to avoid damage

## Slide 14: Beam Optics Matching
Primarily in R2 (2nd pass, 2nd splitter), we had optics problems.
Could not reach design quadrupole setpoints, without losing (most of the) beam
R2: could not reach design
S4,R4: No real attempt to reach design

## Slide 15: Problems in Splitter Line R2
End of R2
Before MLC
After MLC
Orbit response: linear errors throughout R2, nonlinearity after R2
Beam appearance typically “odd” after R2
Here are some images taken during a dispersion response measurement, i.e. all images are related by relatively small R2 quad changes…
Response to kick from R2 dipole 7

## Slide 16: Peacock

## Slide 17: Sideways Bunny

## Slide 18: UFO

## Slide 19: Salvador Dali Painting

## Slide 20: R2 optics matching
It is no coincidence that we were often stuck after the second pass (red line, above)
Source of the problem remains unsolved

## Slide 21: Conclusions
Expected challenges
Microphonics
BPMs for many beams
Multi-beam orbit correction
Stray fields
Dispersion/R56 correction
Laser leakage current
Machine reproducibility, degaussing
Unexpected challenges
Component failures
Magnet power supply instability
Path length adjustment
MLC slow energy drift
Beam arrival phase drift
Matching lattice optics
Microbunching instability
Path towards higher current
Many challenges solved during 12 week operation period
Significant challenges remain for improved 4-pass ER
Check Extra Slides for details on the remaining topics
strikethrough = Included in extra slides

## Slide 22
Backup Slides

## Slide 23
Results from 4-pass operation

## Slide 24: Beam on first dump screen

## Slide 25: Transmission
10% loss
60% loss
Gradual 10% loss
Additional 60% loss after 2nd pass through R2
Percentages improve with lower initial charge (not shown)

## Slide 26: Horizontal Orbits
Note: Final 42 MeV orbit (red) has systematic error due to poor transmission

## Slide 27: Vertical orbits
Offset Vertical Position (mm)

## Slide 28: 4-pass Splitter Orbits (Horizontal)

## Slide 29: 4-pass Splitter Orbits (Vertical)

## Slide 30: MLC arrival phase
Phases are shown relative to 1st pass for pass 1-4, and offset by 180o for pass 5-8
Circles are target values from an optimized BMAD simulation
Transmission seemed to require accuracy better than 2 degrees
    Success would have been impossible without this diagnostic
Red = Before MLC
Blue = After MLC

## Slide 31: Tunes
Best fit to the MLC energy gain from this data
MLC energy gain = 36.5 MeV
Top energy = 152 MeV

## Slide 32
Other challenges / omitted slides

## Slide 33: Microphonics
MLC stability was a concern during 1-pass operation
MLC waveguide support reinforced
  Sorbothane used to absorb vibrations
Improved microphonics by a factor of 2
Note the different scale
Before
After

## Slide 34: Microphonics
MLC Operation
Before: delicate, requires an on-hand expert staff 100% of the time
After: routine, requires only occasional expert staff
Ready before operation began

## Slide 35: MLC Slow Energy Drift
MLC energy drifts ~0.5-1% over first ~30 minutes
  Begins high, drifts lower
  Drift occurs in fast, discontinuous jumps
Manual “fix” button added which finds orbit deviations in S1 along direction of dispersion, predicts energy change
  Reproducible to few kV level, but not foolproof
Origin of problem never understood, remained occasional source of confusion throughout run

## Slide 36: Laser Leakage Current
During single pass, laser “off” produced a worrisome amount of current
Leakage current ~0.3-3 nA
FFA trip threshold: ~1 nA
Added Acousto-optic modulator to further reduce leakage current
Time
EOM: fast, leaves leakage current
AOM: slow, improves leakage
Intended beam
Leakage beam
5x105:1
5x108:1

## Slide 37: Laser AOM
Laser extinction ratio improved from 500,000 to 500,000,000
Leakage current now in pA
Ready before operation began

## Slide 38: Time domain BPMs
Data is averaged in hardware in a window centered on a given pass
  BPM positions only update in currently selected pass
Operators select pass manually, or choose “auto” to have it cycle through all passes
  Can choose by BPM, by section, or in groups of sections
Timing window
Operator BPM Display Screen

## Slide 39: Phase (RF) BPMs
Original plan for beam positions / phases:
Mix with reference signal at frequency = f0 – Df
  f0 = 1.3 and 2.6 GHz (need two frequencies to disentangle two beams)
Requires solving coupled, nonlinear equations
16 adjustable parameters (cable attenuation, cable length) per BPM
Required fine-tuning of parameters
1-pass ER test was promising (extra slides), but ultimately too risky

## Slide 40: BPMs for Many Beams
Plan was in progress before operation began, but:
Major FPGA firmware upgrades on 10/22
Hardware swaps, wiring, software changes continued intermittently throughout run period (grey areas above)
Remaining issues:
5 pC, our operating charge, was near the lower measurable limit
Firmware upgraded 10/22

## Slide 41: Multi-beam orbit correction
SVD-based tools ready well before operation began
Problem: Simple methods for response matrix were unsuccessful
Simulation
  tight tolerance on tune (beam energy)
Measurement
  beam is lost in splitters during response measurement
Magnet selection, weights
BPM selection, weights
Auto/manual periodicity
Convergence criteria
Best fit unknown, but periodic, off-axis orbit
=

## Slide 42: Multi-beam orbit correction
Idea 1: Tune-based empirical
Measure experimental tunes for each energy
Create empirical response using only tunes (FFA only!)
Use SVD to hold orbit constant on last N FFA BPMs (to decouple passes)
Worked well through 3rd FFA pass (4th was already “good enough”, never tried)
Cannot adjust splitter entrance orbits from FFA
Idea for orbit correction

## Slide 43: Multi-beam orbit correction
Idea 2: Matrix refinement in closed-bump subspace
Measure 1st pass matrix with single magnets
Predict next pass closed-bump subspace
Re-measure and refine matrix in that subspace, iterate
Worked very well to correct exit FFA orbit through 4th pass
Promising to additionally correct vertical dispersion growth in FFA
Idea for orbit correction (late Jan.)

## Slide 44: Stray fields
“Linear Combinations” IOC ready by 12/12
Magnet linear combinations added to list throughout rest of run period
Remaining concerns
Combinations occasionally needed significant changes
  Depend on bellows positions? Optics changes? Energy dependent? Nonlinearity?
Confusing hysteresis, not clear how best to degauss
IOC ready for use

## Slide 45: Dispersion R56 Correction
Measured dispersion/R56 response to splitter quads
Worked well for horizontal dispersion, R56… except when it didn’t
  Discovered subtle problem in method in last week of operation
Vertical dispersion cannot be corrected using splitter quadrupoles, requires correction within FFA
  Method tested in last week of operation, seemed promising

## Slide 46: Dispersion R56 Correction
GUI ready at the beginning of the run period
Ideas for vertical dispersion correction occasionally throughout run period, successful correction only at the end of January
Dispersion, R56 GUI

## Slide 47: MLC arrival phase drift
Beam MLC arrival phase drifted many 10s of degrees
  A static beam was never seen to change
  During a shift, phase would seem to have sudden unexplained jumps.
Spent days investigating, looking for problems with BPM hardware / software
Sudden 15o change over 20 minutes

## Slide 48: MLC arrival phase drift
Discovered that the readings were real, and caused by splitter orbit changes
Manual splitter orbit changes produced up to 50o of path length adjustment!
Phases are real
Red path longer than green due to arc length

## Slide 49: Buncher failure
The buncher RF power supply (IOT), rarely a source of previous trouble, was down for significant periods of time (red areas)
Initially, we stopped operation for repairs
In the end, we re-tuned the injector in a novel way to bunch using the ICM instead
Switch to ICM bunching

## Slide 50: ICM bunching
In simulation, using the ICM to bunch leads to higher peak current and longer longitudinal tails
Not ideal, but good enough for the milestone
Baseline, with buncher
ICM bunching, no buncher

## Slide 51: Dipole power supply failure
R2 dipole 4: Power supply failed on 12/10, no spare
Power supply with similar specs found on shelf at BNL
Ready for beam in 2 days!
  Transport to CU
  Wiring
  Control system changes for analog voltage control
Power supply failure

## Slide 52: MLC Cavity SSA Failure
SSA #1 has an internal DC power supply failure, no spare
Ready for beam in 3 days!
  During the wait, retuned MLC for 5 cavity operation
Achieved 4-pass ER milestone the next day
SSA DC power supply failure

## Slide 53: Microbunching Instability?
Occasionally, we would see a charge-dependent structure on the beam profile
As early as the beginning of the second pass
Charge dependent
Single bunch effect
Optics dependent
  causing the instability or just accidentally letting us see it?

## Slide 54: Microbunching Instability?
Entrance to S2: 1.3 pC

## Slide 55: Microbunching Instability?
Entrance to S2: 1.9 pC

## Slide 56: Microbunching Instability?
Entrance to S2: 2.5 pC

## Slide 57: Microbunching Instability?
Entrance to S2: 5.0 pC

## Slide 58: Laser loses BPM timing
Laser is only locked to 1300 MHz (RF rate), not 41.94 MHz (Bunch rate)
  If laser loses lock, will come back in random 41.94 MHz “bucket”
  Occasional timing error within 23.8 ns window
  Synchronous BPM timing is ruined by this error
Laser picks random 1.3 GHz bucket

## Slide 59: Two-frequency RF BPMs
Preliminary test from 1-pass operation: Two beams on BPM before MLC
Problem: Too many coupled adjustable parameters
Here, a vertical kick produces an unphysical phase change.
Promising, but unreliable. Cannot use this method!
Two frequency BPMs with two beams
  8 adjustable scales
  8 adjustable phase offsets
  All parameters are coupled
Single frequency BPMs with single beam
  2 adjustable scales
  4 adjustable phase offsets
  Position and phase are decoupled