## Slide 1
High-flux neutron generation by laser-accelerated ions from single- and double-layer targets
Vojtěch Horný
12th May 2022
Bordeaux, France
GDR APPEL 2022
My co-authors Julien Fuchs, Sophia N. Chen, Laurent Gremillet, Xavier Davoine

## Slide 2: Application of neutrons
  A very distinctive characteristics compared to ions, electrons or x-rays, making them unique tools to investigate or modify the properties of materials.
Mor, I. et al. Reconstruction of material elemental composition using fast neutron resonance radiography. Phys. Procedia
69, 304–313 (2015).
Noguere, G. et al. Non-destructive analysis of materials by neutron resonance transmission. NIMA. 575, 476–488 (2007).
Fast neutron therapy utilizes high energy neutrons typically between 50 and 70 MeV to treat cancer.
Method: Gray, L. & Read, J. Treatment of cancer by fast neutrons. Nature 152, 53–54 (1943).
Tajima, T., Necas, A., Mourou, G., Gales, S. & Leroy, M. Spent nuclear fuel incineration by fusion-driven liquid transmutator operated in real time by laser. Fusion Sci. Technol. 77, 251–265 (2021).
Sowerby, B.D. (2007). CRP Report: Fast Neutron and Gamma-Ray Interrogation of Air Cargo Containers.
Lapinaite, A., Carlomagno, T., and Gabel F. Small-angle neutron scattering of RNA–protein complexes. RNA Spectroscopy. Humana, New York, NY, 2020. 165-188.
Moreau, J. F., et al. "The Dating of a Sixteenth Century Settlement in the Vicinity of Quebec City (Canada) by Means of Elemental Analysis of Glass Beads Through Thermal and Fast Neutron Activation Analyses." Proceedings of the 37th International Symposium on Archaeometry, 13th-16th May 2008, Siena, Italy. Springer, Berlin, Heidelberg, 2011.

## Slide 3: Contemporary neutron sources
Cikhardt, J., et al. "Neutron fluence distribution in experiments with 3 MA deuterium gas-puff z-pinch." Physics of Plasmas 27.7 (2020): 072705.
Facility | Peak neutron flux [n cm-2 s-1] | Average neutron flux [n cm-2 s-1] | Neutron bunch duration | Repetition rate
Institut Laue–Langevin (reactor) | 1015 | 1015 | continuous | continuous
Spallation Neutron source (accelerator) | 1016 | 1012 | 1 μs | 60 Hz
National Ignition Facility (fusion devoted laser) | 1026 | 1010 | 100 ps | once a day
GIT-12 (Z-pinch) | 1018 | 106 | 10 ns | once a day
Current lasers | 1018 | 106 | 1 ns | once per hour

## Slide 4: Laser-driven neutron source
 | E [J] | τ[fs] | f |  | F [N/sr] | F/E[N/sr/J] | fF [N/sr/s]
Roth, et al. PRL (2013) | 80 | 600 | once per hour | CD2+Be | 4.40×109 | 5.50×107 | 1.22×106
Kleinschmidt et al., Phys. Plasmas (2018) | 150 | 500 | once per 90 minutes | CD2+Be | 1.42×1010 | 9.47×107 | 2.63×106
Huang et al., APL (2022) – new theoretical suggestion | 282 | 1000 | once per hour | CD2+Be | 1.70×1011 | 6.03×108 | 4.72×107
Günther et al., Nat Com. (2022) | 20 | 700 | once per hour | CHO+Au | 4.93×109 | 2.47×108 | 1.37×106
Mirfayzi et al., SciRep (2020) | 300 | 1200 | once per hour | CD2+Be+H | 8×105 cold |  | 
State-of-the-art results achieved at PHELIX@GSI, TRIDENT@LANL or LFEX@ILE Osaka.

## Slide 5: Spallation
Martinez, B., et al. Numerical investigation of spallation neutrons generated from petawatt-scale laser-driven proton beams. Matter and Radiation at Extremes, 2022, 7.2: 024401.
Kelley, K. C., Gadolinium-148 and Other Spallation Production CrossSection Measurements for Accelerator Target Facilities, Dissertation, Georgia Institute of Technology, 2004.
A nuclear reaction in which the high-energy level of incident particles causes the nucleus to eject more than three particles, thus changing both its mass number and its atomic number.
cylinder
r = 50 cm

## Slide 6: Ultraintense-laser-based neutron generation
High-energy protons from single-/double-layer targets driven by 1 PW Apollon laser
E = 22 J
μm
μm (FWHM of intensity)
fs (FWHM of intensity)
nm-thick solid CH foil target, ne=200 ncr
μm-thick near-critical plasma layer + nm-thick solid CH foil target, ne=200 ncr
Apollon-class system operates once per minute - it is rather a nuclear security concern.
In fact, they are capable to run at 10 Hz.
Notes: NCD layer advantage: reduces the damage caused by prepulses.

## Slide 7: Light intensification in NCD layer
Thin lens approximation predicts optimal focusing for Apollon 1 PW laser parameters:
  ne=1.93 ncr
  D0=0.73 µm
  L = 14.1 µm
Pazzaglia, A., Fedeli, L., Formenti, A., Maffini, A., & Passoni, M. (2020). A theoretical model of laser-driven ion acceleration from near-critical double-layer targets. Communications Physics, 3(1), 1-13.

## Slide 8: Light intensification in NCD layer
2D PIC CALDER simulation of laser propagation in an uniform plasma with ne=0.74 ncr.
Initial maximum intensity is 2×1021 W/cm2.
After 25.2 µm of propagation in the NCD plasma, the laser reaches a
maximum intensity of 7.4×1021 W/cm2, within a spot size of D = 1.33 µm.

## Slide 9: Light intensification in NCD layer
Maximum intensification is around factor of three for NCD densities in range (0.60,2.11) ncr.
Optimum achieved for lower density of 0.74 ncr.

## Slide 10: Light intensification in NCD layer
Maximum intensification is around factor of three for NCD densities in range (0.60,2.11) ncr.
Optimum achieved for lower density of 0.74 ncr.
Best focusing agrees with model.
The smallest laser spot does not necessarily lead to the highest intensity.
Pazzaglia, A., Fedeli, L., Formenti, A., Maffini, A., & Passoni, M. (2020). A theoretical model of laser-driven ion acceleration from near-critical double-layer targets. Communications Physics, 3(1), 1-13.
Notes: Looses energy on the way.

## Slide 11: Ultraintense-laser-based neutron generation
High-energy protons from single-/double-layer targets driven by 1 PW Apollon laser
E = 22 J
μm
μm (FWHM of intensity)
fs (FWHM of intensity)
nm-thick solid CH foil target, ne=200 ncr
μm-thick near-critical plasma layer + nm-thick solid CH foil target, ne=200 ncr
Apollon-class system operates once per minute - it is rather a nuclear security concern.
In fact, they are capable to run at 10 Hz.
Notes: NCD layer advantage: reduces the damage caused by prepulses.

## Slide 12: PIC simulations of proton acceleration
Other parameters are the same:
Plasma: ne,SD = 200 ncr
Laser: D0 = 5 μm, a0 = 30.6, τ = 20 fs
Last column shows total number of accelerated protons or deuterons with energy above 1 MeV.
Brantov L
Notes: 6: optimum case in terms of locusing

## Slide 13: Proton acceleration with a single- and double-layer targets
Tight laser self-focusing in near-critical plasma leads to significantly faster protons but with reduced number and larger angular divergence!
Case #2
Case #6

## Slide 14: Ion acceleration with a single- and double-layer targets
NCD layer greatly enhances the final ion energy.
NCD decreases the total ion number and worsens the divergence.

## Slide 15: Ultraintense-laser-based neutron generation
High-energy protons from single-/double-layer targets driven by 1 PW Apollon laser
E = 22 J
μm
μm (FWHM of intensity)
fs (FWHM of intensity)
nm-thick solid CH foil target, ne=200 ncr
μm-thick near-critical plasma layer + nm-thick solid CH foil target, ne=200 ncr
Apollon-class system operates once per minute - it is rather a nuclear security concern.
In fact, they are capable to run at 10 Hz.
Notes: NCD layer advantage: reduces the damage caused by prepulses.

## Slide 16: Monte Carlo simulation with FLUKA
Extensions of the FLUKA code
Loading of the primary particles from CALDER produced input
  Transformation from 2D to 3D assuming the cylindrical symmetry
  Each position (x,y) and momentum (px,py) rotated by a random azimuthal angle
  Particle weight divided by the radial distance from the axis
Implementation of the routine for the tracking of the particle flux temporal profile
  Temporal profile considered both at the primary particles and all secondaries.
Simulation parameters
Always at least 3.6×108 primary particles used.
Convergence tests conducted up to 3.6×1010 primaries.
Converter is a cylinder of r = 3 cm.
Further studies on the effect of the laser accelerated electrons and generated x-rays
their contribution to the final neutron yield is negligible.
Kudos to Bertrand Martinez for his contribution to the implementation of those routines.

## Slide 17: Proton transport through Pb converter
Incident proton spectrogram #2
Monte Carlo simulation
Transported
Absorbed
Thin converters: l ≤ 250 μm (#2) or 2 mm (#6), ≤ 1% of incident energy deposited
Thick converters: l > 0.5 mm (#2) or 5 cm (#6), all incident energy deposited

## Slide 18: Neutron source features
Total neutron number emitted from the rear side of the converter (i.e. in 2π sr)
Highest neutron production already in primary double layer target and lead converter.
Only a weak dependence on the exact parameters of the front NCD layer.

## Slide 19: Neutron source features
Neutron source FWHM at the rear side of the converter
The dependence fitted by the Gaussian distribution.
For converter thicknesses higher than ~0.5 mm source size depends linearly on l.

## Slide 20: Neutron source features
The highest immediate neutron flux
Single layer proton acceleration targets in combination with thin converters can provide immediate flux above 1023 neutrons cm-2s-1.
The strong dependence on the source size surpasses the relatively low neutron number.
Notes: For such thin converters, their thickness l is lower than the proton mean free path. The protons do, in this case, experience at most one inelastic collision. On this reason, the highest peak neutron flux is
achieved for the proton acceleration configuration #2 having a thicker single-layer target and a 25 μm thick lead converter. It is a counter-intuitive result, as Figure 4a shows that this proton acceleration configuration corresponds to the generation of the lowest proton energies of all considered cases. The better performance in lead is due to its significantly higher neutron multiplicity, especially for the protons above ≳ 8 MeV.

## Slide 21: Neutron fluence and energy-angle spectra
Proton acceleration #2 + 100 μm thick Pb converter
1.04 × 108 neutrons emitted per shot
Transverse neutron source size ∼ 95 μm
Maximum immediate neutron flux ∼ 1.41 × 1023 n cm−2 s−1
Maximum integrated neutron flux ∼ 1.27 × 106 n sr−1

## Slide 22: Neutron source features
A relatively high
neutrons cm-2s-1
The most energetic neutrons are delivered within a few ps.
After 1 ns, neutrons cm-2s-1,
The less energetic neutrons continuously arrive.
A flux higher than neutrons cm-2s-1 is maintained for 240 ps in this case.
Notes: For such thin converters, their thickness l is lower than the proton mean free path. The protons do, in this case, experience at most one inelastic collision. On this reason, the highest peak neutron flux is
achieved for the proton acceleration configuration #2 having a thicker single-layer target and a 25 μm thick lead converter. It is a counter-intuitive result, as Figure 4a shows that this proton acceleration configuration corresponds to the generation of the lowest proton energies of all considered cases. The better performance in lead is due to its significantly higher neutron multiplicity, especially for the protons above ≳ 8 MeV.

## Slide 23: Neutron source features
The neutron flux at the axis: the quantity important for applications
In 1 PW regime, neutron generation is still slightly better for accelerated deuterons and a Be converter.
The strong forward directionality of the nucleons released by the deuteron break-up.

## Slide 24: Neutron fluence and energy-angle spectra
Proton acceleration #6 + 2 cm thick Pb converter
4.25 × 109 neutrons emitted per shot
Transverse neutron source size ∼ 1.74 cm
Maximum immediate neutron flux ∼ 1.27 × 1018 n cm−2 s−1
Maximum integrated neutron flux ∼ 8.40 × 107 n sr−1

## Slide 25: Comparison to state-of-the-art
 | E [J] | τ[fs] | f |  | F [N/sr] | F/E[N/sr/J] | fF [N/sr/s]
Roth, et al. PRL (2013) | 80 | 600 | once per hour | CD2+Be | 4.40×109 | 5.50×107 | 1.22×106
Kleinschmidt et al., Phys. Plasmas (2018) | 150 | 500 | once per 90 minutes | CD2+Be | 1.42×1010 | 9.47×107 | 2.63×106
Huang et al., APL (2022) – new suggestion | 282 | 1000 | once per hour | CD2+Be | 1.70×1011 | 6.03×108 | 4.72×107
Günther et al., Nat Com. (2022) | 20 | 700 | once per hour | CHO+Au | 4.93×109 | 2.47×108 | 1.37×106
#2 | 22 | 20 | once per minute | CH2+Pb | 4.24×108 | 1.93×107 | 7.07×106
#6 | 22 | 20 | once per minute | CH2+Pb | 1.21×109 | 5.50×107 | 2.01×107
#6b | 22 | 20 | once per minute | CD2+Be | 3.09×109 | 1.40×108 | 5.15×107
Commercially available PW systems could in principle operate at 10 Hz.
Number of neutrons per pulse energy is above 108 n sr-1 J-1.
We expect the highest fF of 5.15×107 n sr-1 s-1.

## Slide 26: Conclusion
Contemporary 1 PW, fs laser systems
Compact setup for high flux neutron sources.
  non-destructive sampling of matter
  investigation of the neutron damage in fusion devices
Front near critical density layer enhances the ion acceleration and the neutron yield.
1 PW power is just below the border where the spallation start to dominate over deuteron fusion → a promising scaling for 10 PW upgrade
Possible configurations should deliver:
  neutron flux above 109 n sr-1
  peak neutron flux above 1023 n cm-2s-1
  time-averaged neutron flux of 109 n sr-1s-1, with a simple thin foil as a primary target
  time-averaged neutron flux above 107 n sr-1s-1 is foreseen using double-layer targets with deuterated solid layer
Dr Vojtěch Horný vojtech.horny@polytechnique.edu https://ft.nephy.chalmers.se/~vojtech
Advertisement
Horný, V., & Veisz, L. (2021). Generation of single attosecond relativistic electron bunch from intense laser interaction with a nanosphere. Plasma Physics and Controlled Fusion, 63(12), 125025.
Horný, V., Krůs, M., Yan, W., & Fülöp, T. (2020). Attosecond betatron radiation pulse train. Scientific Reports, 10(1), 1-8.
Chen, Q., Mašlárová, D., Wang, J., Li, S. X., Horný, V. & Umstadter D. (2022). Transient relativistic plasma grating to tailor high-power laser fields, wakefield plasma waves, and electron injection. Physical Review Letters, 128, 164801.

## Slide 27: Be(d,n) reactions vs. spallation
Roth, M, Schollmeier, M, Ion Acceleration—Target Normal Sheath Acceleration, e Proceedings of the CAS-CERN Accelerator School: Plasma Wake Acceleration, Geneva, Switzerland, 23–29 November 2014
Roth, M., et al. Bright laser-driven neutron source based on the relativistic transparency of solids. Physical review letters, 2013, 110.4: 044802.
TNSA accelerated deutrons

## Slide 28: Laser energy conversion to particles
Optimum near-critical plasma (NCP) can absorb over 40% of laser energy
Fast electrons from NCP enhance proton acceleration from solid foil
10 − 12 % laser energy conversion into protons
#2
#6