## Slide 1: Design and performance challenges of the future high energy colliders
B. Dalena (CEA, Irfu, DACM, Paris-Saclay University)
With contributions from: C. Antoine, P. Bosland, P. Bredy, V. Calvelli, A. Chance, E. Cenni, T. Lecrevisse, C. Lorin, C. Marchand, D. Minenna, L. Quettier, E. Rochepault, D. Uriot and all DACM teams!

## Slide 2: Outline
Future Colliders projects
Design and performance optimization
High Field Magnets (HFM) R&D
Super Conductive Cavities (SRF) R&D

## Slide 3: Future HEP Accelerators
FCC-hh
FCC-he
FCC-ee
HL-LHC
LHeC
CLIC
HE-LHC
HE-eLHC
CepC
SppC
ILC
superKEKB
JPARC MR
PIP I
PIP II
RHIC EIC
BEPCII
C3
Muon Collider
Muon Collider
CEA-DACM is presently implicated in the HL-LHC, EIC, ILC, FCC and Muons Colliders projects

## Slide 4: Design and performance optimization
1

## Slide 5: Arcs design and performance (FCC-ee Booster)
*N-times
Magnets min gradient and Field Quality
Civil engineer constraints
Integration of the Booster and the collider in the same tunnel
Pre-injectors input parameters
& Booster cycle
On momentum and off momentum particles stability
Collective effects: mitigate the impact of impedance and IBS optimizing the optics of the arc cells
FODO cell not optimum
alternative under study

## Slide 6: Rapid Cycling Synchrotrons (RCS) design (Muons)
*N-times
Muons decay very fast (Rest lifetime: 2.2 µs)
Accelerate fast (~10 ms)
norm. cond. RCS
hybrid RCS 1.5 TeV
hybrid RCS
Both in the same tunnel
hybrid RCS 5 TeV
Find the best ratio extraction/injection ratio between the different acceleration stages.
Optimize the total voltage and energy gain per turn
Fit existing tunnels
Optimize the dipole ramp to minimize the power consumption
Chain of rapid cycling synchrotrons, counter-rotating µ+/µ- beams  63 GeV  0.31 TeV  0.75 TeV  1.5 TeV ( 5 TeV)
Objectives:
  Beamline in a parameter table
  Full set of lattices with critical technologies identified
  Start-2-end tracking to demonstrate luminosity performance and to validate the bunch compression and emittance preservation during the acceleration process
Courtesy of A. Chance

## Slide 7: Laser wakefield accelerator design
01
Design of accelerators
Setting component parameters
02
LASER-plasma Simulation
Multi-parameters (laser + plasma profiles)
Cross-checking
06
optimisatioN of accelerators
Numerical optimisation (Machine learning)
03
Transfer Line design
Development of the TraceWin code
EARLI project
Design of a laser wakefield accelerator for electron injection
  Transition toward user facilities
  First step: numerical design, prototypes and viability studies
For the AWAKE collaboration
  As an alternative design for AWAKE
  Comparison with a CERN electron gun will be made
Courtesy of D. Minenna

## Slide 8: Optics Corrections strategy (FCC-ee Booster case)
errors | Case | Plane | 3 x Analytical RMS | 3 x Mean RMS/seeds
MQ offset = 150 µm MB field err = MB roll = 300 µmrad BPM offset = 150 µm MS offset = 150 µm BPM resolution = 50 µm | Residual orbit [m] | x | 188 | 
 |  | y |  | 
 | Correctors strengths [mTm] | x |  | 
 |  | y |  | 
errors | Case | Plane | 3 x Analytical RMS | 3 x Mean RMS/seeds
 | Residual orbit [m] | x | 188 | 
 |  | y |  | 
 | Correctors strengths [mTm] | x |  | 
 |  | y |  | 
Evaluate specifications of the main magnets misalignment of the High Energy Booster arcs cells and of magnets field error
Definition of the orbit correction strategy and of correctors specifications for the booster
Improvements and related work:
Other methods than SVD - AI ?
Full emittance tuning
Study the impact of booster support vibrations on emittance
Study the impact of energy ramp during the booster cycle
offset
roll
Motivation
Orbit correction

## Slide 9: Improve modeling of non-linear magnetic field in tracking simulations
Accurate and efficient modeling of the magnet field extremities required to see their effects on the beam
In the High Luminosity IRs the variation of the beta function along a single magnet is not small, the longitudinal distribution of field errors may impact beam based quantities
Aim: understanding and correction of non-linear effects on the beams
T. Pugnat PhD thesis
Courtesy of S. Bagnis

## Slide 10: Prediction of Phase-Space Stable Region for Hadron Storage Rings (HL-LHC case)
?
Replace CPU costly tracking simulations with fast surrogate model of the time evolution of Dynamic Aperture
Deep Echo State Networks (DeepESN)
M. Casanova et al.
https://doi.org/10.1140/epjp/s13360-023-04167-y

## Slide 11: High Field Magnets (HFM) R&D
2

## Slide 12: Expertise and infrastructures
Magnetic calculations
Conductor design
Magnets Mechanics
Magnets Cryogenics
Quench analysis and magnet protection
Magnet safety and magnet control systems (DIS)
Industrial follow-up
Courtesy of L. Quettier
DIS

## Slide 13: Development plan toward 16 T Nb3Sn Dipoles
16 T
demo
12-14 T demo
Subscales
Powered samples
Non-powered samples
F2D2
D5
SMC
D3
FD
D5
R2D2
D4
Courtesy of E. Rochepault
2025-2026
On-going
2026-2027
Racetrack Dipoles

## Slide 14: Development of Nb3Sn magnets towards 16 T
« Non-powered samples »  Characterizations of materials, development of processes, validation of concepts
« Powered samples »  Study of performances of Nb3Sn
Model coil SMC : successful test!  Development of fabrication processes, infrastructure, gain of experience
R2D2 12T: CEA conceptual design validated by an external committee
Characterization of conductors during heat treatment at 650°C  PhD M. Abdel Hafiz
R2D2 = Research Racetrack Dipole Demonstrator

## Slide 15: Development Plan towards 20 T HTS Dipoles
Phase 1 2023-2025:
Racetrack MI
Phase 2 :
magnet MI 16 T+
« EuCARD V2 »
Phase 3 :
« EuCARD V3 »
MI cold bore 16 T+
magnet
On-going Project
Adapt and validate the numerical tools for electromagnetic + thermal + quench models
Characterize specific parameters of Metal Insulated windings (Turn-to-turn thermal conduction…)
Develop the technologies from winding to assembly including electrical connections
Evaluate the options of conduction cooled dipole
Fabricate and test one racetrack coil for models benchmark
Courtesy of T. Lécrevisse

## Slide 16: HTS solenoids R&D
High Field MI magnet (NOUGAT)
NOUGAT pancake (MI)
NOUGAT magnet
2018 tests at LNCMI
Long-lasting R&D on HTS solenoid @DACM
(example: NOUGAT magnet)
Use «Metal-insulated (MI)» winding:
Concepts:
  20 T @ 4.2K
  Or 16 T @ 20 K  opportunity to lower exploitation costs or simplify cryogenics
 The Muon collider project fit the on-going R&D of Irfu
Courtesy of L. Quettier, P. Fazilleau
Target capture solenoid: 20 T with 150 mm aperture
Final cooling solenoids: 40 T with 50 mm aperture

## Slide 17: Super conductive cavities (SRF) R&D
3

## Slide 18: SUPER CONDUCTIVE CAVITY: SURFACE PREPARATION
Vertical electropolishing cabinet
  Buffer Chemical Polishing
  HF,HNO3,H3PO4: 1/1/2.4
  200 l tank
Integrated chemistry cabinets (BCP)
  HF,H2SO4
  300 l tank
2 systems for production of
18 MW ultrapure water for the chemical treatments and for the 2 clean rooms

## Slide 19: CLEAN ROOMs
ISO 7
28 m2
6.0 m
ISO 5
38 m2
7.8 m
ISO4
112 m²
15.6 m
HPR rinsing in ISO4 clean room
Washing machine
ESS
ISO4: XFEL, ESS cryomodule assembly ISO5/7 R&D, IFMIF, SARAF
HPR rinsing in ISO5 clean room
COBOT in clean room

## Slide 20: Supratech Cryo-HF : infrastructures
The Helium cryogenic system is going to be upgraded for PIP-II (40 K He for thermal shield, supercritical He for cryomodule supply, fast cool down step , increase of LHe production and of 2K He pumping unit)
Two vertical cryostats: Test single and multicell cavities with high frequency (175MHz, 704MHz and 1.3 GHz)
One horizontal cryostat: Enable a complete cavity package test (cavity+tuner+fundamental power coupler)
Two 704 MHz High power klystrons: high power cryomodule test and fundamental power coupler conditioning
One bunker for testing complete cryomodule under HF power and cryogenic conditions
Courtesy of P. Bosland, E. Cenni, P. Bredy
Helium Cryogenic plant

## Slide 21: SRF R&D: Thin films (multilayers concept)
  High Quality factor for colliders (ILC, FCC, …and EVERY other types of accelerators!!!)
    => possibility of operation at 4.5 K or even higher (instead of 2k)
    => investment (~35-40%) and operation cost ( ~60% ) savings in cryogenic installations
    => lower plug power (greener operation)
    => opens the way to new cooling processes (He issues)
Future : totally functionalized material, each layer its own role (thermal conductivity, high superconducting performance, multipacting mitigation….)
  High accelerating gradients for colliders (ILC… and compact small machines for medical/industrial applications)
    => investment savings in building, superconducting material, RF installations….
Courtesy of A. Claire
Expected
Measured

## Slide 22: Implication in FCC
CEA has a long experience in SRF technology and can contribute to FCC:
Cavity preparation recipe and industrialization R&D
Cryomodule assembly
Clean room robotization development
Booster
MACSE
SOLEIL
TTF, SLS
SPIRAL2XFEL
IFMIF LIPAc
ESS, SARAF
PIP-II
DONES
Others
Future
FCC ?
Courtesy of P. Bosland

## Slide 23: Implication in Muon Colliders
Courtesy of C. Marchand
RF cavities for muon cooling cells
Normal conducting cavities
Short RF pulses (~𝜇𝑠)
High acceleration gradients (~30 MV/m)
High magnetic solenoidal field (up to 14 T)
Objective:
  find best cavities & RF properties to minimize breakdown due to High Gradient in high magnetic field
Methodology:
  1/scaling using no-diffusion beamlet model (done)
  2/develop semi-analytical model based on simulations of the electron beam in the cavity (like done in US beamlet approach Palmer et.al PRAB 2009, Stratakis et.al NIMPR 2010, Bowring et.al PRAB 2020)
  3/adjust coefficients of semi-analytical model on existing and new experimental data foreseen in RF test stands
  4/test new ideas (cavity length, couplers,..)
Benefits of short pulse and aluminum multiply

## Slide 24: Conclusions
We are participating in international collaborations to design future HEP Collider projects
We are pursuing R&D on high field magnets, SRF cavities and cryomodules, beam dynamics modeling, and laser-plasma acceleration that can meet some of the challenges of several future collider projects
We continue to upgrade the infrastructures to test, develop and assemble key technological systems for several future colliders
 We are looking forward the next future collider

## Slide 25: Back-up
3

## Slide 26: Arcs design and performance (FCC-hh Collider)
Half arcs cell including
linear and non-linear correctors
*N-times
Civil engineer constraints
Magnets max gradient and Field Quality
Beam-screen design
Integrations of experimental IRs (correction schemes)
Collimation requirements
Beam-stability:
Integration of Landau Damping octupoles
213/2 m

## Slide 27: MARCO Solenoid
Parameter | Parameter Value | Units
Bore diameter | 2.84 | m
Coil Rin | 1.501 | m
Coil thickness | 32.7 | mm
Coil Length | 3492 | m
Nominal Current | 3924 | A
Turns | 1668 | 
Layers | 6 | 
Modules | 3 | 
B0 | 2.00 | T
Bpeak+self field | 2.67 | T
Stored Energy | 45.3 | MJ
Projectivity | 2.41 | Tmm²/A
Homogeneity | 12.3 | %
Transparency Thickness/nuclear interaction length | 0.468 | 
2T Solenoid for the EIC ePIC detector @ BNL
Copper stabilized RIC NbTi conductor (Iseult inspiration)
Inner wounded on a brass mandrel
32.7 mm
30 mm
STATUS
90% design forecast in October (DOI CD2/3A November 2023)
Conductor R&D started in 05/2023
tender  forecast in 2024
Coil cross-section & materials
MARCO Solenoid
MARCO Conductor

## Slide 28: What is a good thin film superconductor ?
  A compromise between:
    High superconducting/RF performance (High Tc, High superheating field)
    Easy fabrication process,
      ≡ high reproducibility at “industrial scale”
      Easy process to go from 1-cell to multi-cells or complex shapes
      Easy process to adapt to various frequencies
    Tunability
      Beware of brittle materials !
    Low sensitivity to trapped flux upon cooling down
      Few crystalline defects or a structure not too sensitive to them (e.g. SIS)
  Thin films on copper are the only route to help cost savings
    Cheaper manufacturing
    Higher operation temperature
    Higher gradients : lower capital costs
Courtesy of A. Claire