## Slide 1: La source X Compton Inverse de l’accélérateur ELSA du CEA
Abel PIRES (CEA DAM, LMCE)
Annaig CHALEIL (CEA DAM) - Anne-Sophie CHAUCHAT (CEA DAM) - Vincent LE FLANCHEC (CEA DAM, LMCE)
Nicolas DELERUE (IJCLab, CNRS)
Les 100 ans de l’effet Compton : des sources aux applications

## Slide 2: Plan de la présentation
Introduction
Inverse Compton Scattering X-ray Sources
ELSA Accelerator
The Inverse Compton X-ray Source at ELSA
Strategy for Source Optimization
Conclusion

## Slide 3: Introduction
1

## Slide 4: Introduction
History
  1922: Arthur Holly Compton conducts an experiment demonstrating that electrons and photons are particles.
Scattered photon
Incident photon
Ex
Ep
Ee
Electron
at rest
Scattered Electron
  Study of the collision between X-ray photons and electrons at rest
  Observation: decrease in photon energy after the collision (increase in wavelength)
  Note : elastic scattering, kinetic energy is conserved
θ
Ep
φ
Ex
Ee
  K-line of molybdenum
  = 17,5 keV
  = 17 keV
  = 0,5 keV
= 82°

## Slide 5: Introduction
Compton Scattering and Inverse Compton Scattering
Compton Scattering
  Transfer of energy from the photon to the electron
α
θ1
Back-scattered Photon
Incident Laser Photon
Relativistic Electron
Ex
Ep
Ee
θ2
θ1/2
θ
Incident Photon
Ep
φ
Electron
At rest
Scattered Photon
Ex
Ee
Scattered
Electron
Inverse Compton Scattering
  Transfer of energy from the electron to the photon

## Slide 6: Introduction
Compton Scattering and Inverse Compton Scattering
Compton Scattering
  Transfer of energy from the photon to the electron
α
θ1
Back-scattered Photon
Incident Laser Photon
Relativistic Electron
Ex
Ep
Ee
θ2
θ1/2
θ
Incident Photon
Ep
φ
Electron
At rest
Scattered Photon
Ex
Ee
Scattered
Electron
Inverse Compton Scattering
  Transfer of energy from the electron to the photon
  Ex: K-line of molybdenum: scattering angle = 82°
  Ex: laser 532 nm + relativistic electron
  photon
  ( )
  = 17,5 keV
  = 17 keV
  = 0,5 keV
( )
  27,6 mrad

## Slide 7: Introduction
Thomson Scattering and Inverse Compton Scattering
θ1
Back-scattered Photon
Incident Laser Photon
Relativistic electron
Ex
Ep
Ee
θ1/2
Inverse Compton Scattering
Thomson Scattering
Incident Photon
Ep
Electron
At rest
Scattered Photon
Ex
Dipole Radiation
  IN THE REFERENCE FRAME OF THE ELECTRON
  IN THE LABORATORY REFERENCE FRAME
  The change of reference frame induces a relativistic Doppler effect that depends on the angle.
  The radiation is concentrated in a cone emitted forward in the laboratory reference frame.
  Incident photon energy small compared to electron rest mass Ep <<
  Negligible transfer of energy, but photon scattered with an angle
  Transfer of energy from the electron to the photon

## Slide 8: Inverse Compton Scattering X-ray Sources
2

## Slide 9: Inverse Compton Scattering X-ray Sources
  Monochromatic and directional radiation sources with high temporal resolution
  Compact sources for imaging or diagnostic characterization
  eg., ELSA
  532 nm laser ( + relativistic electrons (
  X-ray photons
  eg., THOMX
  1030 nm laser ( + relativistic electrons (
  X-ray photons
  Very high-energy X-ray sources for high-energy physics
      eg., Laser Electron Photon beamline at SPring-8 (LEPS)
  351 nm laser ( + relativistic electrons (
  X-ray photons

## Slide 10: Inverse Compton X-ray Sources
Spécificité, Applications et Exemples
Storage Ring-Based Inverse Compton X-ray Sources
Cavity Design, Beamline Development and X-ray Applications
Author: Benedikt Sebastian Günther
https://doi.org/10.1007/978-3-031-17742-2

## Slide 11: Inverse Compton X-ray Sources
Comparisons of different sources
Synchrotron
FEL
  Very high energies accessible to Compton sources
  Significant flux considering compactness
Storage Ring-Based Inverse Compton X-ray Sources
Cavity Design, Beamline Development and X-ray Applications
Authors: Benedikt Sebastian Günther
https://doi.org/10.1007/978-3-031-17742-2
  Objective

## Slide 12: ELSA Accelerator
3

## Slide 13: ELSA Accelerator
3D view
Photo-injector
144 MHz
Ee= 2 MeV
1,3 GHz RF cavity Ee= 30 MeV
Compton interaction region + SMILE
Bremsstrahlung Line
433 MHz RF cavities
Ee= 17 MeV
Double alpha compressor

## Slide 14: The Inverse Compton X-ray Source at ELSA
4

## Slide 15: The Inverse Compton X-ray Source at ELSA
First Experimental results in 2011
Étude de la production de rayonnement X par diffusion Compton sur l’installation ELSA
Author : Anne-Sophie Chauchat
https://theses.hal.science/tel-00652588
Half-angle of radiation cone | 10 mrad | 24 mrad
Number of photons per micro-pulse | 120 | 300
Peak photon flux photons/s | 4,5.1012 | 1.1013
Average photon flux photons/s | 1,2.104 | 3.104
Peak surface photon flux photons/s/cm² | 1,5.1012 | 7.1011

## Slide 16: The Inverse Compton X-ray Source at ELSA
Top view of the interaction point

## Slide 17: The Inverse Compton X-ray Source at ELSA
3D view of the interaction point and SMILE device
Electron
beam
Laser
beam
X-ray
beam
Electron
beam
Laser
beam
X-ray
beam
Schematic of SMILE
1m
32 mm
SMILE :
Système
Multi-passage
pour
Interaction
Laser
Electron
7 mirrors of the SMILE
8 mirrors of the SMILE
View of the laser impacting the mirrors surfaces
Développement d’une source de rayonnement X par diffusion Compton inverse sur l'accélérateur ELSA et optimisation à l'aide d'un système d'empilement de Photons
Author : Annaïg Chaleil
https://hal.science/tel-01435076/

## Slide 18: The Inverse Compton X-ray Source at ELSA
Experimental results in 2016
  With 17,7 MeV and 30 MeV electrons
Chart: Acquisition of time-resolved electrical signals from X-ray diagnostic (PM)
RSB ~2
RSB ~11,2
SMILE OFF
30 MeV
SMILE ON
signal
Compton signal,
SMILE ON
Background signal
Compton signal,
SMILE OFF
Background signal
(without laser)
17,7 MeV
SMILE activation
Développement d’une source de rayonnement X par diffusion Compton
inverse sur l'accélérateur ELSA et optimisation à l'aide d'un système
d'empilement de Photons
Author : Annaïg Chaleil
https://hal.science/tel-01435076/
SMILE activation → yield increases by a factor 8 !

## Slide 19: Strategy for Source Optimization
5

## Slide 20: Strategy for Source Optimization
Sujet de thèse : Optimisation interaction Compton
Laser Induced Damage Threshold (LIDT)
Non-linear effects
Beams alignment difficulties
Mechanical stability
Re-design the interaction area
(SMILE 2)
Temporal stretching by CPA
(Chirped Pulse Amplification)
Electron beam transport optimization
Space charge effects
Pitfalls :
Nd:YAG at 1.064µm, bandwith: 250pm
SMILE 2 : motorization
Twiss parameters and charge
that maximise X-ray yield
After one alpha magnet
At the entrance of the alpha magnet
q = 0,1 nC
q = 1 nC
q = 0,1 nC
q = 1 nC
Increase laser photon number
Increase electron number
Improve alignment

## Slide 21: Strategy for Source Optimization
Sujet de thèse : Optimisation interaction Compton
Re-design the interaction area (SMILE 2)
Beams alignment
Mechanical stability
Pitfalls :
SMILE 2 : motorization with piezo actuator

## Slide 22: Strategy for Source Optimization
Sujet de thèse : Optimisation interaction Compton
Laser Induced Damage Threshold (LIDT)
Non-linear effects
Temporal stretching by CPA
(Chirped Pulse Amplification)
Pitfalls :
Nd:YAG at 1.064µm, bandwith: 250pm
22
Laser oscillator
1064.5nm
Output :
30ps
compressed
high intensity
500ps
stretched
chirped
Input :
30ps
bandwidth 30pm
low intensity
spectral broadening
in fiber
via SPM
bandwidth 250pm
circulator
Chirped Fiber
Bragg Grating
amplifiers
amplified
two gratings
compressor
decrease peak power during amplification
avoid laser damage
reduces non linear effects
reach higher intensity after compression

## Slide 23: Strategy for Source Optimization
Sujet de thèse : Optimisation interaction Compton
      Space charge effects
After one alpha magnet
Phase Space
at the entrance of the
alpha magnet
q = 0,1 nC
q = 1 nC
q = 0,1 nC
q = 1 nC
Pitfalls :
Electron beam transport optimization :
Twiss parameters and charge
that maximise X-ray yield

## Slide 24: Conclusion
6

## Slide 25
MERCI DE VOTRE ATTENTION