## Slide 1: Microrheology and structural quantification of blood clots as a diagnosis of hypercoagulability
Nathalie Westbrook, Julien Moreau
Biophotonics group, Lab. Charles Fabry
in collaboration with
Jean-Marc Allain, Adrien Seripa, Lab. Mécanique des Solides, Ecole Polytechnique, IPP
Chloé James, Laura Wolff-Trombini, Univ. Bordeaux, INSERM, Biology of cardiovascular diseases & CHU Bordeaux Lab. Hématologie
Hubert Galinat, CHU Brest, Service Hématologie Biologique
L. Wolff-Trombini et al, accepted in Biomedical Optics Express (30 june 2023)
150 ans SFP, 5 july 2023

## Slide 2: Hypercoagulability and thrombosis
Clot formed in a blood vessel
2 types of thrombosis :
  Arterial (major)
  Venous
Complications : recurrence and pulmonary embolism
In France : 50 000 to 100 000 phlebitis, 40 000 P. Emb / year
Thromboembolic events: 3rd cause of cardiovascular deaths
Problem : 50% of recurrent deep venous thrombosis events remain unexplained
What is thrombosis?
Berthomier, T. and al. Adv. Sci. Technol. Eng. Syst. J. 2, 48–59 (2017).

## Slide 3: Blood clot and coagulation
Physiological hemostasis and its regulation
 Maintaining blood flow and healing vascular breaches
We start from poor platelet plasma (PPP) = no red or white blood cells nor platelets but with coagulation factors (non activated proteins)
We initiate coagulation by adding tissue factor, calcium and phospholipids + microbeads for our optical microrheology
Primary hemostasis: agregation of platelets in the breach
Secondary hemostasis: formation of fibrin based on coagulation factors (factors I to XII)

## Slide 4: Passive microrheology
Microbeads are incorporated in the blood clot and their brownian motion under thermal fluctuations is measured using an optical tweezer setup when the reflection of a laser beam focused on the bead gives access very precisely to the position of the bead.
Measurement of brownian motion
Blood clot with 6 µm polystyrene beads
Interference pattern used to center the bead on the laser focus
Image used to position the bead on the laser focus
Beads trapped by the clot not by the laser
=> Need to center the bead on the laser focus

## Slide 5: Extraction of viscoelastic ppties
Same shape for all the curves => characterization with one measurement = storage modulus at 30 rad/s
Brownian motion recorded with high spatial and temporal resolution (0.1 to 10kHz)
=> Local viscoelastic properties of the blood clot as a function of frequency
Storage modulus at 30 rad/s

## Slide 6: Measurement protocol
Choice of microrheology parameters to define a reference measurement on normal clots
Choice of bead diameter: 6 µm
=> less dispersion in the measurement
Choice of bead height
(distance to coverslip): 40 to 60µm
=> less variation with height
@30Hz
Storage modulus @100Hz

## Slide 7: Confocal imaging of fibrin
Correlation of mechanical measurements with confocal images of fibrin network (fibrinogen labeled with Alexa488)
Confocal image of a fibrin network.
Control from a human pool. FVIII=100%
Scale bar 25µm. Zoom on an area with a bead (scale bar 10µm).
Quantification of confocal images:
fiber density and length
Example of confocal image of a looser fibrin network
Hemophilic patient
FVIII=1,1%

## Slide 8: Characterization of induced hypercoagulability
Blood clots supplemented at 400% with one specific coagulation factor (Factor VIII) are more rigid than control clots
1 point=1 clot (4 beads)
Blood clots with 10% more fibrinogen are more rigid than control clots
Microrheology measurements
structural imaging

## Slide 9: Perspectives
→ Characterize blood clots from patients with coagulation pathology (thrombotic or hemophilic)
Blood clot containing microbeads
DIODE LASER
Brownian motion detection
→ Compact and automatized prototype transportable to the hospital