## Slide 1: Inverse Compton Scattering 𝛾 source for nuclear photonics applications

## Slide 2: Energy-angle relation
Compton photon:
laser (Eλ=hc/𝜆=1.2eV)
α
θ
e- beam
Klein O. and Nishina Y., Z. Phys. 52(1929) 853; Ginzburg I. et al., Nucl. Instr. Methods in Phys. Research 219 (1984) 5, V. B. Berestetskii, E. M. Lifshitz, L. P. Pitaevskii (1982). Quantum Electrodynamics. Vol. 4 (2nd ed.)
Compton x-section
~0.66b (Ee<1GeV)

## Slide 3: Energy-angle relation
Compton photon:
laser (Eλ=hc/𝜆=1.2eV)
α
θ
e- beam
Compton x-section
~0.66b (Ee<1GeV)
Advantage:
Quasi monochromaticity obtained by use of collimator
Price to pay  Flux reduction

## Slide 4: Gamma-ray applications
Photo-nuclear reactions:
Nuclear Resonance Fluorescence (NRF)
Fine splitting of Pygmee DR
Giant Dipole Resonance (DR)
NRF:
Narrow bandwidth (<1%) required
Backgrounds
Linearly polarized beams are of interest
few MeV at most
8MeV
S. Galès, PoS (INPC2016) 355, R. Hajima et al., Eur. Phys. J. Special Topics 223, 1229–1236 (2014)

## Slide 5: QED opportunity ?
J.K. Koga and T. Hayakawa, PRL 118, 204801 (2017)
Existing measurements:
Few % precision with very large O(1) pollution from Rayleigh, Thomson + nuclear resonances tails
Exploit polarization:
Only Delbrück contributes to some restricted angular range when p-polarisation is considered  1% precision in 2days with PERLE ?
Some caveats:
- Some strong assumptions on resonance modelling
- only lowest order Delbrück scattering

## Slide 6: Some key parameters
Photon rate
Laser-beam single pulse energy
Electron beam intensity
RMS average of transverse beam sizes
Geometrical overlap form factor (Piwinski contribution typically)
effective beam-crossing rate

## Slide 7: Some key parameters
Photon rate
Laser-beam single pulse energy
Electron beam intensity
RMS average of transverse beam sizes
Geometrical overlap form factor (Piwinski contribution typically)
effective beam-crossing rate
Spectral purity
Collimator opening
Beam emittance
Energy spread
Laser bandwidth
Diffraction spread
Strong field electron rest mass shift
On-axis harmonics
Usually limiting contribution

## Slide 8: Combined figure of merit
Photon rate
Spectral purity
Collimator opening
Beam emittance
Energy spread
Laser bandwidth
Diffraction spread
Strong field electron rest mass shift
On-axis harmonics
Usually limiting contribution
Spectral density

## Slide 9: PERLE implementation
Gamma beam:
Opening angle ~ 2mrad
Detector:
Calorimetry
High-res calorimetry ? (HPGe)
Delbrück, ideally 4pi calorimetry, may be simplified to fit in available space
Cost ~ 500kE of hardware

## Slide 10: PERLE: Fast simulation
With 1MW 40MHz laser :
40 (20)x106 photons/(s.eV) within <0.8 (0.5)% BW
NB: ELI-NP 4 x104 photons/(s.eV) for 0.5% BW
A. Martens et al., Phys. Rev. Accel. Beams 24, 091601
Low (0.1%) bandwidth:
Never demonstrated
Of interest for NRF applications (background)
@PERLE depending of charge vs momentum space spread trade-off.
 Approximate relation for Q(ϵ,𝜎E) needed.

## Slide 11: Conclusion: PERLE could be…
A high rate low energy gamma-ray source at 1.1MeV:
~>100x ELI-NP
more at 500MeV e-beam energies, or with halved wavelength laser
A very nice driver for R&D on optical cavities :
Very high average laser power in green (new AFAIK)
A place to demonstrate <0.1% bandwidth gamma source:
NRF backgrounds…
A place to perform QED physics…
Background free Delbrück scattering measurement in few days
but also more conventional NRF research

## Slide 12: Backup

## Slide 13: Typical elements and performance
Amoudry L. & H. Wang, PhD theses; Amoudry L. et al., Applied Optics 59(2020)116
Cost ~ 500kE of hardware

## Slide 14: Laser phase noise
T=1/frep=2p/wr
T. Udem et al. Nature 416 (2002) 233
2Dfce

## Slide 15: Ultra narrow linewidth
The whole comb must be locked:
dilatation (FREP)
translation (FCEO)
NB: Compare with central frequency of
Filtering lines of the optical cavity
Laser spectrum
Not locked
locked
Metrology-level requirement !
Unique laser provider ?

## Slide 16: Fabry-Perot resonator
Trep=1/Frep
Input laser beam must be matched to the cavity:
Temporal superposition
Transverse mode matching
Resonant at different cavity lengths*
*for a non-degenerate cavity
Input laser beam:
Few ps pulse duration
L
2L/c=Frep

## Slide 17: Fabry-Perot interferometric filter
Laser frequency must be precisely tuned
And remain stable !
NB: Compare with central frequency of
Metrology-level requirement !
unique provider but stopped production !!!