## Slide 1
PERLE Status and Plans
Orsay, October 27th 2022
Walid KAABI

## Slide 2: The short story of the PERLE Genesis
Future particle physics imposes strong challenges on accelerators and requires a variety of accelerator R&D programs not only to meet the foreseen performances, but also to lower their energetic consumption and enhance their efficiency.
   Energy Recovery Linacs offer one of the main options for energy frontier colliders
To probe deep inelastic scattering at high energy and to study the Higgs boson, LHeC proposes a high luminosity collider using the HL-LHC protons and an intense electron beam.
For the electron beam, the ERL scenario has many advantages :
  High luminosity, low interference for installation next to LHC, machine size, energy consumption
  Concept also applied to the FCC-eh design
The ERL-ring collider concept of LHeC based on
  synchronous operation of HL-LHC and 50 GeV electron beams
  circumference of e- loop about 1/5 of that of LHC (5.3 km)
  luminosity of 1034 cm-2.s-1
  Multi-turn ERL (3+3 passes), 50 GeV, RF frequency: 801 MHz,
  20 mA beam current (6 x 20 = 120mA load in the cavities).

## Slide 3: The short story of the PERLE Genesis
PERLE: A testbed to explore and validate a broad range of accelerator phenomena & technical choices on the pathway to the LHeC and other new frontier machines realisation.
Main challenges: Multi-turn, high bunch charge, high power energy recovery, …
2 Linacs (Four 5-Cell 801.58 MHz SC cavities)
3 turns (164 MeV/turn)
Max. beam energy 500 MeV
I = 20mA
Target Parameter | Unit | Value
Injection energy | MeV | 7
Electron beam energy | MeV | 500
Normalised Emittance γεx,y | mm mrad | 6
Average beam current | mA | 20
Bunch charge | pC | 500
Bunch length | mm | 3
Bunch spacing | ns | 25
RF frequency | MHz | 801.58
Duty factor |  | CW

## Slide 4: ERL History and achievements
2020, Cornell/BNL
cbeta, FFA-arc
4-pass ERL
(80mA injector, e = 0.3mm mrad)
2002
Jefferson Lab
“IR-Demo”
SRF, 5mA, 48MeV,
2.1kW beam power IR
2003
CEBAF, 1 GeV, single turn
2007 Upgrade:
9mA, 150MeV
1.1MW beam power with ~300kW total power
1965 M. Tigner
“A possible apparatus for electron clashing-beam experiments”
1987 High Energy Physics Lab
Stanford University
SRF cavities, proof of principal experiment
2000
Jefferson Lab
“Front End Test”
SRF, first CW
recovery
1987 Los Alamos
FEL-operation, nc,
coupled acc/dec cavities
2004 BINP, Russia
FEL-operation
normal conducting RF,
30 mA
2007: 4-passes
2002 JEARI, Japan
FEL, SRF, 700kW beam power
2005 Daresbury Lab, GB
“Alice”, SRF, 26MeV, versatile
10-year user program
under construction:
MESA, Germany
particle physics application
PERLE, France
Technology test facility (LHeC/FCC-eh) + eRIB test facility
bERLinPro, Germany
SRF/ERL technology test facility
CeC, BNL, USA
Coherent electron cooling for EIC
2013 KEK, Japan
“cERL”, prototype
ERL light source
Industrial applications
Courtesy to Bettina Kuske

## Slide 5: ERL - The global landscape
Technology Limited
Funding Limited

## Slide 6: The New Frontier : e-RIB (Radioactive Nuclei Beam) scattering
Simple imaging
Full tomography
PERLE is also coupled with Nuclear Physics European Strategy: A completely new horizon to explore the interior of exotic nuclei : charge radius, shape & new properties emerging (halo, pairing..)
All interesting phenomena occur at fm-1 : The higher the q transferred, the lower the cross-section. Considering previous achievements in this domain:
 compromise starting @ MeV (~0.5fm)
Aimed luminosity should be 1029 cm-2s-1 but much can be done at
(with unstable nuclei EVERYTHING is new !)
A long road ahead before reaching the full tomography of an exotic nucleus  The starting point is : DESTIN [DEep STructure Investigation of (exotic) Nuclei]
The beam will confine RIB in longitudinal plane (e- with positive ions), and traps have to confined RIB in transversal plane
Courtesy to David Verney
DESTIN Starts to be structured in Orsay and involving national and international communities. Coupled to the future of GANIL reflexions. A priority for Nuclear Physics Perspectives at national level

## Slide 7: Few words of organisation. PERLE Collaboration & PERLE- France
PERLE international collaboration
A Collaboration Agreement (CA) was signed by all partners.
A bilateral ICRADA between JLab-DOE and IJCLab-CNRS was signed on May 2022.
A collaboration between PERLE & bERLinPro is under discussion and will be formalised by an MoU soon.
Current discussing with other European institutes to join the PERLE collaboration.
PERLE in France. Important News
IN2P3/CNRS National Strategy (end of 2021): Perle a priority for accelerators in line with the ESPP
Application under preparation to the National Recovery Plan (End 2022) to ask for a financial support to realise PERLE phase 1 (250 MeV). Work on going is timely followed by IN2P3-CNRS and led by Maud Baylac.
PERLE infrastructures will benefit of the CPER2 funding (2M€ available from 2022) (programming phase to be started soon)
New Organization in France and significant increase of people involved.

## Slide 8
Denis Reynet System Engineers (IJCLab)
Luc Perrot Beam Dynamics (IJCLab)
Maud Baylac Gun Installation and Operation (LPSC)
Guillaume Olry RF System (IJCLab)
Patxi Duthil Cryogenic (IJCLab)
Hadil Abualrob Magnets (An-Najah / IJCLab)
Sébastien Wurth Security Issues (IJCLab)
Marc Langlet Infrastructures (IJCLab)
Bruno Mercier Vacuum System (IJCLab)
PHD student (ending now) injection lines : Ben Hounsell (100% PERLE)
PHD student (2nd year) on RF/HOM/cavities : Carmelo Barbagallo (100% PERLE)
PHD student (1st year) on Beam Dynamics : Coline Guyot (50% in PERLE)
Postdoc (beam dynamics) Alex Fomin
5 months interns (Magnets/beam dynamics)PHD thesis 2022:Rasha Abukeshek
From Jul 2022
  Postdoc (Injection line) Joshua Yoskowitz
From Oct. 2022
  Permanent CRNS position (beam dynamics) Julien Michaud
  PHD thesis Liverpool/AsTec/IJCLab (injections) Connor Monaghan
Project Organisation: PERLE Collaboration & PERLE- France

## Slide 9: NEWS – Finances and HR - French level mostly
Recent News and next to come : HR
Strong increasing in 2022 of the manpower at IN2P3 (IJCLab-Orsay and LPSC-Grenoble)
Collaboration agreement foresees/demands bilateral MoUs of IJCLab/IN2P3 with PERLE partner institutes about resource loaded (financial, material) contributions ICRADA now signed and a base for such an agreement with Jlab.
Recent News/and next to come: Finances.
TDR Phase 2022-2023, Consolidation with IJCLab/IN2P3.
2M€ from CPER for infrastructure, maybe not sufficient for the full infrastructure works. Search for extra funding.
PEPR for the PERLE Phase I under construction; Deposit of the project with CNRS (INP, IN2P3) and CEA on going.
Contributions from other countries so far only in-kind (e- source, booster, SPL to be discussed). Finances to be discussed, within PERLE and through the newly formed ERL coordination group.
Financial support (~800k€)
CDD/PHD (IN2P3, EU, Univ)
For equipment (IN2P3, CERN, Cremlin+ EURIZON)

## Slide 10: HR involvement and projection - French level mostly

## Slide 11: PERLE Timeline for TDR phase and beyond
The current phase of the project:
Technical Design phase ( 2023)
Machine design (Injector, 250MeV and 500 MeV configurations)
Beam dynamics studies
Main systems design (Buncher, Magnets, HOM couplers, full dressed cavity, power couplers, new CM, IP, dump…)
In-Kind adaptation and/or upgrade studies (DC-Gun, Booster, SPL CM) *
Definition of the needs (Diags, Cryogenics, CC, LLRF, Shielding, machine interlock system, infrastructure…)
Experiments with PERLE beam and their specific needs
Prepare to Build phase (P2B) ( 2025)
DC-Gun reinstallation and test
Equipment specifications (for DC gun)
Prototyping and tests (HOM couplers, Single cell booster cavity, B-COM magnet, 5-cells Nb Cavity) *
In-Kind adaptation and/or upgrade work (DC-Gun, Booster, SPL CM)
PERLE administrative regime (Dossier ASN)
Infrastructure (site investigations and work)
* Prototyping results could be included in the TDR phase if available
* Design of some systems could continue after TDR publication

## Slide 12: PERLE main Milestones (TDR phase and beyond)
2028
End Phase 1: PERLE @ 250MeV
2030
End Phase 2: PERLE @ 500MeV
2025
End Phase 0: Injection line
2023
PERLE TDR

## Slide 13: PERLE Configuration
PERLE: first multi-turn ERL, based in SRF technology, designed to operate at 10MW (20 mA, 500 MeV) power regime
350-500 kV
DC gun
HV tank
Booster: 5 single-cell cavities (802MHz) individually powered
Buncher
Merger
Light box
Green laser 40 MHz
Photocathodes loading chamber (Sb-based photocathodes)
Cryomodule with 4 five-Cell cavities
Total gradient 82 MeV
3 acc & 3 decc beams at different energies travelling in the CM.
Injection line delivering 500pC bunches at 7 MeV.
3 staked recirculation arcs for beams at different energies (Arcs 1, 3, 5).
Interaction Points
Switchyard: vertical separation/recombination of beams at different energies
3 staked (& inversed) recirculation arcs for beams at different energies (Arcs 2, 4, 6)
Target Parameter | Unit | Value
Injection energy | MeV | 7
Electron beam energy | MeV | 500
Normalised Emittance γεx,y | mm mrad | 6
Average beam current | mA | 20
Bunch charge | pC | 500
Bunch length | mm | 3
Bunch spacing | ns | 25
RF frequency | MHz | 801.58
Duty factor |  | CW
Beam dump

## Slide 14: Lattice optimization of the 250 MeV version of PERLE
Lattice design of the 250 MeV version of PERLE
More details Alex Fomin’s talk

## Slide 15: Status of B-com Magnet design
Yoke
Coil
Optimized aperture of 4 cm.
Pole bend radius modified to lower harmonic content.
Yoke material: standard steel (C content < 0.1%).
Magnet geometry | Initial design * | New design
Width | 40 cm | 40 cm
Height | 57 cm | 60 cm
Length | 34 cm | 34 cm
Aperture | 3.6 cm | 4 cm
Pole width | 22 cm | 25 cm
Pole height | 5.25 cm | 5.25 cm
Pole blend radius | 2.4 cm | 0.8 cm
* Courtesy to Jay Benesch (Jlab)
Tool: Opera 3D
Coil Parameters | Value
Excitation current NI | 11520.26 A.turn
Number of turns/coil | 56 = 30
Current | 384 A
Coil cross section | 
Current density J | 5.315 A/
Material | Copper
Coil Parameters | Value
Excitation current NI | 11520.26 A.turn
Number of turns/coil | 
Current | 384 A
Coil cross section | 
Current density J | 
Material | Copper
30° bending angle (8.8 cm exit point).
Hollow copper conductor
Excitation current calculated at B = 0.87 T
Design parameters
Courtesy to Rasha Abukeshek and Hadil Abualrob

## Slide 16: Status of B-com Magnet design
along the magnet length
for 0.34 m yoke length  B = 0.88 T
No chamfer or shims added, only a blend radius of 8 mm is used
Field homogeneity along the beam path: 0.036%
 Quadrupole & sextupole components can be dealt within the lattice.
Initial design: 0.1% field quality
 Improvement by one order of magnitude
Harmonics content calculated along beam trajectory:
Field calculations:

## Slide 17: Plan of magnet activities
Prototype of B-COM magnet:
Pursue the work toward B-COM magnet complete specification.
Proceed to a thermal study and mechanical complete design
Order a B-COM magnet prototype (by mid 2023) to be measured and qualified later.
Design studies of arc magnets
Pursue the ongoing design work on arc dipoles and quadrupoles and set the specifications.
Define the needs on multipoles regarding the two lattice configurations.

## Slide 18: Status of HOM design Studies:
3D- Eigenmode simulation: HOMs Identification in PERLE cavity
TE111
TM110
TM111
TE112
TM120
TM121
TE121
Wakefield simulations for multi-beam excitation scheme (CST Studio)
Longitudinal wake impedance [Ω]:
Transverse wake impedance [Ω/m] – Panofsky-Wenzel Theorem:
More details in Carmelo Barbagallo’s talk

## Slide 19: Status of HOM design Studies:
HOM coupler optimization of 3 different designs
Couplers geometrically optimized according to the HOM spectrum & S-parameters btw port 1 (beam pipe) & port 2 (coupler output) studied.
The hook coupler provides higher damping of the first two dipole passbands (TE111 and TM110)
The DQW coupler exhibits a better monopole coupling for TM010 mode than the probe design.
Study of 2 damping schemes with 4 HOM couplers (Especially for dipole HOM extraction)
Promising results of DQW configuration: It allow damping both monopole and dipole HOMs below the analytically-computed beam-stability limits

## Slide 20: Plans on HOMs and cavity activities :
HOM couplers further studies and prototypes:
Finish the ongoing thermal studies of HOM couplers (COMSOL simulation)
3D printing of 1 DQW, 1 hook and 1 probe HOM couplers (@CERN): in polymer & Copper coated.
 First tests on a 801 MHz mono-cell Cu cavity (provided by CERN) will be performed at JLab this month.
A DQW coupler 3D metal printed (@CERN) is scheduled once the tests on polymer couplers are done and conclusions are obtained. Other couplers will follow.
Cavity prototypes:
A 5-Cell copper cavity will be fabricated soon @Jlab (same design as the 1st Nb 5-cell cavity fabricated in 2017) to allow end group design optimisation with optimised HOM coupler configuration.
A 5-Cell Niobium cavity with optimised end groups will be fabricated once all the tests are made.
First Hook type polymer coupler 3D printed

## Slide 21: Cryomodule design:
Cryomodule design under study: two options are currently considered at IJCLab: the SPL and the ESS design. The two candidates present similar features:
Characteristics | ESS (704MHz) | SPL (704MHz) | PERLE (802MHz)
Number of cavities/cells | 4/5 or 6 | 4/5 | 4/5
Coupler to coupler length (mm) | 1500 | 1490,5 | -
Length flange to flange (mm) | 1258,8 (Mβ) / 1316,3 (Hβ) | 1397,3 | 1292,5
Coupler to flange dim. (mm) | 115 (Mβ) / 130 (Hβ) | 116,4 | 96,7
Cells external diameter (mm) | 378,9 (Mβ) / 385,7 (Hβ) | 386,5 | 335
Designed by IJCLab & CERN
Some components available
Designed by IJCLab
Courtesy to Gilles Olivier

## Slide 22: Cryomodule design:
CIRCUIT | Heat load SPL/HG (W) | Heat load ESS Ell. Hβ (W) | Heat load PERLE (W)
RF losses | 200 | 24,4 | 260 (Q0 1.E+10)
Beam losses |  | 3,25 | To be evaluated
HOM ports |  |  | 80
Static losses | 30 | 13,23 | 30
High static & dynamic heat loads for 4 cavities
>> He low pressure circuit to be well dimensioned
Main dimensioning parameters & constrains
2+2 HOM couplers actively cooled
& RF power extracting circuits
2 Ø100 bursting disk (PED rules)
Ferroelectric fast reactive tuner
Many space need to be available inside the cryomodule

## Slide 23: Cryomodule design:
Intermediate supporting structure (spaceframe)
Cavity string hung by rods
Insertion of the cavity string by the extremity (rollers)
Trap doors for tuner access
Connexion to the valve box on the top of the vacuum vessel
More available space inside (+ 400mm in diameter and more transversal space between cavities)
Design validated: series fab. & tests ongoing (Qty 30)
ESS design
Vacuum vessel with top cover
Insertion of the assembled cavity string by the top
Cavity string supported by couplers
Connexion to valve box at the extremity of the vacuum vessel
Vacuum vessel fabricated (top cover to be modified)
Compact design >> lack of space
SPL design

## Slide 24: Injection line optimisation
Electron source to booster exist optimisation:
The ALICE electron gun electrode geometry has been re-optimised for PERLE’s new requirements.
Optimisation with a 4 cavity booster, from the cathode to the exit of the first main Linac, was performed and meets the specification:
 | Achieved values | Specification
Horizontal emittance | 5.0 mm mrad | < 6 mm mrad
Vertical emittance | 2.7 mm mrad | < 6 mm mrad
Bunch length | 3.2 | 3 mm
Kinetic energy | 86.1 MeV | 88.6 MeV
Horizontal beta function | 6.1 | 8.6
Horizontal alpha function | -0.48 | -0.66
Vertical beta function | 5.1 | 8.6
Vertical alpha function | -0.17 | -0.66
Ben Hounsell PhD work
Hounsell et al. - Linac 22 Conference

## Slide 25: Injection line optimisation
Ben Hounsell PhD work
The charge density distribution of the bunch in the horizontal and vertical planes at the exit of the main linac
Longitudinal phase space distribution prior to entering the main linac. The particle colour indicates initial longitudinal slice.
Transverse phase space distributions at the end of the main linac.

## Slide 26: PERLE e- Source
Alice (Daresbury) DC gun received at Orsay on May 2019. We are currently working on its re-installation and operation at low parameters, then studying its upgrade to meet PERLE requirements.
The “Igloo”: Equipped experimental hall to host the DC gun
All received parts transferred to the installation area (March 22)
More details in a dedicated talk by Maud Baylac
Courtesy to Alexandre Gallas & Denis Reynet

## Slide 27: PERLE e- Source
HV power supply assembly
(July 22)
Checking the HV vessel tightness
(September 22)
HV vessel installation
(June 22)

## Slide 28
Conclusions
ERL machines open a new frontier for the physics of “the electromagnetic probe” (ep, eA, eN). PERLE@Orsay is a key ERL project for HEP and Nuclear Physics communities
PERLE@Orsay has been recognised (together with bERLinPro) an essential pillars of the ERL ESPP strategy. It combines high current and multi-passes (high luminosity / higher energy)
PERLE@Orsay is a very challenging machine : RF CW operation, specific SFR systems, multi-bunches operation, high power machine, complex Lattice design, broad range diagnostics, beam dynamics...
The International collaboration is formed and still opened to new comers.
Important boost in the last 9 months in France (IJCLab and LPSC) and we are actively entered in the TDR and the P2B phases.

## Slide 29
Thank you for your attention!