## Slide 1
Work Package 5 : Cryogenics
P. DUTHIL
H. SAUGNAC
M. PIERENS
September 28th 2022

## Slide 2: Work Package 5 : Cryogenics - Status
Context
  What to cool down:
    1 accelerating device = SRF elliptical cavity (f~ 802 MHz)
    1 feeding device = RF power coupler
    2 or 4 (TBC) HOM couplers (and probes)
    = {RF package}
  Distributed in 3 sets:
    1 Booster (injection chain)
      5 RF packages
    1+1 CMs (accelerating chain):
      4 RF packages
2

## Slide 3: Work Package 5 : Cryogenics - Status
Updated heat loads:
  Dynamic heat loads (due to RF) coarse estimate:
    100 W per SRF cavity (!)
    ~400 W @ 2 K per CM
    ? for the booster
  PERLE’s cooling needs (isothermal heat load @2 K only): ~1 kW
    For comparison, PERLE’s 2 K heat loads
      = 2x heat loads currently considered for MINERVA (MyRRHa) (~100 m long linac);
      = 1/3 of European Spallation source installed cooling power (~400 m long linac);
    → medium scale cooling system is needed (with large turndown capability)
3

## Slide 4: Work Package 5 : Cryogenics - Status
TDR objectives:
  Define the cryogenic architecture :
    User chain: what to cool, how and when
    Cooling power production chain: what to produce, how, where and when
    Cooling power distribution chain: how to cool down
    Asses the cryogenic operational modes of PERLE machine (modelling)
  Propose a preliminary design of the cryogenic distribution system :
    Provide preliminary sizing
    Propose a preliminary engineering study: design, building, installation and commissioning of the system
    Update project costs
  Specify the cryoplant (in view of a call for tender after the TDR)
    Fluids and powers
    Operation modes
    Installation phases
    …
4

## Slide 5: Work Package 5 : Cryogenics
WP6 IJCLab members:
Patxi DUTHIL, Cryo Group
Hervé SAUGNAC, Cryo Group
Matthieu PIERENS, Cryo Group
Design office
WP6 Partners:
Jean-Pierre THERMEAU, APC-IN2P3 (CNRS)
CRYOPLANT
Refrigerator (Cold Box)
Cycle compressors
Cryogenic purifier
Pure gas storage
Gas analysing system
HELIUM RECOVERY, PURIFICATION AND STORAGE SYSTEM
Purification system
Helium recovery system
Liquid helium storage
Liquid nitrogen storage
CRYOGENIC DISTRIBUTION SYSTEM
Cryogenic Distribution Lines
Valves Boxes
Auxiliary lines
End Box (TBC)
CONTROL & COMMAND SYSTEM
Sensors
PLC
Signal coniitioners
Cables and signal routing
C&C architecture and modelling
PBS
WP organization for the TDR:
WP5: Cryogenics
Task 5.1:
Requirements and general specification
Task 5.2:
Cryogenic architecture
Task 5.3:
Cryoplant
Task 5.4:
Cryogenic Distribution System
Task 5.5:
Control and Command system
WBS
5

## Slide 6: Work Package 5 : Cryogenics - Status
Task Status: we started
  Task 5.1. Requirements and general specification
    A list of parameters was issued  to be completed with values by the project members
  Task 5.2. General architecture
    Biblio is ongoing
    (methodology for modeling linac cryogenics is currently being developed for the Myrrha project and might be re-used for PERLE)
6

## Slide 7: Thank you for your attention

## Slide 8: Work Package 5 : Cryogenics
Opened questions
  What are we building: 250 MeV, 500 MeV, both?
  When?
  Together, lets set up the parameters of the machine