## Slide 1: The P3 experiment: a Positron Source Demonstrator for FCC-ee
eeFACT Workshop - Frascati, 15 September 2022
Nicolas Vallis (PSI / EPFL) on behalf of FCC-ee Injector WP6

## Slide 2: The P3 project PSI Positron Production
Introduction
    FCC-ee and P3
    e+ production at SwissFEL
Key Technology and Beam Dynamics
    AMD
    RF Cavities
    Solenoid around RF Cavities
    The P3 beam
Beam Diagnostics
Project Status and Conclusion

## Slide 3: FCC-ee Injector Study
Work package in FCC collaboration.
Two deliverables included in FCC feasibility study:
    Design proposal for FCC-ee Injector.
    Proof-of-principle experiment for novel positron source (P3).
Due to FCC-ee high current requirements
    Only target-based e+ production schemes considered.
    Vast production of e+, poor transport efficiency to DR
    Use of HTS solenoids for the AMD proposed for higher efficiency.
Schematic of FCC-ee Injecor Complex
Target
Adiabatic Matching Device
10 RF Cavities surrounded by solenoids

## Slide 4: The PSI Positron Production (P3) Experiment
Target and HTS Adiabatic Matching Device
6 GeV beam from SwissFEL linac
Solenoids
Beam diagnostics
2 RF Cavities
Concept design of P3

## Slide 5: Goals of P3
References for yield value:
Main goal is to provide first experimental validation of such a yield.
But a compact positron source at PSI can:
    Host further experiments/tests
    Contribute to other future positron machines
E
t
DR Acceptance window
1.54 GeV
SuperKEKB Factory (State of the art, 3 GeV) [1] | 0.5
FCC-ee requirements [2] | 1 (plus safety factor 2)
P3 simulations | 8
Impression of the a e+ beam at entrance of DR
and DR acceptance window
[1] K. Akai, K. Furukawa, and H. Koiso, "Superkekb collider", 2018.
[2] I. Chaikovska et al., "Positron source for FCC-ee", 2019.

## Slide 6: e+ Source at SwissFEL
SwissFEL linac can provide high quality 6 GeV electron beam.
Strict radiation limits do not allow for high bunch charges and rep. rates.
    beam dynamics insensitive of electron charge and time structure.
    thermomechanical study of the target excluded from P3.
SwissFEL facility

## Slide 7: II. Key Technology and Beam Dynamics
High temperature superconductor-based AMD
(12.7 T peak on-axis)
NC or SC solenoids
(0.4 to 1.5 T peak on-axis)
SW, S-band Cavities with large iris aperture 40 mm

## Slide 8: Solenoids: Beam Matching and Confinement
Baseline:
    High temperature SC based Adiabatic Matching Device (12.7 T)
    SC solenoids around cavities (1.5 T) or
    NC solenoids around cavities (0.4 T).
AMD matches the e+ beam into capture system. Part of the beam is lost and norm. transverse emittance decreases over first RF cells.
SC solenoids contain the matched beam. Capture efficiency and emittance stabilize.
12.7 T
1.5 T

## Slide 9: HTS Adiabatic Matching Device
HTS demonstrator built at PSI:
    4 ReBCO tape coils at 2kA
    Operation at 18.2 T, on-axis peak
    Temperature 20 – 30 K, no need of He cooling
    No insulation, quench self-protected
Simulation study at CERN found no critical machine protection issues [1]
Technical design of cryostat in development at PSI
HTS demonstrator at PSI (M. Duda et al.)
Preliminary model of the AMD,
including cryostat (H. Garcia Rodrigues)
[1] B. Humann et al., Radiation Load Studies for the FCC-ee Positron Source with a Superconducting Matching Device, 2022.

## Slide 10: Solenoids Around RF Cavities (I)
Solenoids must create strong and flat magnetic channel.
Mechanical constraints exist, separation must be provided for waveguides and installation
Waveguides
Assembly

## Slide 11: Solenoids Around RF Cavities (II)
41 %
75 %
Extended simulations over 10 RF Cavities with optimized (left) and breached (right) magnetic channels.

## Slide 12: Solenoids Around RF Cavities (III)
Two baseline options for P-cubed:
    Superconducting
        NbTi
        1.5 T on axis
    Normal Conducting
        Copper
        0.4 T on axis
Solenoid strength around cavities [ T ]
25%
72%
0.3 T as NC
reference point
1.5 T as SC
reference point
Capture efficiency after at 200 MeV

## Slide 13: Solenoids Around RF Cavities (IV)
Superconducting:
    Extremely high yield provided (8.0)
    Lower power consumption
    High cost (above tender call limit
    230 kCHF)
Normal conducting:
    Lower yield (3.1), sufficient for FCC-ee requirements
    Extremely high power consumption (>100 kW), large amount of copper required
    Lower cost, conventional technology
Superconducting (NbTi, 1.5 T)
Normal Conducting (Copper, 0.4 T)

## Slide 14: RF Cavities
z
E
+/- 3.8 %
λ
1.54 GeV
Ideally:
    High capture efficiency
    Low energy spread
    Positrons in one bucket
Mechanical model of RF Cavities (R. Zennaro)
Impression of the a e+ beam at entrance of DR
and DR acceptance window

## Slide 15: Estimation of the Yield at DR
E
+/- 3.8 %
λ
1.54 GeV
P3
Φ1
Φ2
8 extra cavities
On-crest
Analytical transformation
in longitudinal plane.
Transverse losses neglected
200 MeV
200 MeV
e+
e- discarded

## Slide 16: RF Working Points
Working point for Max. Yield at DR = 8.0 @ (Phi1 = -170, Phi2 = 0)
Phase cavity 1
Phase cavity 2

## Slide 17: RF Working Points (II)
Second bucket:
Lower energy spread
e+ concentrated in main bunch
Deceleration over first RF cells

## Slide 18: RF Working Points
Yield at DR = 5.1 @ (Phi1 = -40, Phi2 = -100)
Points in this region provide high capture efficiency (>75%) but lower yield!
Phase cavity 1
Phase cavity 2

## Slide 19: RF Working Points (III)
First bucket:
High energy spread
Many electrons in first bucket

## Slide 20: The p3 beam (I)
AMD max. | 12.7 | T
Solenoids max. | 1.5 | T
e+ capture efficiency | 74 | %
Energy Spread | 92 | MeV
Norm. emittance | 15157 | pi mm mrad

## Slide 21: The P3 Beam (II)
 | Yield at DR | 8.0 | 
 | AMD max. | 12.7 | T
 | Solenoids max. | 1.5 | T
@ 200 MeV | Capture efficiency | 72 | %
 | Energy Spread | 66 | MeV
 | Norm. emittance | 14667 | pi mm mrad
Longitudinal profile of e+ beam at DR entrance

## Slide 22: II. Beam Diagnostics
Broadband Pick-Ups
Charge detector
Spectrometer
Faraday Cups

## Slide 23: Broadband Pick-Ups
BBPs measure time structure of the beam after second cavity.
Broadband operation and high sampling frequency (40 GHz) required to differentiate e+ and e- bunches.
Based on SuperKEKB factory diagnostic [1].
e+
e-
4 Pick-Ups
Simulated signal at BBPs (E. Ismaili)
[1] T. Suwada et al., "First simultaneous detection of electron and positron bunches at the positron capture section of the SuperKEKB factory", Sci. Rep., vol. 11, 2011.

## Slide 24: Faraday Cups
Measurement of e+ and e- charge separately.
Alluminum FCs at 25 Ohm. Matching to 50 Ohm through 2 parallel coax cables
Negligible electron backscattering
B
e+
e-
● e+ ● e-
Optimized dimensions of diagnostics chamber.
e+e- beam at faraday cups

## Slide 25: Spectrometer and Charge Detector
Dipole strength scanned to measure e+ energy profile
e+ at different pz detected by narrow screen
Technology of the detector t.b.d.!
e+
B
Schematic of energy spectrum measurement
Pz spectrum reconstruction

## Slide 26: IV. Project Status
Mechanical design of P3 and RF network (A. Magazinik)
Radioprotection studies (I. Besana)
Design of the extraction line and P3 bunker at SwissFEL (D. Hauenstein and M. Schaer)

## Slide 27: Timeline
SwissFEL Shutdowns
Preliminary timeline of the P3 experiment
(M. Schaer and D. Hauenstein)

## Slide 28: Status of Experiment Design
 | Target | Concept design defined.
 | RF Structures | Ready for copper purchase.
Magnets | AMD | HTS tape to be purchased shortly. Design of cryostat almost complete.
 | Solenoids around RF structures | NC and SC options presented.
Beam diagnostics | Faraday Cups and diagnostics chamber | Dimensions optimized. Backscattering simulations performed.
 | Broadband pick-ups | Feedthroughs to be purchased and tested shortly. Optimization of pickups in progress.
 | Spectrometer | Baseline design complete. Mechanical modification of existing dipole in progress.
 | Charge detector | Technology under discussion.
Purchase phase
In progress
Concept design

## Slide 29: Final Remaks
P3 is at advanced design stage and on-schedule. Final design expected for 2023 Q1.
Experiment to take place in 2025. Eventual delays might occur due to installation and integration issues.
Make the most of our compact positron source at PSI:
    A demonstrator for all future e+e- colliders and positron machines.
    Possible host to further experiments and tests.
Open to new ideas and collaborators!

## Slide 30
This work was done under the auspices of CHART (Swiss Accelerator Research and Technology) Collaboration, https://chart.ch
Mike Seidel (thesis advisor)
Paolo Craievich
Riccardo Zennaro
Mattia Schaer
Anastasiya Magazinik
Fabio Marcellini
Erisa Ismaili
Michal Duda
Jaap Kosse
Henrique Garcia Rodrigues
Acknowledgements