## Slide 1: Electron sources and pre-injector
Zdenek Vostrel
FCC-ee Injector Studies Mini-Workshop
14 November 2022

## Slide 2: Overview
Summary of previous work
Study of initial Gaussian distribution
Top-up injection studies

## Slide 3: The electron gun
Overview
What do we optimise?
0.7 m
5.7 m
10.7 m
MaxE = 16.2 MV/m
MaxE = 25 MV/m
MaxE = 25 MV/m
MaxE = 100 MV/m
Phi(2)
Phi(3)
Phi(4)
Phi(1)
MaxB(1)
Bunch energy at the end: ∼ 200 MeV
Electron emission:
Initial distribution
Emission time

## Slide 4: Previous work
Tomas Brezina – Technical Student before me
Focused on optimalisation of 3.4 nC charge
Results were used as an input for Simona

## Slide 5: Previous work
Tomas Brezina – Technical Student before me
Brief study of Gaussian distribution
  Large increase in emittance  work for me
Study of 5 nC bunch with uniform distribution
Uniform
Gaussian
Initial spot size | 1.5 mm
Laser pulse length (FWHM) | 15 ps
Gun solenoid | 0.2413 T
TW Acc. Gradient | 16.2 MV/m
First acc. Section at | 1.068 m
Emittance RMS | 3.1 mm
Energy Spread RMS | 0.4 %
Energy | 206 MeV
Beam size RMS | ~ 0.7 mm
Bunch length RMS | 1.4 mm
Tomas: Uniform, 5 nC

## Slide 6: Previous work
Steffen – Simona´s request for shorter bunches
Shortened bunch by decreasing bunch length & increase spot size
Bunch can be shorten at the expense of the emittance
Initial spot size | 1.5 mm
Laser pulse length (FWHM) | 15 ps
Gun solenoid | 0.2413 T
TW Acc. Gradient | 16.2 MV/m
First acc. Section at | 1.068 m
Emittance RMS | 3.1 mm
Energy Spread RMS | 0.4 %
Energy | 206 MeV
Beam size RMS | ~ 0.7 mm
Bunch length RMS | 1.4 mm
Tomas: Uniform, 5 nC
Uniform distribution, 5.0 nC, spot size: 2.0 mm, Bsol:0.243 T, Accdist:0.9 m, pulse length 4 ps
Emittance: 6.1 um, beam size: 1.9 mm , bunch length: 0.65 mm, deltaE= 0.24 %
Steffen: Uniform, 5 nC

## Slide 7: Previous work
Comparison of phase spaces
Steffen:
Uniform, 5 nC
Emission time: 4 ps
Aim: shorter bunches
Tomas:
Uniform, 5 nC
Emission time: 15 ps
Aim: best emittance

## Slide 8: Gaussian transversal distribution
Optimalised for Gaussian distribution
Difference between Gaussian and Uniform initial distribution is not that large
Bunch parameter | Gaussian Initial Distribution | Uniform Initial Distribution
Transversal emittance | 6.2 mm mrad | 4.9 mm mrad
Beam size RMS | 1.4 mm | 1.6 mm
Longitudial emittance | 400 keV mrad | 281 keV mrad
Bunch length RMS | 1.03 mm | 0.9 mm
Energy spread RMS | 576.5 keV | 350 keV
Average energy | 205.7 MeV | 204.1 MeV
Total charge | 5.5 nC | 5.5 nC
Beam parametres after the aparature (15 m)
Uniform
Gaussian
Tomas

## Slide 9: Top-up injection
Complicated to change at high frequency
Increase only charge ( intensity of inducing laser) realistic?
2. Keep gun and spot size constant
1. Optimise for each charge
3. Keep charge density constant
Optimise only for one given charge (which would be mostly used)
Change spot size so the charge density remains contant  similar space charge effects

## Slide 10: Charge variation at constant gun parameters
I kept the optimised parameters used to obtain results for Gaussian distribtion
Total charge scan
How conservative do we want to be?
Particles lost at the gun
Can be compensated by magnetic field

## Slide 11: Charge variation at constant gun parameters
Transversal size (sig_x, sig_y of the initial Gaussian distributions)
Longitudinal size (emission time Lt)
Change charge density
The particles are lost in the gun itself
Adjust the phase of the gun (didn´t work well)
Gun parameters

## Slide 12: Increase initial bunch size
Transversal size (sig_x, sig_y of the initial Gaussian distributions)
Longitudinal size (emission time Lt)
Change charge density

## Slide 13: Increase initial bunch size
Transversal size (sig_x, sig_y of the initial Gaussian distributions)
Longitudinal size (emission time Lt)
Change charge density

## Slide 14: Increase initial bunch size
3-6 nC  emittance ∼ constant
Emission surface increase ∼ emission time increase
Large increase of emittance for lower charge (can be optimised by the solenoid B field)
How conservative do we want to be? (large margin  worse emittance)
Change charge density
Transversal size (sig_x, sig_y of the initial Gaussian distributions)
Longitudinal size (emission time Lt)

## Slide 15: Increase initial bunch size
Better to increase transversal beam size  better bunch length
Large variation of bunch length and size for charge variation with constant gun parametres

## Slide 16: Top-up injection
Complicated to change at high frequency
Increase only charge ( intensity of inducing laser) realistic?
2. Keep gun and spot size constant
1. Optimise for each charge
3. Keep charge density constant
Optimise only for one given charge (which would be mostly used)
Change spot size so the charge density remains contant  similar space charge effects

## Slide 17: Compensate bunch size to keep Q density constant
Same charge density  similar space charge effects
Changing emittance
More stable beam size (compared to fixed parameters)
Optimised gun parameters for Sig_x = 1.2 mm, Lt = 4 ps
Last simulated charge = 6.5 nC (higher charge not tested)

## Slide 18: Compensate bunch size to keep Q density constant
Same charge density  similar space charge effects
Changing emittance
More stable beam size (compared to fixed parameters)
Optimised gun parameters for Sig_x = 1.2 mm, Lt = 4 ps

## Slide 19: Improve the charge density compensation method
Motivated by Simona  finding optimal value of C_sig_x (which I kept constant previously)
Optimalised for Q = 5.5 nC sig_x = 1.45 mm, C_sig_x = 1.7
Compensating charge by changing only sig_x
Gun parameters constant in all simulations

## Slide 20: Sanity check!
Huge improvement of emittance
Tomas got similar results for the normal distribution  the low emittance makes sense
I still have Gaussian distribution
Initial spot size | 1.5 mm
Laser pulse length (FWHM) | 15 ps
Gun solenoid | 0.2413 T
TW Acc. Gradient | 16.2 MV/m
First acc. Section at | 1.068 m
Emittance RMS | 3.1 mm
Energy Spread RMS | 0.4 %
Energy | 206 MeV
Beam size RMS | ~ 0.7 mm
Bunch length RMS | 1.4 mm
Tomas: Uniform, 5 nC

## Slide 21
Tomas  emittance estimate for uniform initial distribution
Steffen  we can shorten the bunch (by decreasing emission time) at the expense of emittance
Currently optimising mainly for 5.5 nC
Gaussian initial distribution does not significantly worsen the bunch properties
Investigating options for top-up injection
  Charge density compensation seems promising
  Changing sig_x or cut of sig_x in Gaussian distribution?  TODO
    Probably need to talk to laser people
Summary

## Slide 23: Produced beam
Beam parametres after the aparature (15 m)
Parameter | Gaussian Initial Distribution | Uniform Initial Distribution
Charge | 5.5 nC | 5.5 nC
Z distribution | Plateau | Plateau
Emission time | 0.004 | 0.004
Accelerating field gradients | 100 & 16.2 & 25 & 25 MV/m | 100 & 16.2 & 25 & 25 MV/m
Sig x | 1.2 mm | 1.15 mm
Cutt off | 2.2 sigma | -
MaxB(1) | 0.257 T | 0.256 T
Phi(1) | 0 deg | -15 deg
Phi(2) | -10 deg | -19 deg
Phi(3)&Phi(4) | 0 deg | 0 deg
Parameter | Gaussian Initial Distribution | Uniform Initial Distribution
Transversal emittance | 6.2 π mm mrad | 4.9 π mm mrad
Beam size | 1.4 mm | 1.6 mm
Longitudial emittance | 400 π keV mrad | 281 π keV mrad
Bunch length | 1.03 mm | 0.9 mm
Energy spread | 576.5 keV | 350 keV
Average energy | 205.7 MeV | 204.1 MeV

## Slide 24: Phase space comparison
Gaussian
Uniform

## Slide 25: Phase space orientation for charge variation with constant gun parametres
1 nC
3 nC
6 nC
Gun parametres kept constant

## Slide 26: Why sig_x = 1.2 mm
Parameter | Gaussian Initial Distribution | Uniform Initial Distribution
Charge | 5.5 nC | 5.5 nC
Z distribution | Plateau | Plateau
Emission time | 0.004 | 0.004
Accelerating field gradients | 100 & 16.2 & 25 & 25 MV/m | 100 & 16.2 & 25 & 25 MV/m
Sig x | 1.2 mm | 1.15 mm
Cutt off | 2.2 sigma | -
MaxB(1) | 0.257 T | 0.256 T
Phi(1) | 0 deg | -15 deg
Phi(2) | -10 deg | -19 deg
Phi(3)&Phi(4) | 0 deg | 0 deg

## Slide 27: Initial distribution comparison