## Slide 1: e+ Linac of the FCC-ee Injector, Discussing Open Points Based on 2 Possible Layouts
Mattia Schaer :: Paul Scherrer Institute, Andrea Latina :: CERN
FCC-ee Injector Study Collaboration, Mini Workshop, Orsay, 24.11.2022

## Slide 2: What We Have…
First start-to-end particle tracking (RF-Track) from the prod. target to the damping ring  Large transport efficiency  Yield 35 % smaller than expected from simulations of only the capture system
Two possible linac layouts
  Transport with solenoids up to 1.54 GeV
  Transport with solenoids up to 780 MeV + conventional FODO lattice up to 1.54 GeV
Transverse emittance as a function of the considered (core) bunch portion

## Slide 3: e+ Linac Layout 1
Up to 1.54 GeV
3D mechanical model fully consistent
with beam dynamics, RF and magnetic simulation setups

## Slide 4: e+ Linac Layout 1, Transport
Start-to-end tracking with RF-Track
Artifacts
from particles with s < 0
Artifacts
from
particles
with s < 0

## Slide 5: e+ Linac Layout 1, Final Transverse PS

## Slide 6: e+ Linac Layout 1, Final Longitudinal PS

## Slide 7: e+ Linac Layout 1, Final Main Bucket (Long. PS)

## Slide 8: e+ Linac Layout 1, Yield at Damping Ring
Yield at DR = 4.2= 0.65 * expected
After application of +/- 3.8 % energy window

## Slide 9: e+ Linac Layout 1, Emittance of Accepted Particles
10458 mm mrad
vs.
Reduction of a
factor 2!

## Slide 10: e+ Linac Layout 2
780 MeV
Up to 1.54 GeV
3D mechanical model fully consistent
with beam dynamics, RF and magnetic simulation setups

## Slide 11: e+ Linac Layout 2, Different Sections

## Slide 12: e+ Linac Layout 2, Transport
Dynamics up to 780 MeV identical to Layout 1
Start-to-end tracking with RF-Track
Matching section and FODO designed with Elegant
(without acceleration)

## Slide 13: e+ Linac Layout 2, Final Horizontal (X) Transv. PS

## Slide 14: e+ Linac Layout 2, Final Vertical (Y) Transv. PS

## Slide 15: e+ Linac Layout 2, Final Longitudinal PS

## Slide 16: e+ Linac Layout 2, Final Main Bucket (Long. PS)

## Slide 17: e+ Linac Layout 2, Yield at Damping Ring
Yield at DR = 4.6 = 0.70 * expected
After application of +/- 3.8 % energy window

## Slide 18: e+ Linac Layout 2, Emittance of Accepted Particles
9807 mm mrad
vs.
Reduction of a
factor 2!

## Slide 19: Smaller Yields Than Initial Estimations…
Yield estimation at DR = 6.54 (Yongke)
After analytical computation of long. dynamics
and application of +/- 3.8 % energy window
Energy distr.
much more peaked!

## Slide 20: … Probably Due to Ez(r) ≠ const. and Large σr
Trial simulation accelerating with Ez = const.
(Bz identical to Layout 1)
Energy histogram much more similar
to the analytical tracking!
(Hypothesis to be further verified…)

## Slide 21: … and What we Still Need
Apply 6D (?) damping ring acceptance, current energy window is a very rough assumption  Robust yield estimation
Verify feasibility of solenoids up to 780 MeV in detail (misalignments, multipolar components, etc.)
Design chicane to separate e+ and e-, 1st trial will be in the matching section at 780 MeV
Design energy compressor, if e+ charge accepted in the damping ring is not enough (depends on pt. 1)
Consider quadrupoles around RF structures at intermediate energies (depends on pt. 2, costs and mechanical complexity)

## Slide 22: Next Step 1: Apply 6D Damping Ring Acceptance
+/- 2 mm (full)
Dynamic aperture of damping ring
(C. Milardi, A. De Santis)

## Slide 23: Emittance vs. Bunch Portion @ 1.54 GeV

## Slide 24: 1st Estimation of Beta-Func. Required At Injection
+/- 2 mm (full)
, 
With
= norm. emittance of current beam within E window
With
= norm. emittance of current full beam

## Slide 25: About 2 Orders of Magnitude Difference
With
= norm. emittance of current beam within E window
With
= norm. emittance of current full beam
Injection-extraction dog leg
(C. Milardi, A. De Santis)

## Slide 26: Backup Slides

## Slide 27: Emittance vs. Bunch Portion @ 200 MeV