## Slide 1
WP3 - Positron source: target and capture system
I. Chaikovska on behalf of the WP3 team

## Slide 2: WP3 contributions

## Slide 3: FCC-ee positron source: requirements
Ne-/bunch ⨯ ηe+Accepted ≥ 4 nC/bunch ⨯ 2
The complete filling for Z running => Requirement ~2.4 ⨯ 1010 e+/bunch (4 nC)
*A safety margin of 2 is currently applied for the whole studies.
All the studies are focused on the operation scheme: 6 GeV, 2 bunches/pulse, 200 Hz rep. rate, the max e- bunch charge is 4 nC ➜ ~ 9.6 ⨯ 1012 e+/s
Accepted e+ yield is a function of primary beam characteristics + target + capture system + DR acceptance

## Slide 4: Benchmark with the SuperKEKB positron source
e- drive beam: 3.5 GeV, 2 bunches/pulse, 10 nC, 50 (25) Hz
F. Alharthi (IJCLab)
The positron source of SuperKEKB is the world’s highest intensity positron source currently in operation.
KEK has long operation experiences, test facility and the real positron source in operation (simulation results, experimental data) → ideal for a benchmark for the FCC-ee simulation software
Y. Enomoto (KEK)
0.3 e+/e-

## Slide 5: FCC-ee: positron production
Conventional scheme: bremsstrahlung and pair conversion (mainly studied until now)
Hybrid scheme (crystal-based positron source) use the intense radiation emitted by high energy (some GeV) electrons channeled along a crystal axis => channeling radiation.
Schemes under consideration now
L. Bandiera (INFN/Ferrara)

## Slide 6: Hybrid source: preliminary positron production optimization
6
A 2 mm thick crystal has been selected to be used as a radiator for the hybrid positron source.
→ good photon yield, moderate values of photon divergence and energy deposition in the crystal.
M. Soldani (INFN/Ferrara)
→ Comparable e+ production rate but lower thermal load.
→ Next: capture simulations

## Slide 7: FCC-ee: positron capture system (matching device)
HTS solenoid field, with optimised target position
FC on-axis field, with fixed target position
Flux Concentrator (FC)
High-Temperature Superconducting (HTS) solenoid

## Slide 8: Flux Concentrator-based capture system (CDR baseline)
Perform radiation load studies, the first estimation for the target design. First mechanical integration.
Optimize the FC design if needed (rep. rate ?)
P. Martyshkin, Y. Zhao (CERN)

## Slide 9: SC solenoid –based capture system for FCC-ee
The first results (preliminary)
Capture eff. @ 200 MeV: ~0.4
e+ yield : ~ 6 Ne+/Ne-
e+ norm. emittance: ~11 mm.rad
Positron capture section –v0
Capture system “-version 0”
Positron production: conventional scheme
Matching Device is based on the SC solenoid (5 HTS coils, 72 mm bore including shielding)
Capture Linac is based on the L-band TW RF structures ( 2 GHz, 3-m long, Ф = 60 mm)
NC long solenoid B = 0.5 T (realistic design conf. 2)
V. Mytrochenko (IJCLab)
Y. Zhao (CERN)

## Slide 10: AI-driven performance boost (GIOTTO Application)
HTS
Helmholtz coils
0.
1
2
3
4
5
6
7
Helmholtz coils
Bridge coils
Bridge coils
z [m]
Target
L-band TW CERN Study
L-band TW CERN Study
40.7% of extracted e+ in 1st RF bucket E = 45 MeV ΔE = 29 MeV (64% ΔE/E)
εn,x = 1.0 104 mm-mrad
σx = 7.8 mm σz = 9.7 mm
Starting Point
First Ooptimized Working Point
A. Bacci and M. Rossetti-Conti (INFN/Milano)
65.0% of extracted e+ in 1st RF bucket E = 82.14 MeV ΔE = 21.1 MeV (26% ΔE/E)
εn,x = 1.1 104 mm-mrad
σx = 8.63 mm σz = 14 mm
Opt. with bridge coils

## Slide 11: List of current open points
Mechanical design/target reliability. Moving target? Comparison of conventional vs. hybrid schemes.
  Positron source operating conditions for different modes (incident beam power, how many years per mode) ➜ radiation load studies.
Effect of high magnetic field on the positron production in target.
FC-based capture system? Simulations with large aperture acc. structures. FC design (SuperKEKB, CLIC)? Radiation load studies/mechanical integration ?
HTS design ( P3) ➜ shielding layout and impact on e+ capture efficiency. Field profile.
NC vs. SC solenoid for the capture section.
Electron and positron separation (where and how)
Mechanical layout (distances between the target/acc. structures) ➜ impact on acc. e+ yield
6D DR acceptance (how to apply at capture system)

## Slide 12: Before mid 2023
Baseline design of the positron source + capture system
  Comparison of FC-based CS vs. HTS-based CS
  Comparison of the e+ production schemes ?
  Comparison of the NC vs. SC solenoid around the acc. structures ?
  …