## Slide 1
Benchmark of the simulation tools for the FCC-ee positron source with SuperKEKB
Fahad A. ALHARTHI
fahad.alharthi@ijclab.in2p3.fr
Laboratoire de Physique des 2 Infinis Irène Joliot-Curie (IJCLab)
CNRS, Université Paris-Saclay
Many thanks to: I. Chaikovska, R. Chehab, V. Mytrochenko (IJCLab), A. Latina, Y. Zhao (CERN), M. Schaer (PSI), Y. Enomoto, F. Miyahara (KEK).

## Slide 2: Outline
SuperKEKB positron source.
Primary electron beam and Target design
Tracking with RF-Track
Positron beam and matching devise
Initial phase scans
Summary

## Slide 3: SuperKEKB positron source (currently in operation)
W target
BC (bridge coil)
FC (flux concentrator) head
LAS (large aperture S-band)
solenoid
Target material : W
Target size : Φ4 x 14
Inserted in the Cu block
W
hole
looking from downstream side
Electron drive beam: 3.5 GeV, 2 bunches/pulse, 10 nC, 50 (25) Hz
The highest intensity positron source
Positron source
1.1 GeV
Courtesy of Y. Enomoto (KEK)

## Slide 4: Benchmark of the FCC-ee code with SuperKEKB positron source
Initial particles GEANT4
Magnetic field
(FC,BC,DCSs) CST(provided*)
Accelerating structure Superfish (provided*)
Tracking
RF-Track
*Field maps are provided by SuperKEKB

## Slide 5: SuperKEKB primary electron parameters and positron beam distribution
1) Incident electrons (x, y, px, py, E)
N = 20000 (  Num. of loops )
Ekinetic = 2900 MeV (3.5 GeV was initial design)
(px,py)=(0,0)
x and y position are given by gaussian distribution Beam center: (x, y)=(0.2, 0) [cm] Beam size (sx, sy) = (0.05, 0.08) [cm] (sqrt(x2+y2) < 1.0)
z = -1.5 [cm]
e+ and e- data at target exit (z=0)
2) Time distribution at z=0
Gaussian distribution with FWHM=10 ps
FWHM = 2.355 = 4.2 ps = 1.26 mm
EGS5 : Electromagnetic reaction in the targe
Script
Positrons :
N(e+)/N(e-) =~6.3
Beam size (sx, sy) = (1.681, 1.724) [mm]
Bunch length (sz) = (4.2) [ps]
Gaussian distribution of the beam 6 sigmas (0 - 26) ps
F. Miyahara

## Slide 6: Geant4 simulation for SuperKEKB I
Target geometry :
Cu_Holder
W_Target
e-_Hole
Overlap checking
Detector

## Slide 7: Geant4 simulation for SuperKEKB II
Primary electron beam :
As expected part of the beam will hit the Cu_holder .

## Slide 8: Positron beam production (after the target )
Positron beam :
Positrons :
N(e+)/N(e-) =~6.1
Beam size (sx, sy) = (1.35, 1.42) [mm]
Bunch length (sz) = (4.25) [ps]
W => 61%
Cu => 39%
SuperKEKB N(e+)/N(e-) =~6.3
Target
e- hole

## Slide 9: Incident position of primary electron beam and positron Yield
Bunch length = 0
Ne- = 10k
Target center
FC center
SuperKEKB results

## Slide 10: SuperKEKB tracking in RF-track
2 mm
Target
FC
Duct1
Duct2
AC_151
AC_152
RF-Track is a new tracking code developed at CERN for the optimization of particle accelerators, which offers outstanding flexibility and rapid simulation speed.
*A. Latina, “RF-Track: Beam tracking in field maps including space-charge effects, features and benchmarks,” p. MOPRC016. 4 p, 2017. 28th Linear Accelerator Conference, East Lansing, Michigan, 25 - 30 Sep 2016.

## Slide 11: SuperKEKB Adiabatic Matching Devise (AMD)
AMD consists of : Flux concentrator (FC) + Bridge coil (Bc)
FC is placed with 2mm offset in the x-axis
2mm gap between the target and the FC
Target
e- hole

## Slide 12: SuperKEKB AMD + BC & Solenoid

## Slide 13: Positron tracking in the Adiabatic matching devise (RF-Track)
Positrons :
N(e+)/N(e-) ~3.2
Beam size (sx, sy) ~(9.98, 9.95) [mm]
Bunch length (sz) ~ (20) [ps]
SuperKEKB N(e+)/N(e-) =~3.1
Tracking is performed with the actual 3D magnetic field map in volume

## Slide 14: SuperKEKB tracking in RF-track
2 mm
Target
FC
Duct1
Duct2
AC_151
AC_152
AC_15_1, AC_15_2 : 12.56MV/m

## Slide 15: SuperKEKB Accelerating structure – Field map
Field maps:
3 cell cavity under Dirichlet and Neumann boundary condition.
Making 57 cells field map by arranging 19 of the 3-cell field map
2 cells as couplers, total cells/structure = 57+2 = 59
Two fields map provided : open & short :
Open = Neumann condition, Short = Dirichlet condition
1) GPT – analytical field: (trwlinac or trwlinbm)
2) Superfish – cylindrical symmetric field :
Dirichlet condition
Neumann condition
Neumann condition : Tangential electric field is zero (ET = 0)
Dirichlet condition : Tangential magnetic field is zero (HT = 0)
F. Miyahara

## Slide 16: SuperKEKB Ez field along the structure
The two field map combined using this formula :
E = Ez_open - i*Ez_short

## Slide 17: Initial phase scan
AC_15_1
Target exit
Send a single electron with energy 100 MeV at t=0 from the target. (px,py)=(0,0)
A = [0 0 0 0 0 100] => [x px y py s E]
F. Miyahara
24.21 deg
There is ~ 90 deg difference which could be due to the definition of the field map !

## Slide 18: Preliminary Phase scans for the first Accelerating structure(AC_151)
Scan the phase [0:10:350]
Good agreement in terms of the yield (Ne-/Ne+) and energy gain.

## Slide 19: Preliminary Phase scans for the second Accelerating structure(AC_152)
Since the particle is relativistic the phase of the second cavity is : fAC152=fAC151+Z.
Good agreement in terms of the yield (Ne-/Ne+) and energy gain.
Target exit

## Slide 20: Summary
Flexible Geant4 model (source , target , particle distribution …)
Good agreement between our model and SuperKEKB
Next step : perform the tracking until the end of capture section (~150 MeV).
Benchmark with the real experimental data.
By using the developed and validated simulation tools, start/continue the FCC-ee positron source design.
Positron yield is the main optimization parameter as for now (emittance , bunch length , energy spread ).

## Slide 21
Thank you !

## Slide 22
Backup

## Slide 23: Geant4 model for SuperKEKB
Positron beam:
Positrons :
N(e+)/N(e-) =~6.2
Beam size (sx, sy) = (1.591, 1.63) [mm]
Bunch length (sz) = (6.72) [ps]
As you can see there is a long tail in the time distribution which will affect the bunch length.

## Slide 24: Positrons summary :
Main reason for the difference ?
Parameters | SKEKB | G4 (no cut) | G4 (with cut)
Primary electrons bunch length | 0 | 1mm = 3.3 ps | 
Positron Yield | ~ 6.3 | ~6.2 | ~6.1
Beam size (sx, sy) [mm] | 1.681, 1.724 | 1.591, 1.63 | 1.35, 1.42
Bunch length (sz) [ps] | 4.2 | 6.72 | 4.25
Bunch length (sz) [mm] | 1.26 | 2.02 | 1.28
They are using zero value for the production cut which will lead to generate more positrons with Very low energy and high scatter angle, in my case I am using the default (gamma = e- = e+ = 700um = 990eV) .

## Slide 25
Results after the target:
Ne+/Ne- = 6.3
PEDD 27.5 J/g (3.5GeV)
Primary beam:
Ne-=10000
E = 2.9 GeV
Px,Py = 0
Sx=0.5mm ,Sy = 0.8mm
Beam center =(2 ,0,-15)mm
Gaussian Time distribution at z=0 with FWHM =10 ps
Magnetic Fields:
FC =3.5T ,BC = 1.25T, DCS = 0.4T
Front gap = 2mm End gap = 40mm
SuperKEKB positron source :
Results after AMD:
Ne+/Ne- = 3.1
AC_16 _1 - AC_16_4 : 14.292MV/m
AC_15_1, AC_15_2 : 12.56MV/m