## Slide 1: Radiation Load Studies for the FCC-ee Positron Source: AMD and Positron Linac
Barbara Humann (SY-STI-BMI)
Supervisor: Anton Lechner
FCCee Injector Studies Mini-Workshop
(25/11/2022)
Acknowledgments to I. Chaikovska, P. Craievich, M. Schär, Y. Zhao,…

## Slide 2: Agenda
Geometry
Beam Parameters
AMD
Positron Linac
Outlook & Conclusion

## Slide 3: Geometry
1) AMD
https://indico.cern.ch/event/1133621/contributions/4756873/attachments/2418347/4139305/FCC%20injector%20schematic%20layout%2031032022.pdf
2) Positron Linac

## Slide 4: Geometry – Adiabatic Matching Device (AMD)
Radial Coil Position | 6.1cm
Shielding thickness | 1.9cm
Target radial size | 1.5cm
Target position in z | 1.75cm
AMD exit in z | 10cm
Part | Material
Target | Tungsten
Coils | HTS (YBCO)
Cryostat | Stainless steel
Shielding | Tungsten
Support | Aluminum (grey)
Support | Copper (brown)
New:
Target and shielding are made from pure tungsten and in one piece
Thicker shielding  smallest aperture possible chosen
Facilitates cooling, better shielding effect
- Corrected magnetic field

## Slide 5: Geometry – Positron Linac
Self designed shielding (tungsten) to protect RF structure
RF entrance: z=26.6cm
5 cells, 44 cells each, copper
324cm per cell including VC, 297cm cavities (6.75cm per cavity)
Constant magnetic field of 0.5T in cavities
Aperture: 3cm, up to r=7cm
Solenoids: 13cm aperture  what will be in-between cavities and solenoids?
Concept of one long solenoid, 3 shorter ones
Copper with density taking in account the water cooling channels

## Slide 6: Parameters for the FCC-ee positron target
Electron drive beam | 6GeV
Beam size | 0.5mm RMS
Repetition rate | 200Hz
Bunches per pulse | 2
Bunch intensity (filling) | 3.47E10 (5.56nC)
Bunch intensity (top up) | 3.47E9
Beam Power | 13.34kW
Target length | 5X0=17.5mm
Filling time of collider:
2.4% filling from scratch
97.6% at top-up with 10% bunch charge
Current time scheme: needed for reliable dose and DPA values
(no difference between filling and top-up)
Old
(FCC-Week 2022)
New
100% filling with full bunch charge
2bunches*200Hz*3600s*24h*185days*0.804(duty factor)*3.47E10e-/bunch*0.5
e- on target per year: 8.9E19e-/year

## Slide 7: Measured quantities
Instantaneous effects
  Total deposited power (in W): Determines the heat load on the elements
  Power density (in mW/cm3): Quenching of SC if it is too high
Long term radiation effects
  Dose (in MGy): Deterioration of (organic) materials
  Displacement per atom (DPA): Structural damage of inorganic materials; Dimensionless number proportional to the number of Frenkel pairs
Frenkel Pair

## Slide 8: Adiabatic Matching Device Target

## Slide 9: Power on different AMD elements
 | 13.34kW | 3.43kW
Target | 3100W | 869W
Shielding | 1040W | 209W
Coils (1-5) | 0.6-2.9W | 0.27-1.25W
x3.5
x4.9
x3.9
4140W vs.1078W
x3.8
Smaller target, less increase (x3.5)
bigger shielding, more increase (x4.9)
Sum increases proportional (x3.9) to beam power (x3.9)
 Slightly different distribution but total power stays similar
Power Density - 13.34kW Beam power

## Slide 10: Close up on the target
Old
(FCC-Week 2022)
New
Shielding and target in one piece
Pure tungsten
Shielding: 1.5cm  2cm
Aperture: 2cm 1.5cm
Shielding
Target
80kW/cm3
8 DPA/year

## Slide 11: Power density on coils
30mW/cm3
Coils
Values ~3x higher than in old design due to 4x higher beam power.
Power density does not scale directly, due to thicker shielding protecting the coils better and a target position further downstream.
Should be safe considering HTS coils + strong gradient is favourable as well
FCC Week 2022:
up to 10mW/cm3
Coils - 13.34kW Beam power

## Slide 12
Remarks:
long term radiation effects (dose, DPA) are given for one year of Z operation.
Conservative assumption is that values will be ~10x higher for operational time of FCC-ee.
Long-term radiation effects per year of Z operation on coils
Up to 22MGy/year
Up to 2E-4 DPA/year
Dose and DPA values must be investigated if they can be considered as safe

## Slide 13: Positron Linac

## Slide 14: Geometry reminder
AMD
RF Shielding (10.5cm)
Waveguide
Solenoid long
Solenoid short
Cavities
Cell 1
5 cells with each 44 cavities (324cm per cell)
Solenoid connector

## Slide 15: Power loss on aperture in positron linac
Thanks to Y. Zhao for the RF Track values
As soon as particle leaves vacuum and touches a cavity/VC it is dumped, and its properties are stored
Good agreement in data means that FLUKA simulations should be sufficient for energy deposition studies, even with only a constant magnetic field of 0.5T and no electrical field.

## Slide 16: Power loss on aperture in positron linac
 | Electrons |  | Positrons |  | Photons |  | TOTAL | 
 | RF Track | Fluka | RF Track | Fluka | RF Track | Fluka | RF Track | Fluka
Total | 1154W | 1126W | 1037W | 1061W | 4830W | 4822W | 7021W | 7015W
Cell 1 | 1015W | 1026W | 913W | 967W | 3722W | 3721W | 5650W | 5721W
Cell 2 | 85W | 71W | 79.5W | 62.8W | 631W | 607W | 796W | 741W
Cell 3 | 24W | 16W | 23.5W | 19.7W | 265W | 261W | 313W | 297W
Cell 4 | 21.2W | 9.1W | 12.8W | 6.6W | 140W | 148W | 174W | 163W
Cell 5 | 8.8W | 3.4W | 7.9W | 4.1W | 71W | 83W | 88W | 90W
Values are generally in good agreement
Thanks to Y. Zhao for the RF Track values!
Impact on the aperture ≠ energy deposition

## Slide 17: Power deposition on different elements of the positron linac
 | 13.34kW
Shield RF | 1049W
Flange AMD/RF | 132W
Flanges cells | 43W-3.6W
SOL short | 68W*-3.6W
SOL long | 607W-12.66W
SOL connect | 53W-4.3W
First cell most impacted: up to 170W(!) absorbed by cavity
Cell 2 up to 20W per cavity
Shielding protects positron linac solenoids, but not the cavities
If cavities need more protection, elaborate shielding scheme must be elaborated
* Highest value in first short solenoid of cell 2

## Slide 18: Close up to first cell
Hottest spot: 5W/cm3, 3500MGy, 1.2E-3 DPA
Flange:
3.8W/cm3, 2800MGy,
1E-3 DPA
Solenoid: 0.25W/cm3, 35MGy/year (z=100cm), ~3.5E-5 DPA/year
Solenoid: 65MGy/year – shielding?
Organic materials in solenoid?
Which numbers are acceptable?

## Slide 19: Summary
AMD & Target:
  Coils: power density is below critical values, DPA and dose must be understood if they are acceptable
  Target: 13.34kW beam power leads to critically high heat load and DPA  solution pending
Positron Linac:
  Power loss: FLUKA results align well with RFTrack
  Cavities: highly impacted by particles from the inside, so shielding is not possible.
  Solenoids: Protected by large tungsten shielding in front of positron linac. In case of organic material and/or SC solenoid, dose values are too high.
  What power deposition values and DPA levels can the cavities withstand?

## Slide 20
Any questions?