## Slide 1: P3 status and beam dynamics updates
Nicolas Vallis & Riccardo Zennaro :: on behalf of the P3 Team :: Paul Scherrer Institute
Workshop on FCC-ee Injector Studies, IJCLab, 25.11.2022

## Slide 2: The 6 GeV Electron Beam of SwissFEL @ PSI
 | FCC-ee | SwissFEL |  | P3(*)
Beam energy | 6 GeV |  |  | 
RMS beam size | ~ 0.5 mm |  |  | 
Rep. rate | 200 Hz |  | 100 Hz | 1 Hz
Bunch charge | ~ 5 nC |  | 0.2 nC | 0.2 nC
Bunches/pulse | 2 |  | 2 | 1
(*) for radiation reasons we must limit the average beam current of P3
SwissFEL building has been designed to allocate a future beam line (Porthos)
Perfect location for P3

## Slide 3: Running the P3 Experiment in SwissFEL
P3 experiment
Porthos extraction line (Phase Planned)
EMI22+
P3 experiment requires the realization of two PSI projects:
EMI22+ (Erneuerung Modulatoren Injektor):
Production of new HV klystron modulators for the SwissFEL injector based on the technology developed for the PSI HV modulator currently used in for PolariX (X-band deflector).
Porthos extraction line (Phase Planned):
Installation of the initial part of the Porthos extraction line. Most components will remain in place for Porthos Final Phase.

## Slide 4: P3 Experiment
W Target  e+ generation
HTS solenoid (AMD)  Initial focusing of e+ beam
RF SW S-band structures  Acceleration
0.4 T 200 A NC Solenoids around RF accel. structures 
Confinement of beam in transverse direction
Broadband pickups  Resolution of particle bunches in time
Spectrometer dipole  Separation of e+ and e-
Faraday cups  Charge measurement

## Slide 5: HTS Solenoid as Adiabatic Matching Device (AMD)
HTS demonstrator developed at PSI (left)
    4 ReBCO (Rare-earth barium copper oxide) tape coils at 2kA
    Operation at 18.2 T, on-axis peak
    Temperature 20 – 30 K, no need of He cooling
Technical design of cryostat for P3 in development at PSI (right)
CW operation, ramp-up time of magnetic field ~ 2 days
HTS demonstrator at PSI
(M. Duda et al.)
Preliminary model of the AMD for P3
(H. Garcia Rodrigues)

## Slide 6: AMD design and procurements
2x cryocoolers RDK-500B 20K
ordered
2.8km HTS tape quotation received
ready to order
2kA power converter quotation received
ready to order
Cryostat thermal model ready
Mechanical design ready at end 2022

## Slide 7: Acc./bunching with RF S-Band SW cavities
Length | 1.2 m
RF Frequency | 2.9988 GHz
Gradient | ~ 18 MV/m
N cells | 21
Q-factor | 21600
R/L | 13.9 MOhm/m
Aperture | 40 mm
Mode Separation | 5.3 MHz (π mode)
Coupling factor | 2
Status:
Cups under production at VDL delivery March/April 2023
Brazing at PSI in May/June 2023

## Slide 8: RF cavity support study
Compact design
easy insertion/extraction of NC solenoids with small radius
Uncertainty in the correct Young’s modulus for heat-treated (830 °C) copper
Young's modulus: 60 GPa
Max. deformation 8 mm
Young's modulus: 10 GPa
Max. deformation 40 mm
Support alone
Max. deformation 5 mm
Courtesy of Mattia Schär

## Slide 9: Overview S-Band RF System
Nr | S-band Components | Qty | Units
1 | Splitter | 3 | Pieces
2 | H-bend | 14 | Pieces
3 | E-bend | 11 | Pieces
4 | Directional coupler | 3 | Pieces
5 | Window | 1 | Pieces
6 | Circulator | 1 | Pieces
7 | Pumping port | 4* or 18** | Pieces
8 | Phase shifter | 1 | Pieces
9 | Waveguides | 58687 | Length (mm)
About 59 m waveguides needed,
will be borrowed from CERN
* SF6 vs. ** Vacuum solution

## Slide 10: P3 Experiment, S-Band RF Network
Pumping port
Phase shifter
Directional coupler
Accelerating structure
Compact and low waveguide layout to provide the possibility to add shielding on top
The full experiment will be mounted on the girder outside the SwissFEL tunnel

## Slide 11: P³ Bunker
Side wall
Chicane will be mounted at the end, really needed?

## Slide 12: Radiation and shielding study
Neutrons
Photons
Above the roof (including 0.4 m soil)
Limit 0.5 mSv/h
Limit 1 mSv/h (Tunnel)
Main critically: radiation above the roof
Values for 0.2 pC/bunch 1 Hz, 1 bunch/ pulse
Probably no need of chicane
Courtesy of I. Besana
Next step:
Study of the possibility to install the fast scope and solenoid power supply in the tunnel next to the experiment

## Slide 13: Time Schedule
Q3 2025 Start of the experiment
Q1 2025 cooling water and electricity available to start:
klystron/modulator commissioning (technical gallery)
beam line commissioning (tunnel)
2023-2024 Aramis modification and Porthos installation, new girder under production, quadrupoles ordered, dipole yoke modification planned
Very limited resources from service groups

## Slide 14: Broadband Pick-Ups
BBPs measure time structure of the beam after second cavity.
Very broad band required to differentiate e+ and e- bunches, separated ~167 ps.
Based on SuperKEKB factory diagnostics [1].
e+
e-
4 Pick-Ups
[1] T. Suwada et al., "First simultaneous detection of electron and positron bunches at the positron capture section of the SuperKEKB factory", Sci. Rep., vol. 11, 2011.

## Slide 15: Broadband Pick-Ups 2
A gaussian approximation of the main e+ bunch is simulated with CST wakefield solver over vacuum chamber.
Pick-up geometry optimized:
    Maximum peak voltage
    Minimum signal tail

## Slide 16: Broadband Pick-Ups 3
Feedthrough from Allectra GmbH
First hardware tested for P3
Large bandwidth
(S11<-20 dB 0-20 GHz)

## Slide 17: Faraday Cups
Measurement of e+ and e- charge separately.
Alluminum FCs at 25 Ohm. Matching to 50 Ohm through 2 parallel coax cables
Negligible electron backscattering
B
e+
e-
● e+ ● e-
Current dimensions of diagnostics chamber.
e+e- beam at faraday cups

## Slide 18: Spectrometer and energy spectrum
Dipole strength scanned to measure e+ energy profile
e+ at different pz detected by scintillating fiber
Test/calibration of the Fiber Q2 next year at the Swiss Federal Institute of metrology (METAS)
Pz spectrum reconstruction
e+
B
Scintillating fiber
Schematic of energy spectrum measurement

## Slide 19: Implementation of NC Solenoids
 | P3 (SC) | P3 (NC)
Ee- [GeV] | 6 | 6
Cavity aperture [mm] | 40 | 40
B0 [T] | 12.7 | 12.7
Bs [T] | 1.5 | 0.4
Estimated Yield at DR | Up to 8.0 | Up to 3.69
Superconducting (NbTi, 1.5 T)
Normal Conducting (Copper, 0.4 T)

## Slide 20: Implementation of NC Solenoids 2
Implementation of NC solenoids is a turning point in the design:
    Yield at DR decrease
    Re-adjustment of most experiment parameters, particularly the beam diagnostics section (e.g. faraday cup & pick-up dimensions, dipole reference field, etc.)
New parameter optimization, work in progress:
    Geant4 simulations at target
    Transverse beam dynamics: Theoretical and simulation of the AMD
    Longitudinal beam dynamics: Study of RF phase working points

## Slide 21: Estimation of Yield at DR
~0 – 200 MeV: ASTRA particle tracking over 10 RF Cavities.
    Phases of 2 first cavities are free parameters
    Rest of 8 cavities on crest
~200 MeV – 1.54 GeV:
    Electron removal at 200 MeV
    Analytical transformation of positron distribution up to 1.54 GeV.
1.54 GeV: DR acceptance window.
    +-3.8 % in energy
    One RF bucket length (+- 5 cm) in z
E
+/- 3.8 %
λ
1.54 GeV
Impression of the a e+ beam at entrance of DR
and DR acceptance window

## Slide 22: Yield at DR
(-160, 0)
(-90, -120)
(-160, 0): Preferred working point
(-90, -120): Max. Yield.

## Slide 23: (-160, 0): Preferred
 | Yield at DR | 3.34 | 3.69 | 
@ 200 MeV | Capture efficiency | 27.46 | 30.89 | %
 | Energy Spread | 36.93 | 40.73 | MeV
 | Norm. emittance | 5181 | 5133 | pi mm mrad
(-90, -120): Max. Yield

## Slide 24: (-90, -120): Max. Yield at DR
e+ and e- completely overlapped!
Low energy

## Slide 25: (-160, 0): Preferred working point
Excellent bunching
But first bunch very close!
High center-of-bunch energy
Reasoably high capt. efficiency

## Slide 26: Recap
(-160, 0): Preferred
(-90, -120): Max. Yield
RF phase scan combined with BBP measurements can provide a direct observation of the positron capture.
Several issues to be considered in BBP design:
    First and second bunches can be very close to each other
    Overlapping of e+ and e- can happen.