## Slide 1: PERLE France Meeting
PERLE beam dynamics status

## Slide 2: PERLE France Meeting
Injector design
  Injector : from RF gun to booster
  Merger : from booster to PERLE
PERLE lattice and design
  Global architecture
  Optimization and matching
Beam dynamics studies
  Tools developed
  Effects investigated

## Slide 3: PERLE injector purpose and specifications
The injector is the link between the source and the machine
It should match the Perle specifications initially set at :
Photocathode
Booster
350 keV
eGun
Injector
Merger
PERLE
Emittance | Bunch charge | Rep. rate | Current | RMS bunch lenght | Total inj. energy
<6mm.mrad | 500 pC | 40.1 MHz | 20 mA | 3 mm | 7 MeV
7 MeV

## Slide 4: Alice Photoinjector
POISSON mesh
Field map
Original alice gun
Upgrade alice gun
Optimized alice gun
Original gun under installation at IJCLab
R. Roux
M. Baylac
D. Reynet

## Slide 5: 4 possible injector designs : from Ben Hounsell’s PhD thesis
As all designs seem to meet the specifications, only Baseline design has been studied (for now)
Studies by F. Bouly (LPSC), J. Michaud (IJCLab), R. Roux (IJCLab)
:DC Egun
(350kV)
:Solenoid
:NC RF cavity
(buncher)
:SC RF cavity
(booster)
Elements :

## Slide 6: Injector Fields and energy
Egun
Buncher
Booster
Solenoid
Solenoid

## Slide 7: Machine parameters
Elem. attribute | Value
Egun Voltage | 350 kV
Egun laser freq. | 40 MHz
Bunch charge | 500 pC
Solenoid 1 field | 0.0323 T
Buncher Field | 1,305 MV/m
Buncher freq | 801 MHz
Solenoid 2 field | 0.0238 T
Booster field | 20.8/24.0/14.4/11.7 MV/m
Booster freq | 801 MHz
Spec | Value
Transverse emittance | <6mm.mrad
Bunch charge | 500 pC
Bunch freq | 40 MHz
Beam current | 20 mA
RMS bunch lenght | 3 mm
Total inj. energy | 801 MHz
Current injector design
meets Perle specification
Specifications initially given for Perle
might not be totally fixed :
This will depend on full start-to-end Perle tracking
(Especially bunch lenght and energy spread)
Reducing one value might mean, increasing another quantity
 Design of injector is not totally fixed yet (fields amplitudes, elements positions…)

## Slide 8: Working plan for injector
Booster and injector needs to be consolidated
Implementation of 3D field maps
« M-shape » has to be controlled according to ERL recquirements
Beam dynamics design has to be accorded to real elements :
  New buncher design
  Cryomodule design
  Cavity independently powered (Tbd)
Integration of the full beamline:
  Steerers
  Beam diagnostics (test bench) positions and recquirements have to be defined
‘M-shape’
Longitudinal beam distribution at the Booster exit Ek = 6.5 MeV
Need of simple, robust design and efficient tuning procedure
To do so : benchmark with different codes
  OPAL (J. Michaud) : Code used for original design by B. Hounsell. Does 3D tracking including collective effects
  ASTRA (R. Roux) : Powerful code using field maps including space charge
  TraceWin (F. Bouly) : Well known code @IN2P3. Envelope and tracking including field maps and space charge. Need to be tested for electrons.

## Slide 9: From the beam point of vue
Transverse phase space (x-px)
Longitudinal phase space (z-pz)
Solenoids focus beam in transverse plans
Buncher focus beam in longitudinal
M shape in z-pz axis at the end of injector : could be a problem

## Slide 10: 4 different merger design (from B. Hounsell PhD thesis)
Merger : Matching the injector beam to the eigen-ellipse of PERLE
Studies by B. Jacquot (GANIL)
Constraints :
  Compact: not a big constraint.
  Achromaticity: avoid emittance increase
Circulating beam perturbation to be considerer:
  Transverse matching to be done with minimal number of quadrupoles in ring
  Flexibility: various injector conditions

## Slide 11: The 2 simplest mergers : UBEND and SBEND
UBEND
SBEND (dogleg)
Matching : OK for the two geometries
UBEND is the simplest (7 quads) : solution preferred 2x 22,5° (Bend ~ 15cm)
SBEND (10 quads required) could be preferred for building consideration (parallel to the ring)
Deal with the circulating beam perturbation (influence of « re-injection chicane) :
  With 22.5° magnet : 83MeV beam  Dx’ ~ 33 mrad
  166MeV beam  Dx’~ 17 mrad
  250MeV beam  Dx’~ 11 mrad
Quads n° : 2 quads in ring and 4 quads after 7MeV booster needed
7 MeV
250 MeV

## Slide 12: Injector : conclusion
Injector design and associated files transmitted to us by Nov. 2022
  Input files for simulations
  Field maps
  Thesis of Ben Hounsell
Simulations of :
  Injector with different codes : OPAL (J. Michaud), ASTRA (R. Roux), TRACEWIN (F. Bouly)
  Merger by B. Jacquot
Degrees of freedom for specification matching : laser pulse lenght, laser spot size, buncher/booster voltages/phases.
Simulations of Perle show that a 3mm bunch lenght might be too long (unstability during deceleration)
   necessity to investigate for shorter bunch lenght (2mm)

## Slide 13: PERLE France Meeting
Injector design
  Injector : from RF gun to booster
  Merger : from booster to PERLE
PERLE lattice and design
  Global architecture
  Optimization and matching
Beam dynamics studies
  Tools developed
  Effects investigated

## Slide 14: Two models studied
250 MeV version :
3 energies -> 6 arcs
1 linac
1 spreader ; 1 merger
3 straight sections
500 MeV version :
6 energies -> 6 arcs
2 linac
2 spreader ; 2 merger
Images and design (250MeV) by Alex Fomin
Arcs are identical : reduction of immediate expenses and construction time :
1 (of 2) cryomodules, 60 (78) dipoles and 136 (148) quads)
Fields in quads are consistant with current design (no saturation)

## Slide 15: Lattice parameters : 250 MeV version

## Slide 16: Stacking effect on 250 MeV lattice – longitudinal emittance
Injection
Post-linac
Spreader
Middle arc1
End arc 1
Str section
Arc 2
Merger
Lack of symmetry (lack of 1 spreader and 1 merger) in 250MeV lattice creates stacking effect.
 Can be corrected by closing term M56 (momentum compaction factor)

## Slide 17: Optimization objectives
What needs to be tuned :
What can we play on :
Twiss functions stable over all linacs
Merger output :
initial twiss functions
- K1 gradient of quads in spreader
(7 quads families)
- K1 gradient of quads in arcs
(11 quads families)

## Slide 18: Filling pattern (Alex Fomin)

## Slide 21: PERLE France Meeting
Injector design
  Injector : from RF gun to booster
  Merger : from booster to PERLE
PERLE lattice and design
    Global architecture
    Optimization and matching
Beam dynamics studies
  Tools developed
  Effects investigated

## Slide 22: Beam dynamics in CODAL
PhD work of Coline Guyot :
Analytical model implemented in CODAL
Benchmarked with field maps (ASTRA)
Transverse particle motion in radiofrequency linear accelerators
J. Rosenzweig (UCLA), L. Serafini (Milan U.)

## Slide 23: Code benchmarking : LINAC transverse dynamics
BMAD
CODAL/ASTRA
Coline Guyot
BMAD, ASTRA & CODAL agree on 6D Linac dynamics
Actually, dynamics equations from the same publication !

## Slide 24: Bunch lenght 3mm or 1,4mm (250 MeV)
3mm bunch lenght
1,4mm bunch lenght
z/pz
x/px
BMAD simulations (high order tracking, no collective effects)
Studies showned by Kevin Andre :
Single and multi-bunch tracking for PERLE (Kevin Andre talk at
PERLE collaboration meeting 16/07/21)
“So far the issue is the RF curvature for 3 mm bunch length more than the CSR even for 1.4 mm bunch length”.
Migh reconsider initial spec of
3mm bunch lenght for the injector
Possible solutions :
Play with off-crest phase advance in linac
Sextupoles

## Slide 25: Transverse beam size
Transverse beam size stable
for a 1,4mm beam
Transverse beam size unstable after deceleration
for a 3mm beam
Preliminary simulations (BMAD) show a limit at ~2 - 2,5mm bunch lenght
(CSR and collective effects not included yet)

## Slide 26: Conclusion
Lattice design is now fully finalised :
  Reference trajectory and envelops
  Dispersion closed
  Twiss parameters stable/symetric
  Momentum compaction factor stable
  Filling patterns
Tools developed/benchmarked :
  Numerical tool for multiturn and collective effects is ready (PhD work of C. Guyot)
  BMAD simulations ready : CSR, space charge, linac dynamics benchmarked, lattice matched
Next steps :
  Start-to-end multiturn tracking (bunches of many particles)
  Include collective effects (space charge, CSR…) in simulations
  Higher-order optics (sextupoles…)
  Everything should be tuned finely : e-spread, chirp…
  Injector parameters should be re-defined from these studies (especially bunch lenght)
Other studies ongoing:
  Misalgnments & magnet studies by Rasha
  Halo formation and beam loss (Master student – Belgium, Lode Vanhecke)
  Diagnostics integration in lattice : all activities in proximity with WP diags
  PTC under investigation (linac dynamics)

## Slide 27
Thank you !
WP02 : Accelerator design members at IN2P3
Coordinator : Luc Perrot
PERLE beam dynamics:
R. Abukeshek, A. Fomin, C. Guyot (supervisor : C. Bruni), J. Michaud, L. Perrot
Injector and merger:
F. Bouly, B. Jacquot, J. Michaud, R. Roux

## Slide 28: Try to play with different parameters
Buncher focal point
Beam size fixed (v = c)
Exemple : effect of eGun laser pulse lenght on the beam :
RMS bunch lenght
Transverse emittance

## Slide 30: Step 3 : Full passes (Linacs only) matching
Inject final twiss as initial conditions : a good (1st) guess but not totally stable
Not stable (high betas)
Stable (minimum Betas)
Adjust init. twiss

## Slide 31: Momentum compaction (R56 term)
Not closed for 250 MeV lattice ( because of lack of merger)
Match R56 = 0 on :
  End arc1
  End merger 1
  End arc3
  …
Additional conditions:
Disp x & y =0 (end arcs)
Disp’ x & y = 0 (end arcs)
Alpha x & y = 0 (center arcs)
Alpha x & y = 0 (center strs)
Need to cancel at injection