## Slide 1: E-TEST : Einstein Telescope EMR Site and Technology
Rasa Jamshidi
Precision Mechatronic Group (PML)
2nd Einstein Telescope Annual Meeting: Nov. 14, 2023 -- Nov. 16, 2023

## Slide 2
E-TEST objectives
Large mirror (100 Kg)
Cryogenic temperature (10-20 K)
Isolated at low frequency (0.1-10 Hz)
Compact suspension (4.5 meters)
E-TEST feasibility strategy
E-TEST is a project funded by the Interreg Euregio Meuse-Rhine and ET2SME consortium, which allow us to capitalize on existing infrastructure at Centre Spatial Liège (CSL) for the construction of the facility.

## Slide 3
Prototype E-TEST
Liège Space Center
Hybrid (active + passive) isolation
Radiative cooling

## Slide 4
Vibration isolator
1) GAS filter
2) Inverted Pendulum (IP) platform
3) Marionette
4) IP legs
10) Active platform
Cryogenic payload
5) Heat exchanger and
cold platform
7) 25K inner thermal shield
8) 80K outer thermal shield
Submitted: 12/2021
Revised: 03/2022

## Slide 5
Mechanical design state-of-the-art
Production drawings of the whole prototype finished!
All mechanical parts in production
Start assembly in May 2023
Contact: Ameer Sider (PML)
asider@uliege.be
r.jamshidi@uliege.be

## Slide 6
Cryostat development
Outer cryostat
(connected to the vacuum chamber):
80K LN2 shield (brown)
25K GHe panels (green)
Inner cryostat
suspended and conductively linked to the silicon mirror
overall dimensions: 1.8 x 1.6 x 2 m3
conventional radiator design with horizontal fins (25K)
three 30-mm diameter optical feedthroughs towards the mirror
radiation heat transfer for mirror cooling
Contact: Cedric Lenaerts (CSL)
Cedric.Lenaerts@uliege.be

## Slide 7
Ultra-cold vibration control
single crystal
Si suspension rods
Crucial technology aspect for ET: no proven solution exists
Four machined samples delivered
Crystalline silicon mirror suspension
⦰ 3-mm
All samples, including the new ones with bonding flats, sent to Università di Perugia for mechanical loss vs T and tensile strength measurements
ET2SME partners Mat-Tech (NL) and MaTecK (D) will do R&D on Si-metal interfaces
Al-6061 dummy mirror
Bonding flat
Contact: Alessandro Bertolini (Nikhef)
alberto@nikhef.nl

## Slide 8
Ultra-cold vibration control
Inertial sensors development for active seismic attenuation at low frequency
Laboratory prototype is getting turned into its final design
Production drawings in progress; manufacturing starting in the coming weeks
Vertical sensor prototype
Horizontal sensor
Vertical sensor
Anthony Amorosi (PML)
Anthony.Amorosi@uliege.be
Loïc Amez-Droz (PML)
lamezdroz@uliege.be

## Slide 9: Final validation of the prototype
Tests at CSL timeline:
2023: with dummy Al mirror
2024: with 100kg Si mirror
White light interferometry (residual stress)
Temperature measurement
Quality factor

## Slide 10: E-Test Assembly Procedure
Active Platform

## Slide 11
Active Platform

## Slide 12
Active Platform

## Slide 13
Top Platform
Safety Tubes & Legs & Inner Cryostat

## Slide 14
Top Platform on Legs
Mirror Suspension & Cryostat

## Slide 15
Inertial sensors
Bossem & Actutor

## Slide 18
Contacts:
Prof. Christophe Collette
Christophe.Collette@uliege.be
Dr. Rasa Jamshidi
rjamshidi@uliege.be
Useful links:
TDR
https://arxiv.org/abs/2212.10083
E-TEST Project website
https://www.etest-emr.eu/
PML website
http://www.pmlab.be/