## Slide 1
Measurement of 35Cl(n,p) Cross Section at NPL in the Energy Range 0.5 – 5 MeV
D. Smith, Pablo Torres, A. Bennet, M. Birch, M. Bunce, N. Florea, S. Kolmogorova, G. Lorusso, H. Mahmood, J. Mewburn, J. Praena, G. Taylor, D. Tofan, and T. Wright

## Slide 2
Molten Salt Reactors and the need for 35Cl(n,p)35S data
Pros:
Fuel can be drained
Operation at atmospheric pressure
High temperature ≈700˚
Kr/Xe gas bubbles out
Refuel while operating
Cons:
Molten salt is corrosive
Sensitive to neutron transmutation
keff uncertainty < 300 pcm
(currently due to 35Cl(n,p)35S is ~1000 pcm)
High priority list of the Nuclear Energy Agency (NEA)

## Slide 3
Discrepancies among models
Discrepancies between models and experiment
Evaluations are poorly constrained
ENDF/B-VIII
EAF-2010
Cross section for σ (n,p)

## Slide 4
Sharp cut between resonant and non-resonant cross section obviously an artefact
Experimental resonances broader than from models  density of state included is too small
Discrepancy with Batchelder 2019 measurement
S. A. Kuvin et al., PRC 102, 024623 (2020)
LANL spallation neutron source using the LENZ experimental setup
35Cl(n,p)35S recent measurement at LANL

## Slide 5
Positive Ion Accelerator – Protons, deuterons and tritons
Produces a stable and controllable beam over wide range of energies – 1.0 – 3.5 M V
Producing free neutrons with various nuclear reactions
3.5 MeV Van De Graff
Energy (MeV) | Reaction | Fluence (cm2s-1)
0.144 | 7LI (p,n) 7Be | 1 102
0.250 | 7LI (p,n) 7Be | 6 102
0.565 | 7LI (p,n) 7Be | 1.6 103
1.2 | T (p,n) 9He | 2 102
2.5 | T (p,n) 9He | 6 102
5.0 | D (d,n) 9He | 6 102
16.5 | T(d,n)4He | 4.5 102
neutron fluence @ 1 m
Neutron fluences are measured using a BF3 long counter
NPL Chadwick building
Van de Graaff electrostatic particle accelerator

## Slide 6
Low neutron scattering (area size 18m x 18m x 26m)
Well know fluence from well calibrated long counter allows for absolute cross section measurements
Downstream view
Upstream view
NPL monoenergetic neutron facility

## Slide 7
Proton beam axis rotates (50Hz)
1 cm
Neutron source distribution
Absolute measurement difficult
Large relative uncertainty of target distance
Stability of beam position is unknown
Profile of the beam is unknown
This data is an opportunity to study the feasibility of absolute cross section at NPL at short range
Beam spot
Fluence measurement at ~ 1 m with BF3 long counter
Heat load management (T<180˚)
Neutron fluence measurement
Cai Dunjiu, evaluation of cross section for dosimetry reactions, IAEA report, 1991, IMDC(CPR)-024
115In(n,n’)115mI cross section as standard reference
318.5 +/- 1.7 mb
@ 5 MeV

## Slide 8
Activation measurement using the InCl3 target
compressed air hose
Deuterium target 50 μg/cm2
proton beam
InCl3 target
~500 mg InCl3
Encapsulated in quartz crystal in Argon
Pressed sample fabricated at Target Preparation Laboratory IFIN-HH
Held at approx. 1.5 cm distance from target
FISPACT-II calculations
114mIn, T1/2 = 49.5 d
but low abundance of 113In
115Cd, T1/2 = 53.5 h
115mCd ,T1/2 = 44.5 d
but low (n,p) cross section
natCl  35Cl + 37Cl
5 hour irradiation test Dec23

## Slide 9
γ ray spectroscopy
96512 counts in 8600 s  A ≈150 Bq
(γ- efficiency needs to be measured)  will achieve <1% uncertainty
No evidence of 114mIn and 115,115mCd
HPGe of the NPL g-spec lab
336 keV
113mIn, 115mIn, 116mIn
KeV
Counts / keV
115In(n,n’)115mIn
114mIn  190, 311 keV
115Cd  336.2 keV, 527 keV
115mCd  no strong γ-rays
114mIn
115mCd
Contamination analysis can be improved running after 115mIn decay

## Slide 10
Liquid scintillation counting (detecting 35P &32S)
Scintillation Cocktail (Aqualight + NPE Free scintillant)
60-99% by volume is solvent + solubiliser
Primary fluor – Most primary fluor emit light in the UV range with wavelengths shorter than 400 nm.
Secondary fluor (wave shifter) –increases the wavelength of the emitted light to one more efficiently absorbed by the PMT.
High counting efficiency (99.8 % 32P and 91% 35S)
No backscatter
Passive/active shield  Low background
Coincidence counting  low noise
Well suited to accurate measurement of low activity pure beta emitters
PMT 2
PMT 1
Low 39,41K borosilicate vial

## Slide 11
Liquid scintillation measurements
2 samples InCl3 made into 0.5 g solution
1 sample of cocktail with HCl for background
Counting time 720 min (BKG, sample #1, sample #2)
Background
Activity after irradiation
A(32P) = 3.02(4) Bq
A(35S) = 0.640(16) Bq
32P
PMT pulse high spectrum
35S
Sample 1
Bkg

## Slide 12
Preliminary result  σ(n,p) relative to σENDF(n,α)
decay during irradiation
decay before LS measurement
35Cl(n, α)32P
35Cl(n, p)35S
= 154 (25) mb @ 5 MeV
(n,p0)+(n,p1)+ (n,p2)+ (n,p3)+ (n,p4)+ (n,p5)
C() = 175(5) mb
S. A. Kuvin (2020)
= 135 mb @ 5 MeV (ENDF/B-VIII)
S. A. Kuvin (2020)

## Slide 13
Summary
35Cl(n,p)35S cross section measurement is ongoing at NPL as part of ARIEL
First test run in December 2023 at NPL has provided data to optimising the measurement
Preliminary data shows compatibility with Kuvin et al., with potential to reduce the uncertainty
New irradiations at different energies are scheduled in February 2024
Target optimisation (thickness)
Redesign target holder
Characterise target distance