## Slide 1: Assessment of the feasibility of measuring neutron-induced reactions at a laser-driven neutron beam
ARIEL FINAL WORKSHOP (IJC Lab, Orsay, France)
17 - 19 JANUARY 2024
M. A. Millán-Callado1,2,*, C. Guerrero1,2, A. Alejo3, S. Assenbaum5, J. Benlliure3, R. Beyer4, B. Fernández2,
E. Griesmayer6,7,8, A. R. Junghans4, J. Kohl9, F. Kroll5, I. Prencipe5, J. M. Quesada1, C. Rödel9,
T. Rodríguez-González1,2, S. Scheuren9, U. Schramm5, S. Urlass4, C. Weiss6,8 and K. Zeil5
  1 Dpt. Física Atómica, Molecular y Nuclear (FAMN), Facultad de Física. Universidad de Sevilla (US), Sevilla, Spain.
  2 Centro Nacional de Aceleradores (CNA, US - Junta de Andalucía – CSIC), Sevilla, Spain.
  3 Instituto Galego de Física de Altas Enerxías, Universidad de Santiago de Compostela (IGFAE-USC), Santiago de Compostela, Spain.
  4 Institute of Radiation Physics, Dpt. Nuclear Physics, Helmholtz-Zentrum Dresden-Rosendorf (HZDR), Dresden, Germany.
  5 Institute of Radiation Physics, Dpt. Laser Particle Acceleration, Helmholtz-Zentrum Dresden-Rosendorf (HZDR), Dresden, Germany.
  6 CIVIDEC Instrumentation GmbH, Wien, Austria.
  7 Faculty of Electrical Engineering and Information Technology, Technische Universität Wien, Wien, Austria.
  8 Atominstitut, Technische Universität Wien, Wien, Austria.
  9 Institute for Nuclear Physics, Technische Universität Darmstadt, Darmstadt, Germany.

## Slide 2: 1.INTRODUCTION
COMPACT NEUTRON SOURCES AND LASER ACCELERATION

## Slide 3: NEED FOR SMALL-SCALE NEUTRON SOURCES
Image credit: F. Gunsing and then_TOF collaboration
Restricted transfer of knowledge outside a research center.
Not exploited to their full capacity.
Limited availability
Huge size and complexity of conventional high intensity neutron sources.
Progressive shut down of research reactors.
WHY?
EAR1 @200 m
1,4 GeV
Booster
20 GeV PS
50 MeV Linac
n_TOF@CERN spallation source Accelerators chain extended for about 1 km
Collaboration > 30 institutions

## Slide 4
“
”
There is a general belief […] that neutron methods are an emerging technique and not exploited to their full capacity. This is partly due to the fact that useful neutron beams can only be generated at advanced research reactors and/or high energy neutron spallation sources.
- IAEA-TECDOC-1439, Development opportunities for small scale accelerator driven neutron sources, Report of a technical meeting, Vienna, 18-21 May 2004

## Slide 5: LASER-DRIVEN NEUTRON SOURCES
PW Laser VEGA@CLPU (Salamanca, SPAIN)
World-class table-top lasers:
Short pulse duration (few fs)
High repetition rate, typically 1-10 Hz
High power (~PW range)
Intensities exceeding 1021 W/cm2
Technology in fast development  Next generation of multi-PW lasers (up to 10 PW) under construction (about 1 shot/minute)
CPA PRINCIPLE

## Slide 6: LASER-DRIVEN NEUTRON SOURCES: TARGET NORMAL SHEATH ACCELERATION (TNSA)

## Slide 7: LASER-DRIVEN NEUTRON SOURCES: PITCHER-CATHER SETUP
Brack, FE., Kroll, F., Gaus, L. et al. Spectral and spatial shaping of laser-driven proton beams using a pulsed high-field magnet beamline. Sci Rep. 10, 9118 (2020). https://doi.org/10.1038/s41598-020-65775-7

## Slide 8: LASER-DRIVEN NEUTRON SOURCES: STATE-OF-THE-ART
Neutrons per pulse of a laser-driven neutron source vs laser intensity. – Roth, M. et al. Los Alamos National Lab. (LANL) Technical Report. LA-UR-17-23190. (2017). https://doi.org/10.2172/1352436
Neutron flux based in M. Roth, et al. results from 2013 experiments at TRIDENT PW Laser System. (80 J, 600 fs, 1021 W/cm2). 1 m of flight path and 10 Hz are supposed.
C. Guerrero et al. Eur. Phys. J. A, 53, 87 (2017). https://doi.org/10.1140/epja/i2017-12261-2

## Slide 9: 2.DRACO@HZDR (LDNS)
FEASIBILITY STUDY OF NUCLEAR PHYSICS EXPERIMENTS

## Slide 10: EXPERIMETAL CAMPAIGN AT DRACO@HZDR (DRESDEN, GERMANY)
Establishing a link between the laser acceleration community and the neutron-users community.
Performing a series of experiments at a laser facility to produce and characterize the neutron beam resulting from laser-driven ion beams.
Analyzing the response of the different nuclear physics detectors in this new environment.
Assessing the suitability of laser-driven neutron beams for nuclear physics experiments.
DRACO@HZDR
PW-class 30 J Laser System (18 J on target)
30 fs laser pulse / ~ps ion pulse
Up to 1 Hz (compressor) (~ 1 shot/minute during the experiment)
~200 shots/day
HZDR hosts both the nELBE neutron facility and the DRACO laser facility, a combination of facilities that make it the best suited research center for the purpose discussed herein
.

## Slide 11: “PITCHER-CATCHER” NEUTRON PRODUCTION SETUP
Pitcher-Catcher Setup
Pitcher Targets
~200 nm formvar
Catcher Targets
25 mm LiF
Beamdump
60 mm PE
3 mm Cu
~ 180 nm deuterated polystyrene
~ 180 nm polystyrene

## Slide 12: ION DIAGNOSTICS
LASER DIAGNOSTICS
Electron spectrometers: Plasma characteristics and the acceleration mechanism.
Bremsstrahlung spectrometer (BS): γ-ray background
Electron lanex in the specular direction: Target focus
ION BEAM DIAGNOSTICS
Proton profiler: Spatial distribution and alignment of the ion beam in the catcher.
Proton frontside spectrometer: Backwards ion beam energy distribution.
Thomson Parabola Spectrometer (TPS): Shot-to-shot ion beam energy spectrum calibrated for the number of particles.
Radiochromic film (RCF) stacks: Integral double differential (in energy and angle) proton production per shot.

## Slide 13: ION SOURCE CHARACTERIZATION: RCF STACK
Data provided from a previous characterization campaign of the proton source  Used as a reference proton shot.
5 · 1011 p/shot & 20° divergence

## Slide 14: ION SOURCE CHARACTERIZATION: THOMSON PARABOLA SPECTROMETER
H+
Neutrals
ECut-off
Cn+
MCP Image
Ep (MeV)
LANEX Image
Cn+
H+
Neutrals
Ep (MeV)
Spectrum
TNSA analytical spectrum fit
Proton profiler

## Slide 15: ION SOURCE STABILITY
Source stable shot-to-shot 20-30%
But
Up to x2 difference between days

## Slide 16: NEUTRON DETECTION SETUP
Neutron detectors Setup
Scintillators
2 x EJ200 (US)
Particle detectors
EJ232Q (USC)
2 x diamond detector (CIVIDEC + HZDR)
Passive detectors
EJ232Q + Gated PMT (HZDR)
13 x Bubble detectors (TUD + USC)

## Slide 17: NEUTRON PRODUCTION: BUBBLE DETECTORS
Bubbles detectors distribution (in different runs):
In the chamber wall, at 0º, ±22,5º, ± 45º, ± 67,5º, ± 90º, ± 112,5º, 135º, 157,5º (from the proton line).
~ 8(3)·108 neutrons*/shot
* Assuming isotropic production
Nb  Number of bubbles.
C (bubbles/rem)  Calibration factor (given by the manufacturer).
S = 3,5 · 105 bubbles/(n·cm2) correction factor
L2 (cm)  Distance to the neutron source

## Slide 18: BACKGROUND SIMULATIONS
Direct component: 50-40% for the bubbles
PHITS simulations  S. Scheuren (TUD) PhD thesis.
BUBBLE DETECTOR AT 0º

## Slide 19: SINGLE-EVENT DETECTORS (DIAMONDS)
For fast neutrons detection
Low sensitive to gammas.  Small shielding needed.
Fast response (sub ns rise time) and small size  Fast recovery after saturation.
Sensitive to charged particles in (n,chp) reactions.  Suitable for nuclear physics measurements
Need of a high repetition source  Typical of neutron physics exp. but limited in lasers
Operated with a 2 GHz Broadband Amplifier (low-noise)

## Slide 20: SINGLE-EVENT DETECTORS (DIAMONDS)
For fast neutrons detection
Low sensitive to gammas.  Small shielding needed.
Fast response (sub ns rise time) and small size  Fast recovery after saturation.
Sensitive to charged particles in (n,chp) reactions.  Suitable for nuclear physics measurements
Need of a high repetition source  Typical of neutron physics exp. but limited in lasers
Operated with a 2 GHz Broadband Amplifier (low-noise)

## Slide 21: SIGNAL ANALYSIS ALGORITHM
Substration of the oscilating average baseline
Definition of the gamma flash temporal threshold (set to 20 ns)
Threshold in amplitude Ampth to find signal candidates
Define signal parameters: Ampmax, FWHM, t30
Define signal limits  No signal detected until the previous one ends
Define the individual signal baseline
Recalculate signal parameters from the signal baseline
Trace baseline (set to zero)
Small signal pop-up once the ringing is substracted
Ampth(Detect signal candidates)

## Slide 22: NEUTRON SCATERING BACKGROUND IN DIAMOND (SHADOW BARS)
Geant4 Simulations  Shadow bar features 99,9% efficiency to remove or scatter neutrons below 50 MeV (99,0% if only En > 10 MeV considered)
40-50% BACKGROUND
DETECTOR
40-50% BACKGROUND

## Slide 23: EXPERIMENTAL NEUTRON FLUX
LiF(p,n): 9(3)·106 n/sr/shot (kT ~19 MeV)
Cu(p,n): 7(2)·106 n/sr/shot (kT ~17 MeV)
TNSA ANALYTICAL SPECTRUM:

## Slide 24: EXPECTED NEUTRON FLUX (RCF+Geant4)
QGSP_BIC_AllHP
FROM RCF

## Slide 25: EXPERIMENTAL vs SIMULATIONS: DIAMOND DETECTOR

## Slide 26: 3.CONCLUSIONS
SUMMARY AND OUTLOOK

## Slide 27: CONCLUSIONS AND OUTLOOK
Strong EMP: High-frequency noise ringing in detector signals.  Reduced, but not avoided, with EM shielding.
Harsh/challenging radiation environment: Strong detector saturation due to prompt components (with a limited duration). Need of huge shielding (extra source of background) or ultrafast detectors with low efficiency (e.g. diamonds. Need of a high repetition source).
Almost 1300 shots & laser-plasma source setup mostly unchanged  Statistical analysis of shot-to-shot fluctuations and proton acceleration stability.
First single-event measurement of a fast neutron flux produced by a PW laser with a nuclear physics detector with results in agreement with the expectations from simulations  First steps for nuclear reactions measurements in a laser facility.
The work opens the door to future measurements of nuclear reactions at LDNS, considering:
It is carried out in a room adjacent to the laser-interaction room, in order to reduce the EMP, the gamma-flash saturation and the neutron scattering background
Fully exploitation of the laser repetition rate  Target refreshment (Hot topic in laser acceleration community) + Plasma mirror limitation
Low efficiency detectors to reduce the effect of the gamma flash saturation and the signal pile-up

## Slide 28
Acknowledgements
This project has received funding from the EC H2020-Euratom research and training programme 2014-2018 under grant agreement 847594 (ARIEL).
¡¡GRACIAS!!
Any question?

## Slide 29: BACK-UP SLIDES

## Slide 30: PSD LIMITATIONS
F ~1  Point-like ionization
F ~2  Homogeneous ionization
F < 1,6 Usual qualifier for neutrons

## Slide 31: BACKGROUND SIMULATIONS
Direct component: 30-40% for the diamond detector  50-60% according to the SB.
PHITS simulations  S. Scheuren (TUD) PhD thesis.
DIAMOND DETECTOR

## Slide 32: BACKGROUND SIMULATIONS
Direct component: 1-6% for the EJ-232Q Scintillator
PHITS simulations  S. Scheuren (TUD) PhD thesis.
SCINTILLATORS

## Slide 33: NEUTRON PRODUCTION: BUBBLE DETECTORS
Nb  Number of bubbles.
C (bubbles/rem)  Calibration factor (given by the manufacturer).
S = 3,5 · 105 bubbles/(n·cm2) correction factor
L2 (cm)  Distance to the neutron source

## Slide 34: DATA COMPARISON WITH SIMULATIONS: BUBBLES
* The value for PHITS corresponds to the simulation in the forward direction (2π)

## Slide 35: NOISE REDUCTION
For a previous campaign in May 2021 (different detector)

## Slide 36: DETECTION EFFICIENCY AND ENERGY CALIBRATION
Geant4 Simulations  Monoenergetic beams in 1 MeV steps

## Slide 37: DETECTION EFFICIENCY AND ENERGY CALIBRATION
Geant4 Simulations  Monoenergetic beams in 1 MeV steps
5 MeV
15 MeV
A (V·s)  Signal area
Z = 50 Ω  Impedance
G = 150  Amplifier gain
Q = 1,6· 10-19 C  e- charge
Eioniz = 13 eV  Ionization energy
Noise

## Slide 38: SCINTILLATOR TIME-OF-FLIGHT TRACES
Superposition of all the signals produced during each shot (pile-up)
+
Mixed field of gammas and neutrons
+
Shielding effect
Need of deconvolution algorithms and detailed simulations to resolve it

## Slide 39: SIGNALS FROM THE SCINTILLATORS
Pitcher-catcher production comparison
Gammaflash substractions
This traces are the result of the superposition of all the signals produced during each shot (pile-up)
Extra effort to be unfolded

## Slide 40: ACCELERATOR-BASED & LASER-DRIVEN NEUTRON SOURCES
~ 200 shots/day
(plasma mirror)
DRACO@HZDR |  | HiSPANoS@CNA
PW-class 30 J Laser System (18 J on target) | Facility | 3 MV Tandem Accelerator
30 fs laser / ~ps ions | Pulse duration | 1-2 ns
Up to 1 Hz (compressor) (1 shot/minute during the experiment) | Repetition rate | 500 kHz
7-9·106 (Assuming isotropic production) | Production (n/sr/pulse) | ~ 105
7-9·106 | Flux (n/sr/s) | 4-5·1010
LASER-DRIVEN
(LDNS)
Advantages
Higher instantaneous flux
Shorter pulses
Technology in fast development
Drawbacks
Lower repetition rate (for now)
Lower reproducibility
New /Unknown environment
Accelerator-based (ABNS)
Advantages
Higher integrated flux
Higher stability
Robust and well-know technology
Drawbacks
Longer pulses
Lower instantaneous flux

## Slide 41: THE HiSPANoS NEUTRON SOURCE
General
1H, 2H, 4He beams
Up to 6 MeV (9 MeV for 4He)
Continuous mode
Up to 10 uA
Pulse mode
1-2 ns pulse width
32,5 kHz - 2 MHz
2 % duty cycle at 500 kHz
1- 4 m flight path
Reaction | Q-value (MeV) | Eth (MeV) | Target |  |  | Neutron spectra
 |  |  | Material | Thickness | Diameter | 
2H(d,n)3He | 3,27 | 0,0 | D/Ti | 546 µg/cm2 | 30 mm | Quasi-monoenergetic 2,2 – 6,1 MeV
9Be(p,n)9B | -1,85 | 2,06 | Be | 500 µm | 25 mm | Continuum up to 4 MeV
9Be(d,n)10B | 4,36 | 0,0 |  |  |  | Continuum up to10 MeV
7Li(p,n)7Be | -1,64 | 1,88 | Li | 500 µm | 25 mm | Continuum up to 4 MeV
7Li(d,n)8Be | 15,03 | 0,0 |  |  |  | Continuum up to20 MeV

## Slide 42: PLASMA MIRROR

## Slide 43: AVERAGE SIGNAL AND DISPERSION

## Slide 44: EXPERIMENTAL CAMPAIGN AT VEGA@CLPU (Spain)
VEGA3@CLPU
PW-class 30 J Laser System
30 fs laser pulse / ~ps ion pulse (200 fs during the experiment)
Up to 1 Hz (compressor) (~ 0,1 Hz during the experiment)
~ 500 shots/day (+ 3500 during the whole campaign)
~ 1·107 neutrons/shot (Based on LiF activation)
CLPU (Centro de Láseres Pulsados) is an ICTS (Unique research facility) opened to external users and located in Salamanca (Spain). It hosts the VEGA laser facility with 3 different beamlines (VEGA1, VEGA2 and VEGA3). It

## Slide 45: Campaign VEGA3@CLPU: Pitcher-Catcher
Laser Beam
Neutron Detectors
Rotating Wheel:
8000 targets
Capable to rotate at 0.1 Hz @ 30J
1 Hz @ 12 J

## Slide 46: Campaign VEGA3@CLPU: Neutron Detectors
Diamond detector
EJ200 + Gated PMT EJ232Q
PPAC (U-238/Th-232)
Rotating “Pitcher” target wheel
LiF “catcher” target
B-11 sample
Thick PE beam-dump
Laser Beam
Bonner Spheres
Bonner Spheres
He-3 Counters

## Slide 47: Campaign VEGA3@CLPU: Neutron Detectors
Diamond detector
EJ200 + Gated PMT EJ232Q
PPAC (U-238/Th-232)
Rotating “Pitcher” target wheel
LiF “catcher” target
B-11 sample
Thick PE beam-dump
Laser Beam
Bonner Spheres
Bonner Spheres
He-3 Counters

## Slide 48: CONCLUSIONS AND OUTLOOK
Harsh radiation environment: Strong detector saturation due to prompt components (with limited duration)  Need of huge shielding (extra source of background) or ultrafast detectors with low efficiency (e.g. diamonds. Need of a high repetition source).
Strong EMP: High frequency noise ringing in diamond and PPAC signals.  Reduced, but not avoided, with EM shielding.
***
More than 3500 shots & laser-plasma source setup mostly unchanged  Statistical analysis of shot-to-shot fluctuations and proton acceleration stability.
We were able to measure with conventional scintillators in single signal mode substituting the massive lead shielding for a 5 cm Pb filter
Bigger room + Longer flightpath  Reduction of the number of signal in the detector and increasing the signal to noise ratio.
Lower power  Less neutron production and lower cut-off energy (Still suitable for nuclear physics)  Compensated with a high repetition neutron source (0,1 Hz)…
But all this factors reduce the counting in the low efficiency detectors (PPACs + Diamonds)

## Slide 49: CONCLUSIONS AND OUTLOOK
Harsh radiation environment: Strong detector saturation due to prompt components (with limited duration)  Need of huge shielding (extra source of background) or ultrafast detectors with low efficiency (e.g. diamonds. Need of a high repetition source).
Strong EMP: High frequency noise ringing in diamond and PPAC signals.  Reduced, but not avoided, with EM shielding.
***
More than 3500 shots & laser-plasma source setup mostly unchanged  Statistical analysis of shot-to-shot fluctuations and proton acceleration stability.
We were able to measure with conventional scintillators in single signal mode substituting the massive lead shielding for a 5 cm Pb filter
Very very very preliminary...

## Slide 50: NEUTRONS FOR NUCLEAR PHYSICS: ENERGY RANGE AND APPLICATIONS
NEUTRON ENERGY RANGES:
High energy: >20 MeV
Fast: From 100s keV to 20 MeV
Epithermal: From eV to 100s keV
Thermal: Water moderated at room temperature ∼25 meV
Cold: Less than < 25 meV
NEUTRON TEMPORAL STRUCTURE:
Continuous beams: Irradiation studies, activation analysis, production of radioisotopes, dosimetry, and other applications that focus on integral effects.
Pulsed beams: differential cross-section measurements, neutron resonance imaging, detector characterization, metrology, and applications to which the energy of the neutrons is relevant.
Image credit: n_TOF collaboration

## Slide 51: A WORLD-CLASS EXAMPLE: ELI-NP
“
”
2x10 PW HIGH-POWER LASER SYSTEM
80 International Scientific Collaborations
310 M€ budget
Intensities of 1023 W/cm2 and electrical fields up to 1015 V/m
Fundamental Research
laser-driven acceleration mechanism
Exotic nuclei and photo-fission
Vacuum properties and particle creation in laser-gamma beams interactions
Nuclear structure and astrophysics studies
Applied Research
Materials under extreme irradiation for space science
Management of nuclear materials
Industrial tomography
Brilliant positron source for materials / processes characterization
Radioisotopes for medical applications
The infrastructure will provide a new European laboratory addressing a broad range of scientific research areas, from frontier fundamental physics, new nuclear physics and astrophysics to applications in nuclear materials, radioactive waste management, material science and life sciences.
Webpage: www.eli-np.ro