## Slide 1: GRAPE : GELINA Reproduction on Accelerator of PETALE Experiments
T. Ligonnet, A. Laureau, V. Lamirand, A. Pautz
ARIEL Final Workshop
January 17, 2024
Laboratory for Reactor Physics and Systems Behaviour

## Slide 2: Objective: stainless steel nuclear data
Provide new constraints in the MeV-range and above for stainless steel nuclear data
Fission: heavy reflectors (GEN-III PWR)
Fusion: 14 MeV neutrons
Accelerators: activation
Programme in CROCUS on elemental-type reflector experiments, in the prospect of data assimilation
Separate study of steel, Fe, Ni and Cr
Reactivity worth of reflectors
Transmission using activation dosimetry
Collaboration between CEA & EPFL
By ChNPP at English Wikipedia, CC BY 3.0, https://commons.wikimedia.org/w/index.php?curid=22017751
EPR heavy reflector
Flux tilt at
interface?
Iron inelastic scattering cross section data (JANIS)
Collaboration
between CEA & EPFL
ARIEL Final Workshop

## Slide 3: Objective: stainless steel nuclear data
Provide new constraints in the MeV-range and above for stainless steel nuclear data
Fission: heavy reflectors (GEN-III PWR)
Fusion: 14 MeV neutrons
Accelerators: activation
Programme in CROCUS on elemental-type reflector experiments, in the prospect of data assimilation
Separate study of steel, Fe, Ni and Cr
Reactivity worth of reflectors
Transmission using activation dosimetry
Collaboration between CEA & EPFL
Cross section of the CROCUS
reactor core for PETALE
1.3 m
By ChNPP at English Wikipedia, CC BY 3.0, https://commons.wikimedia.org/w/index.php?curid=22017751
EPR heavy reflector
~4 m
~20 cm
≫
Collaboration
between CEA & EPFL
ARIEL Final Workshop

## Slide 4: Experimental design by uncertainty propagation
Relating XS uncertainty distribution with measured reaction rates using Total Monte Carlo and Correlated Sampling1,2
1 A. Laureau et al., “Uncertainty propagation for the design study of the PETALE experimental programme in the CROCUS reactor,” EPJ Nucl. Sci. Technol., vol. 6, p. 9, 2020.
Reaction rate distributions with In(n,γ)
in the iron metal reflector (128 ACE files)
56Fe cross sections dispersion in TENDL 2017
Energy (MeV)
Cross section (barn)
Reaction rate
(a.u.)
15
10
5
0
-5
-10
Variation
(%)
1.2
1.0
0.8
0.6
0.4
0.2
Dosimeter position in the reflector
Entry
2
4
6
8
Exit
2%
✔
× N full core Monte Carlo calculations
⇔ 1 node week
2 V. Lamirand et al., “An Experimental Programme optimized with Uncertainty Propagation: PETALE in the CROCUS Reactor,” EPJ Web Conf., vol. 211, p. 03003, Jun. 2019.
ARIEL Final Workshop

## Slide 5: Experimental design by uncertainty propagation
Relating XS uncertainty distribution with measured reaction rates using Total Monte Carlo and Correlated Sampling1,2
1 A. Laureau et al., “Uncertainty propagation for the design study of the PETALE experimental programme in the CROCUS reactor,” EPJ Nucl. Sci. Technol., vol. 6, p. 9, 2020.
Reaction rate distributions with In(n,γ)
in the iron metal reflector (128 ACE files)
Reaction rate
(a.u.)
15
10
5
0
-5
-10
Variation
(%)
1.2
1.0
0.8
0.6
0.4
0.2
Dosimeter position in the reflector
Entry
2
4
6
8
Exit
× N full core Monte Carlo calculations
⇔ 1 node week
2 V. Lamirand et al., “An Experimental Programme optimized with Uncertainty Propagation: PETALE in the CROCUS Reactor,” EPJ Web Conf., vol. 211, p. 03003, Jun. 2019.
Comparison between measurement uncertainties and expected variation coming from nuclear data in the system
2%
✔
ARIEL Final Workshop

## Slide 6: GRAPE at JRC-Geel
Within the HARVEST-X project
Reproduction of PETALE transmission experiments
  Activation dosimeters between reflector sheets
  Output: reaction rates in dosimeters
  4 metal blocks: Fe, Cr, Ni, stainless steel (304L)
GRAPE
  White neutron source instead of spectrum from light water reactor (fission + moderation)
  Focused on the fast neutron range
  Objective of a Benchmark in SINBAD
Sheet
Foils
Metal reflector
30 × 30 × 16
M. Pillon et al., “Integral Benchmark Experiments on a Large Copper Block Using the GELINA Accelerator to Validate natCu Neutron Cross Sections From Different Neutron Cross-Sectional Databases,” IEEE Transactions on Plasma Science 47 6, 2943 (2019); https://doi.org/10.1109/TPS.2019.2911706.

## Slide 7: Activation Dosimetry Setup
5 types of activation dosimeters
  Over the fast neutron range only
3 of them need onsite measurements
  ,
2 of them will be measured later, at our lab
  and
Material |  |  |  |  | 
Reaction | n, n’ | n, p | n, p | n, p | n, α
Half-life | 4.49 h | 70.86 days | 312.2 days | 2.58 h | 15 h
Median activation energy | 1.8 MeV | 3.8 MeV | 4.3 MeV | 8.3 MeV | 9.3 MeV
Material |  |  |  |  | 
Reaction | n, n’ | n, p | n, p | n, p | n, α
Half-life | 4.49 h | 70.86 days | 312.2 days | 2.58 h | 15 h
Median activation energy | 1.8 MeV | 3.8 MeV | 4.3 MeV | 8.3 MeV | 9.3 MeV
ARIEL Final Workshop

## Slide 8: Computational Methods
Monte Carlo neutron transport simulation
Serpent2, modified build
Transport using the JEFF-3.3 nuclear data library
Dosimetry using the IRDFF-II library
Normalization by the 3rd dosimeter (default)
Covariances propagation
←fuel PETALE reflector→
Correlations
considered sources of uncertainty
NDsource
Position
Computations
NDdosi
HPGe Calibration
Auto-absorption
Measurements
Block depth
Metal block
ARIEL Final Workshop

## Slide 9: Methods… up to PETALE results
Monte Carlo neutron transport simulation
Serpent2, modified build
Transport using the JEFF-3.3 nuclear data library
Dosimetry using the IRDFF-II library
Normalization by the 3rd dosimeter (default)
Covariances propagation
ARIEL Final Workshop

## Slide 10: Methods… up to PETALE results
Monte Carlo neutron transport simulation
Serpent2, modified build
Transport using the JEFF-3.3 nuclear data library
Dosimetry using the IRDFF-II library
Normalization by the 3rd dosimeter (default)
Covariances propagation
What are the remaining risks?
Biases!!!
  Methodology → Motivation for BLOOM in CROCUS
  System → Motivation for GRAPE
ARIEL Final Workshop

## Slide 11: GRAPE design with perturbed XS
Set of perturbed XS obtained using available covariance matrices
  Processed with NJOY
  Some minor isotopes do not have covariances and are not currently perturbed.
Performed Monte Carlo simulations
  Currently, simulations with 256 perturbed XS
  Output: dosimeter reaction rates
  Spectrum from “On the feasibility to perform integral transmission experiments in the GELINA target hall at IRMM”, Pierre Leconte et al. (2017)

## Slide 12: GRAPE design with perturbed XS
Propagation results are close to PETALE
Observed dispersion smaller for JEFF-3.3 than ENDF/B-VII.1 and B-VIII.0
  For both Cr and Ni
  B-VIII.0 similar to B-VII.1, for both elements
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Reflector | Iron |  |  |  |  | Chromium |  |  |  |  | Nickel |  |  |  | 
Database | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
Isotopes | 54,56,57,58 |  | 54,56,57 |  | 56 | 50, 52, 53, 54 |  | 50, 52, 53 |  | 50, 52, 53 | 58, 60, 62 |  | 58, 60 |  | 58, 60
Setup Dosimeter | PETALE | GRAPE | PETALE | GRAPE | GRAPE | PETALE | GRAPE | PETALE | GRAPE | GRAPE | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 4.34 ± 0.17 | 3.77 ± 0.15 | 5.5 ± 0.2 | 5.9 ± 0.3 | 4.14 ± 0.17 | 1.23 ± 0.05 | 0.96 ± 0.04 | 6.4 ± 0.3 | 5.2 ± 0.2 | 5.1 ± 0.2 | 1.18 ± 0.05 | 1.08 ± 0.04 | 6.6 ± 0.3 | 5.7 ± 03 | 5.8 ± 0.2
Ni | 6.7 ± 0.3 | 5.5 ± 0.3 | 5.1 ± 0.2 | 5.1 ± 0.2 | 7.2 ± 0.3 | 2.32 ± 0.10 | 2.00 ± 0.08 | 9.4 ± 0.4 | 7.6 ± 0.3 | 7.4 ± 0.4 | 2.03 ± 0.09 | 1.77 ± 0.08 | 10.4 ± 0.5 | 8.6 ± 0.4 | 8.2 ± 0.3
Fe-54 | 7.0 ± 0.4 | 5.6 ± 0.3 | 5.4 ± 0.2 | 5.4 ± 0.2 | 7.6 ± 0.3 | 2.48 ± 0.10 | 2.13 ± 0.08 | 9.9 ± 0.4 | 8.0 ± 0.3 | 7.9 ± 0.4 | 2.33 ± 0.10 | 1.99 ± 0.08 | 11.2 ± 0.6 | 9.1 ± 0.4 | 8.6 ± 0.4
Fe-56 | 5.0 ± 0.2 | 4.5 ± 0.2 | 8.3 ± 0.4 | 8.1 ± 0.3 | 8.0 ± 0.4 | 2.17 ± 0.09 | 2.09 ± 0.09 | 10.2 ± 0.4 | 10.6 ± 0.5 | 10.5 ± 0.6 | 2.97 ± 0.13 | 2.79 ± 0.11 | 8.7 ± 0.4 | 8.3 ± 0.4 | 7.9 ± 0.4
Al | 5.5 ± 0.2 | 4.4 ± 0.2 | 9.1 ± 0.4 | 8.5 ± 0.4 | 7.9 ± 0.4 | 2.28 ± 0.10 | 2.22 ± 0.09 | 11.9 ± 0.5 | 11.9 ± 0.5 | 12.2 ± 0.6 | 3.01 ± 0.13 | 2.88 ± 0.12 | 8.4 ± 0.4 | 8.5 ± 0.4 | 8.2 ± 0.4
Ni

## Slide 13: GRAPE design with perturbed XS
Propagation results are close to PETALE
Observed dispersion smaller for JEFF-3.3 than ENDF/B-VII.1 and B-VIII.0
  For both Cr and Ni
  B-VIII.0 similar to B-VII.1, for both elements
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Reflector | Iron |  |  |  |  | Chromium |  |  |  |  | Nickel |  |  |  | 
Database | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
Isotopes | 54,56,57,58 |  | 54,56,57 |  | 56 | 50, 52, 53, 54 |  | 50, 52, 53 |  | 50, 52, 53 | 58, 60, 62 |  | 58, 60 |  | 58, 60
Setup Dosimeter | PETALE | GRAPE | PETALE | GRAPE | GRAPE | PETALE | GRAPE | PETALE | GRAPE | GRAPE | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 4.34 ± 0.17 | 3.77 ± 0.15 | 5.5 ± 0.2 | 5.9 ± 0.3 | 4.14 ± 0.17 | 1.23 ± 0.05 | 0.96 ± 0.04 | 6.4 ± 0.3 | 5.2 ± 0.2 | 5.1 ± 0.2 | 1.18 ± 0.05 | 1.08 ± 0.04 | 6.6 ± 0.3 | 5.7 ± 03 | 5.8 ± 0.2
Ni | 6.7 ± 0.3 | 5.5 ± 0.3 | 5.1 ± 0.2 | 5.1 ± 0.2 | 7.2 ± 0.3 | 2.32 ± 0.10 | 2.00 ± 0.08 | 9.4 ± 0.4 | 7.6 ± 0.3 | 7.4 ± 0.4 | 2.03 ± 0.09 | 1.77 ± 0.08 | 10.4 ± 0.5 | 8.6 ± 0.4 | 8.2 ± 0.3
Fe-54 | 7.0 ± 0.4 | 5.6 ± 0.3 | 5.4 ± 0.2 | 5.4 ± 0.2 | 7.6 ± 0.3 | 2.48 ± 0.10 | 2.13 ± 0.08 | 9.9 ± 0.4 | 8.0 ± 0.3 | 7.9 ± 0.4 | 2.33 ± 0.10 | 1.99 ± 0.08 | 11.2 ± 0.6 | 9.1 ± 0.4 | 8.6 ± 0.4
Fe-56 | 5.0 ± 0.2 | 4.5 ± 0.2 | 8.3 ± 0.4 | 8.1 ± 0.3 | 8.0 ± 0.4 | 2.17 ± 0.09 | 2.09 ± 0.09 | 10.2 ± 0.4 | 10.6 ± 0.5 | 10.5 ± 0.6 | 2.97 ± 0.13 | 2.79 ± 0.11 | 8.7 ± 0.4 | 8.3 ± 0.4 | 7.9 ± 0.4
Al | 5.5 ± 0.2 | 4.4 ± 0.2 | 9.1 ± 0.4 | 8.5 ± 0.4 | 7.9 ± 0.4 | 2.28 ± 0.10 | 2.22 ± 0.09 | 11.9 ± 0.5 | 11.9 ± 0.5 | 12.2 ± 0.6 | 3.01 ± 0.13 | 2.88 ± 0.12 | 8.4 ± 0.4 | 8.5 ± 0.4 | 8.2 ± 0.4
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  | 
 | Chromium |  |  |  | 
 | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
 | 50, 52, 53, 54 |  | 50, 52, 53 |  | 50, 52, 53
 | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 1.23 ± 0.05 | 0.96 ± 0.04 | 6.4 ± 0.3 | 5.2 ± 0.2 | 5.1 ± 0.2
Ni | 2.32 ± 0.10 | 2.00 ± 0.08 | 9.4 ± 0.4 | 7.6 ± 0.3 | 7.4 ± 0.4
Fe-54 | 2.48 ± 0.10 | 2.13 ± 0.08 | 9.9 ± 0.4 | 8.0 ± 0.3 | 7.9 ± 0.4
Fe-56 | 2.17 ± 0.09 | 2.09 ± 0.09 | 10.2 ± 0.4 | 10.6 ± 0.5 | 10.5 ± 0.6
Al | 2.28 ± 0.10 | 2.22 ± 0.09 | 11.9 ± 0.5 | 11.9 ± 0.5 | 12.2 ± 0.6
Cr
ARIEL Final Workshop

## Slide 14: A closer look at Chromium
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  | 
 | Chromium |  |  |  | 
 | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
 | 50, 52, 53, 54 |  | 50, 52, 53 |  | 50, 52, 53
 | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 1.23 ± 0.05 | 0.96 ± 0.04 | 6.4 ± 0.3 | 5.2 ± 0.2 | 5.1 ± 0.2
Ni | 2.32 ± 0.10 | 2.00 ± 0.08 | 9.4 ± 0.4 | 7.6 ± 0.3 | 7.4 ± 0.4
Fe-54 | 2.48 ± 0.10 | 2.13 ± 0.08 | 9.9 ± 0.4 | 8.0 ± 0.3 | 7.9 ± 0.4
Fe-56 | 2.17 ± 0.09 | 2.09 ± 0.09 | 10.2 ± 0.4 | 10.6 ± 0.5 | 10.5 ± 0.6
Al | 2.28 ± 0.10 | 2.22 ± 0.09 | 11.9 ± 0.5 | 11.9 ± 0.5 | 12.2 ± 0.6
Propagation results are close to PETALE
  A bit lower for In, Ni, and 54Fe dosimeters
ARIEL Final Workshop

## Slide 15: A closer look at Chromium
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  | 
 | Chromium |  |  |  | 
 | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
 | 50, 52, 53, 54 |  | 50, 52, 53 |  | 50, 52, 53
 | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 1.23 ± 0.05 | 0.96 ± 0.04 | 6.4 ± 0.3 | 5.2 ± 0.2 | 5.1 ± 0.2
Ni | 2.32 ± 0.10 | 2.00 ± 0.08 | 9.4 ± 0.4 | 7.6 ± 0.3 | 7.4 ± 0.4
Fe-54 | 2.48 ± 0.10 | 2.13 ± 0.08 | 9.9 ± 0.4 | 8.0 ± 0.3 | 7.9 ± 0.4
Fe-56 | 2.17 ± 0.09 | 2.09 ± 0.09 | 10.2 ± 0.4 | 10.6 ± 0.5 | 10.5 ± 0.6
Al | 2.28 ± 0.10 | 2.22 ± 0.09 | 11.9 ± 0.5 | 11.9 ± 0.5 | 12.2 ± 0.6
Propagation results are close to PETALE
  A bit lower for In, Ni, and 54Fe dosimeters
JEFF-3.3: similar for most dosimeters
  Around 2%-2.5%
  Lower for 115In(n,n’)
1% – 2.5%
ARIEL Final Workshop

## Slide 16: A closer look at Chromium
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  | 
 | Chromium |  |  |  | 
 | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
 | 50, 52, 53, 54 |  | 50, 52, 53 |  | 50, 52, 53
 | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 1.23 ± 0.05 | 0.96 ± 0.04 | 6.4 ± 0.3 | 5.2 ± 0.2 | 5.1 ± 0.2
Ni | 2.32 ± 0.10 | 2.00 ± 0.08 | 9.4 ± 0.4 | 7.6 ± 0.3 | 7.4 ± 0.4
Fe-54 | 2.48 ± 0.10 | 2.13 ± 0.08 | 9.9 ± 0.4 | 8.0 ± 0.3 | 7.9 ± 0.4
Fe-56 | 2.17 ± 0.09 | 2.09 ± 0.09 | 10.2 ± 0.4 | 10.6 ± 0.5 | 10.5 ± 0.6
Al | 2.28 ± 0.10 | 2.22 ± 0.09 | 11.9 ± 0.5 | 11.9 ± 0.5 | 12.2 ± 0.6
Propagation results are close to PETALE
  A bit lower for In, Ni, and 54Fe dosimeters
JEFF-3.3: similar for most dosimeters
  Around 2%-2.5%
  Lower for 115In(n,n’)
ENDF: uncertainties increase with increasing dosimeters’ energy range
  From 5% up to 12%
  No significant differences between ENDFs
5% – 12%
ARIEL Final Workshop

## Slide 17: A closer look at Chromium
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  | 
 | Chromium |  |  |  | 
 | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
 | 50, 52, 53, 54 |  | 50, 52, 53 |  | 50, 52, 53
 | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 1.23 ± 0.05 | 0.96 ± 0.04 | 6.4 ± 0.3 | 5.2 ± 0.2 | 5.1 ± 0.2
Ni | 2.32 ± 0.10 | 2.00 ± 0.08 | 9.4 ± 0.4 | 7.6 ± 0.3 | 7.4 ± 0.4
Fe-54 | 2.48 ± 0.10 | 2.13 ± 0.08 | 9.9 ± 0.4 | 8.0 ± 0.3 | 7.9 ± 0.4
Fe-56 | 2.17 ± 0.09 | 2.09 ± 0.09 | 10.2 ± 0.4 | 10.6 ± 0.5 | 10.5 ± 0.6
Al | 2.28 ± 0.10 | 2.22 ± 0.09 | 11.9 ± 0.5 | 11.9 ± 0.5 | 12.2 ± 0.6
Propagation results are close to PETALE
  A bit lower for In, Ni, and 54Fe dosimeters
Observed dispersion smaller for JEFF-3.3 than ENDF/B-VII.1 and B-VIII.0
  For both Cr and Ni blocks
1% – 2.5%
5% – 12%
ARIEL Final Workshop

## Slide 18: A closer look at Chromium…
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  | 
 | Chromium |  |  |  | 
 | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
 | 50, 52, 53, 54 |  | 50, 52, 53 |  | 50, 52, 53
 | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 1.23 ± 0.05 | 0.96 ± 0.04 | 6.4 ± 0.3 | 5.2 ± 0.2 | 5.1 ± 0.2
Ni | 2.32 ± 0.10 | 2.00 ± 0.08 | 9.4 ± 0.4 | 7.6 ± 0.3 | 7.4 ± 0.4
Fe-54 | 2.48 ± 0.10 | 2.13 ± 0.08 | 9.9 ± 0.4 | 8.0 ± 0.3 | 7.9 ± 0.4
Fe-56 | 2.17 ± 0.09 | 2.09 ± 0.09 | 10.2 ± 0.4 | 10.6 ± 0.5 | 10.5 ± 0.6
Al | 2.28 ± 0.10 | 2.22 ± 0.09 | 11.9 ± 0.5 | 11.9 ± 0.5 | 12.2 ± 0.6
Propagation results are close to PETALE
  A bit lower for In, Ni, and 54Fe dosimeters
Observed dispersion smaller for JEFF-3.3 than ENDF/B-VII.1 and B-VIII.0
  For both Cr and Ni blocks
NB: JEFF design dispersion
was unrealistic for PETALE
when compared to results
ARIEL Final Workshop

## Slide 19: … and iron
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  | 
 | Iron |  |  |  | 
 | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
 | 54,56,57,58 |  | 54,56,57 |  | 56
 | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 4.34 ± 0.17 | 3.77 ± 0.15 | 5.5 ± 0.2 | 5.9 ± 0.3 | 4.14 ± 0.17
Ni | 6.7 ± 0.3 | 5.5 ± 0.3 | 5.1 ± 0.2 | 5.1 ± 0.2 | 7.2 ± 0.3
Fe-54 | 7.0 ± 0.4 | 5.6 ± 0.3 | 5.4 ± 0.2 | 5.4 ± 0.2 | 7.6 ± 0.3
Fe-56 | 5.0 ± 0.2 | 4.5 ± 0.2 | 8.3 ± 0.4 | 8.1 ± 0.3 | 8.0 ± 0.4
Al | 5.5 ± 0.2 | 4.4 ± 0.2 | 9.1 ± 0.4 | 8.5 ± 0.4 | 7.9 ± 0.4
Propagation results are close to PETALE
Libraries behave differently for different dosimeter ranges
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Reflector | Iron |  |  |  |  | Chromium |  |  |  |  | Nickel |  |  |  | 
Database | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
Isotopes | 54,56,57,58 |  | 54,56,57 |  | 56 | 50, 52, 53, 54 |  | 50, 52, 53 |  | 50, 52, 53 | 58, 60, 62 |  | 58, 60 |  | 58, 60
Setup Dosimeter | PETALE | GRAPE | PETALE | GRAPE | GRAPE | PETALE | GRAPE | PETALE | GRAPE | GRAPE | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 4.34 ± 0.17 | 3.77 ± 0.15 | 5.5 ± 0.2 | 5.9 ± 0.3 | 4.14 ± 0.17 | 1.23 ± 0.05 | 0.96 ± 0.04 | 6.4 ± 0.3 | 5.2 ± 0.2 | 5.1 ± 0.2 | 1.18 ± 0.05 | 1.08 ± 0.04 | 6.6 ± 0.3 | 5.7 ± 03 | 5.8 ± 0.2
Ni | 6.7 ± 0.3 | 5.5 ± 0.3 | 5.1 ± 0.2 | 5.1 ± 0.2 | 7.2 ± 0.3 | 2.32 ± 0.10 | 2.00 ± 0.08 | 9.4 ± 0.4 | 7.6 ± 0.3 | 7.4 ± 0.4 | 2.03 ± 0.09 | 1.77 ± 0.08 | 10.4 ± 0.5 | 8.6 ± 0.4 | 8.2 ± 0.3
Fe-54 | 7.0 ± 0.4 | 5.6 ± 0.3 | 5.4 ± 0.2 | 5.4 ± 0.2 | 7.6 ± 0.3 | 2.48 ± 0.10 | 2.13 ± 0.08 | 9.9 ± 0.4 | 8.0 ± 0.3 | 7.9 ± 0.4 | 2.33 ± 0.10 | 1.99 ± 0.08 | 11.2 ± 0.6 | 9.1 ± 0.4 | 8.6 ± 0.4
Fe-56 | 5.0 ± 0.2 | 4.5 ± 0.2 | 8.3 ± 0.4 | 8.1 ± 0.3 | 8.0 ± 0.4 | 2.17 ± 0.09 | 2.09 ± 0.09 | 10.2 ± 0.4 | 10.6 ± 0.5 | 10.5 ± 0.6 | 2.97 ± 0.13 | 2.79 ± 0.11 | 8.7 ± 0.4 | 8.3 ± 0.4 | 7.9 ± 0.4
Al | 5.5 ± 0.2 | 4.4 ± 0.2 | 9.1 ± 0.4 | 8.5 ± 0.4 | 7.9 ± 0.4 | 2.28 ± 0.10 | 2.22 ± 0.09 | 11.9 ± 0.5 | 11.9 ± 0.5 | 12.2 ± 0.6 | 3.01 ± 0.13 | 2.88 ± 0.12 | 8.4 ± 0.4 | 8.5 ± 0.4 | 8.2 ± 0.4
Fe
ARIEL Final Workshop

## Slide 20: … and iron
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  | 
 | Iron |  |  |  | 
 | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
 | 54,56,57,58 |  | 54,56,57 |  | 56
 | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 4.34 ± 0.17 | 3.77 ± 0.15 | 5.5 ± 0.2 | 5.9 ± 0.3 | 4.14 ± 0.17
Ni | 6.7 ± 0.3 | 5.5 ± 0.3 | 5.1 ± 0.2 | 5.1 ± 0.2 | 7.2 ± 0.3
Fe-54 | 7.0 ± 0.4 | 5.6 ± 0.3 | 5.4 ± 0.2 | 5.4 ± 0.2 | 7.6 ± 0.3
Fe-56 | 5.0 ± 0.2 | 4.5 ± 0.2 | 8.3 ± 0.4 | 8.1 ± 0.3 | 8.0 ± 0.4
Al | 5.5 ± 0.2 | 4.4 ± 0.2 | 9.1 ± 0.4 | 8.5 ± 0.4 | 7.9 ± 0.4
Propagation results are close to PETALE
Libraries behave differently for different dosimeter ranges
  JEFF: larger dispersion for Ni/54Fe ranges
  B-VII.1: larger dispersion for 56Fe/Al ranges
ARIEL Final Workshop

## Slide 21: … and iron
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  | 
 | Iron |  |  |  | 
 | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
 | 54,56,57,58 |  | 54,56,57 |  | 56
 | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 4.34 ± 0.17 | 3.77 ± 0.15 | 5.5 ± 0.2 | 5.9 ± 0.3 | 4.14 ± 0.17
Ni | 6.7 ± 0.3 | 5.5 ± 0.3 | 5.1 ± 0.2 | 5.1 ± 0.2 | 7.2 ± 0.3
Fe-54 | 7.0 ± 0.4 | 5.6 ± 0.3 | 5.4 ± 0.2 | 5.4 ± 0.2 | 7.6 ± 0.3
Fe-56 | 5.0 ± 0.2 | 4.5 ± 0.2 | 8.3 ± 0.4 | 8.1 ± 0.3 | 8.0 ± 0.4
Al | 5.5 ± 0.2 | 4.4 ± 0.2 | 9.1 ± 0.4 | 8.5 ± 0.4 | 7.9 ± 0.4
Propagation results are close to PETALE
Libraries behave differently for different dosimeter ranges
  JEFF: larger dispersion for Ni/54Fe ranges
  B-VII.1: larger dispersion for 56Fe/Al ranges
  B-VIII.0: large and similar values for all four
ARIEL Final Workshop

## Slide 22: Conclusion on dispersion
Given the estimated dispersions, aiming for 1% HPGe precision seems reasonable
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Reflector | Iron |  |  |  |  | Chromium |  |  |  |  | Nickel |  |  |  | 
Database | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
Isotopes | 54,56,57,58 |  | 54,56,57 |  | 56 | 50, 52, 53, 54 |  | 50, 52, 53 |  | 50, 52, 53 | 58, 60, 62 |  | 58, 60 |  | 58, 60
Setup Dosimeter | PETALE | GRAPE | PETALE | GRAPE | GRAPE | PETALE | GRAPE | PETALE | GRAPE | GRAPE | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 4.34 ± 0.17 | 3.77 ± 0.15 | 5.5 ± 0.2 | 5.9 ± 0.3 | 4.14 ± 0.17 | 1.23 ± 0.05 | 0.96 ± 0.04 | 6.4 ± 0.3 | 5.2 ± 0.2 | 5.1 ± 0.2 | 1.18 ± 0.05 | 1.08 ± 0.04 | 6.6 ± 0.3 | 5.7 ± 03 | 5.8 ± 0.2
Ni | 6.7 ± 0.3 | 5.5 ± 0.3 | 5.1 ± 0.2 | 5.1 ± 0.2 | 7.2 ± 0.3 | 2.32 ± 0.10 | 2.00 ± 0.08 | 9.4 ± 0.4 | 7.6 ± 0.3 | 7.4 ± 0.4 | 2.03 ± 0.09 | 1.77 ± 0.08 | 10.4 ± 0.5 | 8.6 ± 0.4 | 8.2 ± 0.3
Fe-54 | 7.0 ± 0.4 | 5.6 ± 0.3 | 5.4 ± 0.2 | 5.4 ± 0.2 | 7.6 ± 0.3 | 2.48 ± 0.10 | 2.13 ± 0.08 | 9.9 ± 0.4 | 8.0 ± 0.3 | 7.9 ± 0.4 | 2.33 ± 0.10 | 1.99 ± 0.08 | 11.2 ± 0.6 | 9.1 ± 0.4 | 8.6 ± 0.4
Fe-56 | 5.0 ± 0.2 | 4.5 ± 0.2 | 8.3 ± 0.4 | 8.1 ± 0.3 | 8.0 ± 0.4 | 2.17 ± 0.09 | 2.09 ± 0.09 | 10.2 ± 0.4 | 10.6 ± 0.5 | 10.5 ± 0.6 | 2.97 ± 0.13 | 2.79 ± 0.11 | 8.7 ± 0.4 | 8.3 ± 0.4 | 7.9 ± 0.4
Al | 5.5 ± 0.2 | 4.4 ± 0.2 | 9.1 ± 0.4 | 8.5 ± 0.4 | 7.9 ± 0.4 | 2.28 ± 0.10 | 2.22 ± 0.09 | 11.9 ± 0.5 | 11.9 ± 0.5 | 12.2 ± 0.6 | 3.01 ± 0.13 | 2.88 ± 0.12 | 8.4 ± 0.4 | 8.5 ± 0.4 | 8.2 ± 0.4
Fe
Ni
Cr
ARIEL Final Workshop

## Slide 23: GRAPE Irradiation Revised Schedule
Constraints
  10000 counts per dosimeter in HPGe (3 detectors, on site)
  No longer than a week
  2 hours of waiting for dose decay before retrieval
    More for In dosimeters (high activity)
    As much as possible for blocks changes
  No late-night stay for dosimetry (if possible)
  50% operational margin on source rate
ARIEL Final Workshop

## Slide 24: GRAPE Irradiation Revised Schedule
Beam Status
HPGe No. 1 Schedule
HPGe No. 2 Schedule
HPGe No. 3 Schedule
ARIEL Final Workshop
Constraints
  10000 counts per dosimeter in HPGe (3 detectors, on site)
  No longer than a week
  2 hours of waiting for dose decay before retrieval
  No late-night stay for dosimetry (if possible)
  50% operational margin on source rate

## Slide 25: GRAPE Irradiation Revised Schedule
Constraints
  10000 counts per dosimeter in HPGe (3 detectors, on site)
  No longer than a week
  2 hours of waiting for dose decay before retrieval
  No late-night stay for dosimetry (if possible)
  50% operational margin on source rate
Measurements
Decay
Beam shutdown
Dosimeters retrieval
Al & 56Fe
In
ARIEL Final Workshop

## Slide 26: Conclusion
GRAPE nuclear data dispersion estimates are of the same order as PETALE
  Same level of feedback is expected, i.e. beneficial!
  Thus useful for bias identification
Dispersion for nickel and chromium are surprisingly low with JEFF-3.3
  2% vs. up to 12% with ENDF/B
  Too low wrt. to PETALE results (see PETALE presentation at 2023 JEFF meetings)
Dispersion for iron shows different energy trends between libraries, but with similar order of magnitude
  Ranging from 4% to 8%
  Globally highest for ENDF/B-VIII.0
Conclusion of the design study
  The irradiation campaign was proved feasible and useful for one week beam time
  An optimized schedule has been prepared
Final objective: new benchmark in SINBAD
“This project has received funding from the Euratom research and training programme 2014-2018 under grant agreement No 847594 (ARIEL).“
ARIEL Final Workshop

## Slide 27: Merci
© Maxime Filliau
Thomas Ligonnet
ARIEL Final Workshop

## Slide 28: Any Questions ?
ARIEL Final Workshop

## Slide 29: Annexes
ARIEL Final Workshop

## Slide 30: GRAPE Irradiation Revised Schedule
Constraints
  10000 counts per dosimeter in HPGe (3 detectors, on site)
  No longer than a week
  2 hours of waiting for dose decay before retrieval
    More for In dosimeters (high activity)
    As much as possible for blocks changes
  No late-night stay for dosimetry (if possible)
  50% operational margin on source rate

## Slide 31: GRAPE Irradiation Schedule
Irradiation planning optimization ongoing
  In(n,g) reaction is driving the radioprotection
  Fe-56 are measurements should start 2h after irradiation
Table version and day per day close-up on the next slides

## Slide 32
Under the assumption that our box design allows swift retrieval of the dosimeters
Fe/Al retrieval after 2h and Indium retrieval after 4h for decay of 116In (lower dose-rate)
Sheets change to steel after 8h for lower room dose-rate
GRAPE Irradiation Revised Schedule

## Slide 33: GRAPE Irradiation Revised Schedule
Constraints
  10000 counts per dosimeter in HPGe (3 detectors, on site)
  No longer than a week
  2 hours of waiting for dose decay before retrieval
  No late-night stay for dosimetry (if possible)
  50% operational margin on source rate

## Slide 34
Taking into account that at least three HPGe, with an efficiency similar to ours, should be usable. the number of necessary irradiation was reduced to 6 irradiations with a characterization one
The neutron used for the planning is 1.7x1013 n/s
Current cumulative beam time: 63h
Requested to ARIEL: 78h
GRAPE Irradiation Revised Schedule
Day | Hour | Description | Beam time [h] | Cumulative beam time [h]
1 | 10:00 | Characterisation (low intensity possible) | 1 | 1
1 | 13:00 | Dosimeters retrieval and reflector setup (iron sheets) | - | -
1 | 15:00 | Iron reflector irradiation | 14 | 15
2 | 07:00 | Fe and Al dosimeters retrieval | - | -
2 | 08:00 | Change of reflector to chromium and In dosimeters retrieval | - | -
2 | 09:00 | Chromium reflector irradiation | 4 | 19
2 | 15:00 | Fe and Al dosimeters retrieval | - | -
2 | 16:00 | Change of reflector to Nickel and In dosimeters retrieval | - | -
2 | 18:00 | Nickel reflector irradiation | 14 | 33
3 | 10:00 | Fe and Al dosimeters retrieval | - | -
3 | 12:00 | In dosimeters retrieval | - | -
3 | 16:00 | Change of reflector to Steel (304L) | - | -
3 | 17:00 | Steel reflector irradiation | 14 | 47
4 | 09:00 | Fe and Al dosimeters retrieval | - | -
4 | 11:00 | In dosimeters retrieval | - | -
4 | 15:00 | Change of reflector to Iron with 18 sheets | - | -
4 | 16:00 | Iron (18 sheets) reflector irradiation (Beam time is provisional) | 16 | 63
5 | 10:00 | Fe and Al dosimeters retrieval | - | -
5 | 12:00 | In dosimeters retrieval | - | -

## Slide 35: GRAPE at JRC-Geel
HARVEST-X:
Heuristic Assimilation, Reproduction, and Validation of Experiments for stainless STeel Cross sections
Reproduction of the PETALE experimental program on stainless-steel heavy reflectors.
Neutron transmission experiments
  Activation dosimeters between reflector sheets
  Output: dosimeters reaction rates
Four reflectors
  Iron, chromium, nickel, stainless-steel (304L)
GRAPE
  White neutron source instead of a heavily thermalized reactor
  Focused on the fast neutron range
  Endorsed by ARIEL-h2020
UMo

## Slide 36: GRAPE shielding
Shielding test with INTEGRAAL2-like shield
  15cm of polyethylene on sides and 30cm on back
  Simulation with 0.5 mm thick cadmium layer as neutron absorbent
    Comparison with 5 mm B4C layer
UMo
He
Reflector
polyethylene
Cadmium
Dosimeter

## Slide 37: GRAPE shielding
Shielding test with INTEGRAAL2-like shield
  15cm of polyethylene on sides and 30cm on back
  Simulation with 0.5 mm thick cadmium layer as neutron absorbent
  Test with large aluminum table (30cm thick)
  Effect from the wall on reaction rates decreased from 15% to 1%

## Slide 38: GRAPE shielding
Video space
Shielding test with INTEGRAAL2-like shield
  15cm of polyethylene on sides and 30cm on back
  Comparison between 0.5 mm of cadmium and 5 mm of B4C
    Systematic differences due to the change in shield

## Slide 39: GRAPE shielding
Video space
Shielding test with INTEGRAAL2-like shield
  15cm of polyethylene on sides and 30cm on back
  Simulation with cadmium as neutron absorbent
He
UMo
He

## Slide 40: GRAPE shielding
Video space
Shielding test with INTEGRAAL2-like shield
  15cm of polyethylene on sides and 30cm on back
  Simulation with 0.5 mm thick cadmium layer as neutron absorbent
  Test with large aluminum table (30cm thick)

## Slide 41: GRAPE shielding
Video space
Shielding test with INTEGRAAL2-like shield
  15cm of polyethylene on sides and 30cm on back
  Simulation with 0.5 mm thick cadmium layer as neutron absorbent
  Test with large aluminum table (30cm thick)

## Slide 42: GRAPE Irradiation Revised Schedule
Short irradiation for beam characterization and HPGe efficiency ratio measurement
Small number of dosimeters, low intensity possible
Preparation of the first reflector irradiation

## Slide 43
Biggest day while the residual radiation should be the lowest
  Only day with two reflector irradiations
Shorter irradiation with Chromium reflector (implying long HPGe measurements)
  Last HPGe start around 22:00, goes through the night
Dosimeters are numbered from the nearest to the farthest from the source
GRAPE Irradiation Revised Schedule

## Slide 44: GRAPE Irradiation Revised Schedule
Under the assumption that our box design allows swift retrieval of the dosimeters
Fe/Al retrieval after 2h and Indium retrieval after 4h for decay of 116In (lower dose-rate)
Sheets change to Iron (18 plate instead of 8) after 8h for lower room dose-rate

## Slide 45: GRAPE Irradiation Revised Schedule
End of last irradiation
Provisional duration: 16h
Measurement times to be estimated

## Slide 46: GELINA design with perturbed XS
Propagation results are close to PETALE
Observed dispersion tends to be smaller for JEFF-3.3 than ENDF/B-VII.1 and B-VIII.0
  Especially for Cr and Ni
    B-VIII.0 similar to B-VII.1 for both elements
  Surprising with respect to PETALE C/E
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Reflector | Iron |  |  |  |  | Chromium |  |  |  |  | Nickel |  |  |  | 
Database | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
Isotopes | 54,56,57,58 |  | 54,56,57 |  | 56 | 50, 52, 53, 54 |  | 50, 52, 53 |  | 50, 52, 53 | 58, 60, 62 |  | 58, 60 |  | 58, 60
Setup Dosimeter | PETALE | GRAPE | PETALE | GRAPE | GRAPE | PETALE | GRAPE | PETALE | GRAPE | GRAPE | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 4.34 ± 0.17 | 3.77 ± 0.15 | 5.5 ± 0.2 | 5.9 ± 0.3 | 4.14 ± 0.17 | 1.23 ± 0.05 | 0.96 ± 0.04 | 6.4 ± 0.3 | 5.2 ± 0.2 | 5.1 ± 0.2 | 1.18 ± 0.05 | 1.08 ± 0.04 | 6.6 ± 0.3 | 5.7 ± 03 | 5.8 ± 0.2
Ni | 6.7 ± 0.3 | 5.5 ± 0.3 | 5.1 ± 0.2 | 5.1 ± 0.2 | 7.2 ± 0.3 | 2.32 ± 0.10 | 2.00 ± 0.08 | 9.4 ± 0.4 | 7.6 ± 0.3 | 7.4 ± 0.4 | 2.03 ± 0.09 | 1.77 ± 0.08 | 10.4 ± 0.5 | 8.6 ± 0.4 | 8.2 ± 0.3
Fe-54 | 7.0 ± 0.4 | 5.6 ± 0.3 | 5.4 ± 0.2 | 5.4 ± 0.2 | 7.6 ± 0.3 | 2.48 ± 0.10 | 2.13 ± 0.08 | 9.9 ± 0.4 | 8.0 ± 0.3 | 7.9 ± 0.4 | 2.33 ± 0.10 | 1.99 ± 0.08 | 11.2 ± 0.6 | 9.1 ± 0.4 | 8.6 ± 0.4
Fe-56 | 5.0 ± 0.2 | 4.5 ± 0.2 | 8.3 ± 0.4 | 8.1 ± 0.3 | 8.0 ± 0.4 | 2.17 ± 0.09 | 2.09 ± 0.09 | 10.2 ± 0.4 | 10.6 ± 0.5 | 10.5 ± 0.6 | 2.97 ± 0.13 | 2.79 ± 0.11 | 8.7 ± 0.4 | 8.3 ± 0.4 | 7.9 ± 0.4
Al | 5.5 ± 0.2 | 4.4 ± 0.2 | 9.1 ± 0.4 | 8.5 ± 0.4 | 7.9 ± 0.4 | 2.28 ± 0.10 | 2.22 ± 0.09 | 11.9 ± 0.5 | 11.9 ± 0.5 | 12.2 ± 0.6 | 3.01 ± 0.13 | 2.88 ± 0.12 | 8.4 ± 0.4 | 8.5 ± 0.4 | 8.2 ± 0.4

## Slide 47: GELINA design with perturbed XS
Propagation results are close to PETALE
Observed dispersion tends to be smaller for JEFF-3.3 than ENDF/B-VII.1 and B-VIII.0
Exception: B-VIII.0 in Ni/54Fe dosimeter range
  Superior to both other that are close to each other
And B-VII.1 in the 115In(n,n’) dosimeter range
 | Relative standard deviation for the ninth dosimeter [%] |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Reflector | Iron |  |  |  |  | Chromium |  |  |  |  | Nickel |  |  |  | 
Database | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII | JEFF-3.3 |  | ENDF/B-VII.1 |  | ENDF/B-VIII
Isotopes | 54,56,57,58 |  | 54,56,57 |  | 56 | 50, 52, 53, 54 |  | 50, 52, 53 |  | 50, 52, 53 | 58, 60, 62 |  | 58, 60 |  | 58, 60
Setup Dosimeter | PETALE | GRAPE | PETALE | GRAPE | GRAPE | PETALE | GRAPE | PETALE | GRAPE | GRAPE | PETALE | GRAPE | PETALE | GRAPE | GRAPE
In | 4.34 ± 0.17 | 3.77 ± 0.15 | 5.5 ± 0.2 | 5.9 ± 0.3 | 4.14 ± 0.17 | 1.23 ± 0.05 | 0.96 ± 0.04 | 6.4 ± 0.3 | 5.2 ± 0.2 | 5.1 ± 0.2 | 1.18 ± 0.05 | 1.08 ± 0.04 | 6.6 ± 0.3 | 5.7 ± 03 | 5.8 ± 0.2
Ni | 6.7 ± 0.3 | 5.5 ± 0.3 | 5.1 ± 0.2 | 5.1 ± 0.2 | 7.2 ± 0.3 | 2.32 ± 0.10 | 2.00 ± 0.08 | 9.4 ± 0.4 | 7.6 ± 0.3 | 7.4 ± 0.4 | 2.03 ± 0.09 | 1.77 ± 0.08 | 10.4 ± 0.5 | 8.6 ± 0.4 | 8.2 ± 0.3
Fe-54 | 7.0 ± 0.4 | 5.6 ± 0.3 | 5.4 ± 0.2 | 5.4 ± 0.2 | 7.6 ± 0.3 | 2.48 ± 0.10 | 2.13 ± 0.08 | 9.9 ± 0.4 | 8.0 ± 0.3 | 7.9 ± 0.4 | 2.33 ± 0.10 | 1.99 ± 0.08 | 11.2 ± 0.6 | 9.1 ± 0.4 | 8.6 ± 0.4
Fe-56 | 5.0 ± 0.2 | 4.5 ± 0.2 | 8.3 ± 0.4 | 8.1 ± 0.3 | 8.0 ± 0.4 | 2.17 ± 0.09 | 2.09 ± 0.09 | 10.2 ± 0.4 | 10.6 ± 0.5 | 10.5 ± 0.6 | 2.97 ± 0.13 | 2.79 ± 0.11 | 8.7 ± 0.4 | 8.3 ± 0.4 | 7.9 ± 0.4
Al | 5.5 ± 0.2 | 4.4 ± 0.2 | 9.1 ± 0.4 | 8.5 ± 0.4 | 7.9 ± 0.4 | 2.28 ± 0.10 | 2.22 ± 0.09 | 11.9 ± 0.5 | 11.9 ± 0.5 | 12.2 ± 0.6 | 3.01 ± 0.13 | 2.88 ± 0.12 | 8.4 ± 0.4 | 8.5 ± 0.4 | 8.2 ± 0.4

## Slide 48: Context and Background: CROCUS
Experimental zero power reactor
Two fuel zones
  Inner zone: 336 enriched at 1.806 wt.%
  Outer zone: 174 enriched at 0.947 wt.%
Criticality control systems
  2 control rods (privileged for PETALE)
  Spillway for adjustable water level
4 operation monitors
  2 fission chambers E/W (power monitors)
  2 ionization chambers N/S
Video space