## Slide 1: Delayed neutron data measurements for the fast neutron induced fission of 238U at the PTB Ion Accelerator facility
ARIEL final meeting – 17th-19th January 2024
1 CEA/DES Cadarache
2 ILL, Grenoble
3 PTB, Braunschweig
4 GANIL, Caen
5 IN2P3 / LP2i Bordeaux
6 IN2P3 / LPSC Grenoble
D.Belverge1, P.Leconte1, B.Geslot1, G.Kessedjian1, R. Combe1 P.Mutti2,
F.Rodiac1, E.Pirovano3, B.Lutz3, X.Ledoux4, L.Mathieu5, O.Meplan6

## Slide 2: Summary
Context of work
Principle of the measurement
Experimental setup
ALDEN-U238 campaigns: First results
Conclusions and outlooks

## Slide 3: Context of work
1

## Slide 4
4
Delayed neutrons
  0,5 – 2,5 % of the emitted neutrons
  Emean  500 keV
  Emitted 1 ms - 1 min after fission
  Key role in nuclear reactors control and safety
  Microscopic data: associated to each precursor (FY, Pn)
  Macroscopic data: integrated over groups of precursors
Precursor
Emitter
Delayed neutron
Fission
Prompt emission
βn- decay
Nucleus + neutron
Fission fragments
Fission products
Delayed neutrons
Context: The delayed neutrons (DN)

## Slide 5
5
From Spriggs & al, « An 8-Group Delayed Neutron Model Based on a Consistent Set of Half-lives » (1998)
i : considered group
k : group I precursors

Exact model
Groups model(G = 8)
Delayed neutron multiplicity νd
Kinetics parameters describing the emission : group parameters (ai, λi)
Mean number of delayed neutrons emitted after fission
Precursors gathered in 8 families  8 relative abundances (ai)
  Spriggs model (1997)
Group spectra
Measured in the past but with high uncertainties !
Context: The DN macroscopic data

## Slide 6
Account for 10 - 20 % of the βeff in thermal reactors *
More challenging experimental conditions
  Low cross sections and neutron flux
Subject of a PhD (2021 - )
2018
2019
2020
2021
ALDEN – 1
235U – thermal spectrum
ILL (Grenoble)
ALDEN – 2
235U – thermal spectrum
ILL (Grenoble)
ALDEN – 3
235U, 233U, 239Pu – thermal spectrum
ILL (Grenoble)
2021 - : 238U – fast spectrum !
Average Lifetime of Delayed Neutrons (2018 - )
  New evaluation of the delayed neutrons macroscopic data: νd and (ai, λi)
  Reduced uncertainties
  Isotopes of interest for Gen2&3 reactors
βeff : effective delayed-neutron fraction, fraction of fissions induced by delayed neutrons
* V. Zammit-Averlant. Validation Integrale des Estimations du Parametre Beta Effectif pour les Reacteurs MOX et Incinerateurs. PhD thesis, Universite Aix-Marseille I, 1998.
Context: the ALDEN collaboration

## Slide 7
7
Experimental data: insufficient quality
  Uncertainties: 7 – 10 %
  No identifiable trend (< 5 MeV)
  Gap with no data (7 – 14 MeV)
New experimental data needed
  Target accuracy < 5 %
  1 – 5 MeV : reactor calculations
  7 – 20 MeV : nuclear physics model
Delayed neutron multiplicity
Discrepancies between evaluations
  Up to 8 % between ENDF/B-VIII.0 and JEFF-3.3
2 measurement only analysed with the 8 groups model - 3.75 MeV and 14 MeV
Group abundances:
Context: Motivation and state of the art for 238U(nf, f)

## Slide 8: Principle of the measurement
2

## Slide 9
“Macroscopic” technique: measurement of the integral of all delayed neutrons precursors
Example of experimental curve obtained for 235U – From D.Foligno PhD (2019)
Phase 2
Decay
Phase 1 Irradiation
Phase 1: Irradiation – creation of precursors
Phase 2: Decay – delayed neutrons counting
Principle of the measurement: In theory …

## Slide 10
Phase 1: Irradiation – creation of precursors
Phase 2: Decay – delayed neutrons counting
F: Fission rate in the sample
εp, d,i: Detector efficiency for prompt neutrons / delayed neutrons from group i
Phase 2
Phase 1
End of irradiation
“Macroscopic” technique: measurement of the integral of all delayed neutrons precursors
Principle of the measurement: In theory …

## Slide 11
Phase 1: Irradiation – creation of precursors
Phase 2: Decay – delayed neutrons counting
F: Fission rate in the sample
εp, d,i: Detector efficiency for prompt neutrons / delayed neutrons from group i
For tirr >> max(Ti,1/2) (saturation of the precursors population)
Challenges:
  Irradiation cut off: efficient and fast
  νd measurement: saturation of precursors population
  ai measurement: low background
Phase 2
Phase 1
End of irradiation
“Macroscopic” technique: measurement of the integral of all delayed neutrons precursors
Principle of the measurement: In theory …

## Slide 12
12
νd : short cycles (ex. 2s on / 0.2s off)
  Short tmeasurement
    νd is obtained at the beginning of the decay phase
  Short tirrad.
    Compromise between precursors saturation and statistics
  Precursors equilibrium built during the first cycles (≈ 10 min.)
Abundances: long cycles (ex. 50s on / 300s off)
  Long tmeasurement
    Counting of the delayed neutrons emitted from the 8 groups (T1/2, i = 0.195 – 55.6s)
  Long tirrad.
    Precursors equilibrium built for each cycle
 Cycles of irradiation / decay to increase the statistic in a limited time !
 After summation of the cycles:
t = 0 end of irradiation
tirr irradiation duration
tm cycle duration
Principle of the measurement: … and in practice !

## Slide 13: Experimental setup
3

## Slide 14
Monoenergetic neutron flux between 1 and 20 MeV
  Reactions: T(p, n), D(d, n), T(d, n)
Similar measurements performed in the past
  Delayed neutron measurements of 232Th neutron-induced fission, X.Ledoux, D.Dore et al., 2014
From R. Nolte et D. J. Thomas, « Monoenergetic fast neutron reference fields: I. Neutron production » (2011)
Low scatter hall - PIAF
D + d
3.5 – 8 MeV
T + p
1.2 – 3.2 MeV
T + d
14 - 19 MeV
PTB Ion Accelerator Facility (PIAF, Braunschweig, Germany)
Experimental setup

## Slide 15
Protons
Deuterons
Target
Tritium or Deuterium
Neutrons
Reactions
T(p, n), D(d,n) et T(d,n)
Magnetic deflection
Acceleration
Tandetron
Cyclotron
Beam cut off
En
7 – 14.7 MeV
En
1.2 – 6.8 MeV
14.8 – 19 MeV
Typical fluxes (n . cm-2 . s-1)
  ILL : 109 (PF1B)
  PTB : 2 . 103 – 2 . 104 (at 1 m)
* 10-5 !!!
PTB Ion Accelerator Facility (PIAF, Braunschweig, Germany)
Experimental setup

## Slide 16
Rear view of LOENIEv2
  - Polyethylene cylinder
     Neutron moderation
  - 16 3He counters
     Thermal neutron detection
  - Flexibore
     Thermal neutron absorption, noise reduction
Neutron detector: LOENIEv2
 Flat efficiency between 0.1 and 1 MeV (≈ 12%)
Experimental setup

## Slide 17
- Purity: | 99.8% (238U)
- Mass: | 30 g
- Diameter: | 15 mm
- Height: | 9.7 mm
Plug
Container
Sample
Sample: uranium metal
Inside LOENIEv2  Start measuring as soon as irradiation stops
Close to LOENIEv2 entrance  Compromise detection efficiency / fission rate
  - Polyethylene cylinder
     Neutron moderation
  - 16 3He counters
     Thermal neutron detection
  - Flexibore
     Thermal neutron absorption, noise reduction
Neutron detector: LOENIEv2
 Flat efficiency between 0.1 and 1 MeV (≈ 12%)
Sample in irradiation position
Experimental setup

## Slide 18
Proximity with the neutron production target (few cm)
  Maximisation of the fission rate
  Saturation of the acquisition during irradiations
   Inhibition of the 3He counters (except for the rising and falling edges)
   Synchronisation with the accelerator
- Purity: | 99.8% (238U)
- Mass: | 30 g
- Diameter: | 15 mm
- Height: | 9.7 mm
Plug
Container
Sample
Sample: uranium metal
Inside LOENIEv2  Start measuring as soon as irradiation stops
Close to LOENIEv2 entrance  Compromise detection efficiency / fission rate
  - Polyethylene cylinder
     Neutron moderation
  - 16 3He counters
     Thermal neutron detection
  - Flexibore
     Thermal neutron absorption, noise reduction
Neutron detector: LOENIEv2
 Flat efficiency between 0.1 and 1 MeV (≈ 12%)
Tritium solid target (top)
Deuterium gas target (down)
Sample in irradiation position
Experimental setup

## Slide 19: ALDEN-U238 campaigns: First results
4

## Slide 20: ALDEN-U238 campaigns: First results
2 * test week : Dec. 2022 and June 2023
2 * measurement campaign (2 weeks each)
  ALDEN-4 (Feb. 2023) : 8 νd + 3 abundances measurement  En = 1.5 – 2.5 – 3 – 4 - 5 – 6.5 - 14.8 – 19 MeV (Tandetron)
  ALDEN-5 (Sept. 2023) : 7 νd measurements  En = 2 – 3.5 – 6 MeV (Tandetron) + 8 – 10 – 12.2 – 14.7 MeV (Cyclotron)
Overview

## Slide 21: ALDEN-U238 campaigns: First results
2 * test week : Dec. 2022 and June 2023
2 * measurement campaign (2 weeks each)
  ALDEN-4 (Feb. 2023) : 8 νd + 3 abundances measurement  En = 1.5 – 2.5 – 3 – 4 - 5 – 6.5 - 14.8 – 19 MeV (Tandetron)
  ALDEN-5 (Sept. 2023) : 7 νd measurements  En = 2 – 3.5 – 6 MeV (Tandetron) + 8 – 10 – 12.2 – 14.7 MeV (Cyclotron)
≈ 225 h of beam time !
7 experimenters
Overview

## Slide 22: ALDEN-U238 campaigns: First results
Neutron flux calibration (PIAF staff) (2h)
Detector placement (1h)
Optimisation / measurement of the background and beam cut off duration (1 – 2h)
Neutron flux calibration with dosimetry (30’ – 1h)
  Measurement of the short-lived radionuclides at the facility
νd / abundances measurement (1 – 7h)
Typical day (1 energy / day)
Measurement of the distance between LOENIEv2 and the accelerator
Stack of dosimeters
Placement and irradiation of the sample

## Slide 23: ALDEN-U238 campaigns: First results
Analysis process: 3 main steps
Detector efficiency estimation
  Monte-Carlo model of LOENIEv2
  Experimental validation with an AmBe neutron source
For each energy !
Encapsulation and counting of an AmBe neutron source
Dosimeters placement and counting (left, centre)
Post-irradiation counting of the sample (right)
Irradiation
Delayed neutrons counting
Irradiation
Example of delayed neutron counting curve obtained
(νd measurement)
Delayed neutron counting curves production
  Many step to process the acquisition files (conversion to readable format, synchronisation and summation of cycles, dead time correction …)
Fission rate estimation (3 methods tested)
  Neutron flux monitoring
  Dosimetry (Indium, Nickel, Cobalt, Magnesium, Iron, Titanium, Niobium)
  Sample activation (1st energy of each campaign)

## Slide 24: ALDEN-U238 campaigns: First results
11 νd measurements analysed (for monoenergetic flux)
Good agreement overall with the literature
Reduced uncertainties: 2 – 3 %
  Remaining geometrical uncertainties to be propagated
νd lower than expected at ≈ 2 MeV
Apparent decrease between 1.5 and 2 MeV
  Evolution of the precursors Fission Yields ?
νd energy dependence

## Slide 25: Conclusions and outlooks
5

## Slide 26: Conclusions and outlooks
Four weeks of measurements performed at the PTB Ion Accelerator Facility (Germany) in 2023
15 delayed neutron yield measurements for 238U (1.5 – 19 MeV)
3 group abundances measurements (2.5, 5 and 14.8 MeV)
11 νd measurements analysed yet
Outlooks
Analysis of the 3 ai measurements
Analysis of the 4 remaining νd measurements (10, 12, 14.2 and 19 MeV)
  Non monoenergetic neutron flux due to contaminations (D break up reactions / impurities in the target)
  Additional measurements required (TOF)  performed by PIAF staff in the beginning of 2024
Evaluation of the νd energy dependence + comparison with the current evaluations for reactor applications
Submission of an article on the νd measurements to a peer-reviewed journal by the end of 2024
Conclusion

## Slide 27: Thank you for your attention
CEA CADARACHE
13115 Saint-Paul-lez-Durance Cedex
France
dorian.belverge@cea.fr
From left to right: P.Leconte, X.Ledoux, D.Belverge, E.Pirovano, L.Mathieu
Acknowledgment
Special thanks to the PIAF technical STAFF for their support !
This project has received funding from the Euratom research and training programm 2014-2018 under grant agreement No 847594 (ARIEL)
This project was partly funded by I3P (CEA, EdF, Framatome).

## Slide 28: Appendices

## Slide 29: Appendices: Principle of the measurement
29
νd measurement: short cycles (e.g. 2s on / 0.2s off)
  Short tdecay: νd obtained at the beginning of the decay phase
  tirr: compromise between precursors saturation and statistics
  Equilibrium built by the first cycles, maintained by the following
   Cycles 2/0.2 s: 95% of the saturation
Simulation of delayed neutrons counting in LOENIEv2 for cycles 2-0.2s – Energy 2.5 MeV
Simulation of the delayed neutrons counting in LOENIEv2 per group for cycles 50 - 300s – Energy 2.5 MeV
ai measurement: long cycles (e.g. 50s on – 300s off)
  Long tdecay: counting delayed neutrons emitted from the 8 groups
    T1/2, i = 0.195 – 55.6s
  Long tirr: equilibrium must be built for each cycle
  Background estimation during the last 50s
    DN emission negligible after 5 x max(T1/2, i)

## Slide 30: Appendices: Experimental setup
Alignment of the detector
Front face with lasers
Rear face with telescopes

## Slide 31: Appendices: Experimental setup
Measurement of the distance between LOENIEv2 and the accelerator
Modified depth gauge used to measure the distance separating LOENIEv2 from the target

## Slide 32: Appendices: Experimental setup
Placement of the 238U sample
Three wings aluminium holder used to ensure radial centring
238U sample in irradiation position
Insertion of the 238U sample inside LOENIEv2
Model of a stack of dosimeters in irradiation position

## Slide 33: Appendices: Experimental setup
Acquisition system
Generation of inhibition signal and synchronisation with the accelerator
Acquisition system

## Slide 34: Appendices: Experimental setup
PIAF HPGe detector
Neutron source measured in P4
Sample + europium source
Dosimeter measurement in P1

## Slide 35: Appendices: Analysis
Fission rate estimation (2 methods)
1 : Flux calibration and monitoring performed by PIAF
Real fission rate
(s-1)
Simulated fission rate
(nsource-1)
Simulated Φsurf (1m, 0°)
« open field »
(n . cm-2 . nsource-1)
TRIPOLI-4® model of the setup
E = f(θ) and I = f(θ) distributions of the sources
Real Φsurf (1m, 0°)
« open field »
(n . cm-2 . s-1)
Neutron monitor counting rate during the measurement
PIAF calibration
Simulation of the experimental setup with TRIPOLI-4®
Emitted flux (4π)
(n . s-1)
NeusDesc
TRIPOLI-4®
Upper-view of the PIAF experimental hall
Monitor 2
97 °
Monitor 1
16 °
Source

## Slide 36: Appendices: Analysis
Fission rate estimation (2 methods)
2 : Flux calibration using dosimetry
Real fission rate
(s-1)
Simulated fission rate
(nsource-1)
Emitted flux (4π)
(n . s-1)
TRIPOLI-4® model of the setup
E = f(θ) and I = f(θ) distributions of the sources
Fluctuation of the neutron flux
Neutron monitor counting rate during the measurement
Neutron monitor counting rate during the dosimeters irradiation
Dosimeters measured reaction rates
(s-1)
Dosimeters irradiation
Dosimeters activity measurement
(PTB / LBA)
Gamma counting of a dosimeter using the HPGe detector of the facility
NeusDesc
Dosimeters simulated reaction rates
(nsource-1)
TRIPOLI-4®

## Slide 37: Appendices: Analysis
Fission rate estimation (2 methods)
Additional method: 238U sample activation
  Only available for the 1st energy of each campaign  Energy 14.8 MeV : FY better known
  Validation of the 2 other methods
Cumulative Fission Yields
Real fission rate
(s-1)
Fluctuation of the neutron flux
Activities of fission products
(s-1)
238U sample irradiation
Sample activity measurement
(PTB)
92Sr, 135I
JEFF-3.11
Gamma counting of the sample after activation
No simulation required !!!

## Slide 38: Appendices: Analysis
Dosimetry
Dosimeter | Isotope | Reaction | Product | T ½ | Threshold | Rays (keV)
Indium | 113In | (n, g) | 114mIn | 49.5 j | Thermal | 190.3 – 558.4 – 725.2
 | 113In | (n, n’) | 113mIn | 1.66 h | 0.5 MeV | 391.7
 | 115In | (n, g) | 116mIn | 54.3’ | Thermal | 138.3 - 416.9 – 818.7 – 1097.3 – 1293.5 – 1507.4
 | 115In | (n, n’) | 115mIn | 4.5 h | 340 keV | 336.24
 | 115In | (n, 2n) | 114mIn | 49.5 j | 9 MeV | 190.3 – 558.4 – 725.2
Nickel | 58Ni | (n, p) | 58Co | 70.5 j | 0.4 MeV | 810.76
 | 60Ni | (n, p) | 60Co | 5.3 a | 4 MeV | 1173.2 – 1332.5
 | 58Ni | (n, 2n) | 57Ni | 1.5 j | 12.5 MeV | 136.5 – 1377.6
Cobalt | 59Co | (n, g) | 60Co | 5.3 a | Thermal | 1173.2 – 1332.5
 | 59Co | (n, p) | 59Fe | 44.5 j | 3 MeV | 192.3 – 1099.2 – 1291.6
 | 59Co | (n, α) | 56Mn | 2.6 h | 5 MeV | 846.8 – 1810.7
 | 59Co | (n, 2n) | 58Co | 71 j | 11 MeV | 810.76
Magnesium | 24Mg | (n, p) | 24Na | 15 h | 6 MeV | 1368.6
Iron | 58Fe | (n, g) | 59Fe | 44.5 j | Thermal | 1099.2 – 1291.6
 | 54Fe | (n, p) | 54Mn | 312 j | 2 MeV | 834.8
 | 56Fe | (n, p) | 56Mn | 2.6 h | 5 MeV | 846.8
Titanium | 47Ti | (n, p) | 47Sc | 3.3 j | 1 MeV | 159.4
 | 46Ti | (n, p) | 46Sc | 83.8 j | 2 MeV | 889.3 – 1120.5
 | 48Ti | (n, p) | 48Sc | 1.8 j | 4 MeV | 175.4 – 983.5 – 1037.5 – 1212.8 – 1312.12
Niobium | 93Nb | (n, 2n) | 92mNb | 10.15 j | 9 MeV | 912.6 – 934.44

## Slide 39: Appendices: Analysis
Dead time correction
Non-paralyzable model:
Paralyzable model:
Dead time parameter τ = 7.61 ± 0.07 µs

## Slide 40
Delayed neutrons counting
Irradiation
Background measurement
Total counting rate in LOENIEv2, cycles “50 – 300s
Summation of 61 cycles (6h)
n(t = tirr) ≈ 450 counts/s
Background ≈ 16 counts/s
tirr / tdecay ≈ 50 / 300 s
Tcut off ≈ 15 ms
   Veto time after end of irradiation
Preliminary decay curves
 ai measurement at 14.8 MeV (2h, 3 121 cycles)
Preliminary
Appendices: First results