## Slide 1: Status of the TCCP assembly
Hana HAVLIKOVA, on behalf of CERN SY-STI-TCD
11/12/2023

## Slide 2: Summary
Requirements for TCCP device
From requirements to operational designs
Impedance simulations
Schedule

## Slide 3: Target Collimator Crystal for Precession (TCCP)
TCCS
TCCP

## Slide 4: Requirements for TCCPs (Goniometers) devices
  Compatibility with UHV and bake-out requirements
  Monitoring of crystal motion and temperature
Crystal motion
  Linear motion towards the beam
  Yaw control to reach channelling angle
Target motion
  Linear motion towards the beam (independent from the crystal motion)
  Distance target-crystal 100-500 µm
  Compatibility with impedance losses in operation position
  Low-intensity runs (~ protons at 7 TeV)
Compatibility with impedance losses in parking position
  All types of run (including HL runs)

## Slide 5: Design to requirement Target Collimator Primary Crystal (TCPC)
  Device existing and employed in CERN
  Respecting all the requirements regarding the crystal motion
  Needed improvements:
  No target
  Not adapted for the TCCP crystal (size, weight)
  Replacement chamber not suited for TCCP due to space constraints

## Slide 6: Requirement for TCCP (Goniometers) devices TCCP crystal assembly characteristics
Courtesy of INFN
TCPC
TCCP
Property | TCPC | TCCP
Crystal length along the beam | 4±0.1 mm | 70±5 mm
Minimal thickness in bending (vertical) direction | 2±0.1 mm | 2±0.1 mm
Minimal width in horizontal direction | 35 mm | 8±0.1 mm
Weight ported by rotational stage | ~100 g | ~350 g

## Slide 7: Design to requirement TCPC Rotational stage re-use
Piston
Pre-load spring
Rotor
Wedge
Stopper
Blades
Piezoelectric material
  Heavier crystal of the TCCP:
  Simulation to evaluate the impact on CoG and inertia
  Actuator control tested by CEM on existing rotational stage with a 350g crystal assembly mock-up

## Slide 8: Design to requirement Motion assembly
Bender + crystal
Rotation actuator
Retroreflectors
UHV Linear bearings
Crystal support
  Crystal support adjusted for the new shape of the crystal

## Slide 9: Design to requirement Motion assembly
Target
Target alignment system
Target linear motion system
Target holder
  Linear motion system for target identical to rotational stage
  Independent alignment system for target to bring it to the correct distance with respect to the crystal 100 - 500µm

## Slide 10: Design to requirement Motion assembly
Support linear stages
  Support plate for linear motion system made separate from the tank
  Allows motion and assembly checks before insertion in the tank
  Reduce the complexity of tank machining

## Slide 11: Impedance losses in the TCPCs
* Quartullo, Danilo et al. “Electromagnetic characterization of the crystal primary collimators for the HL-LHC.” Nuclear Instruments & Methods in Physics Research Section A-accelerators Spectrometers Detectors and Associated Equipment 1010 (2021): 165465.
TCPC with crystal in operating position for HL ions runs: up to 9W*
TCPC with crystal in parking position for HL protons runs: up to 595W* without replacement chamber
Goals for TCCP design:
Losses with crystal in operating position during low intensity runs acceptable without active cooling
Losses with crystal in parking position during HL proton runs acceptable without replacement chamber and active cooling
TCPC with replacement chamber retracted *

## Slide 12: Impedance losses reduction strategy for TCCP
Design choices:
RF beam tube in the tank cavity
Isolation of crystal bender and target with dielectric supports
RF contacts on cut-outs in the tube to close the RF cavity
RF contacts
Tank cavity
Inner cavity beam tube
«RF closed» cavity

## Slide 13: Impedance simulation of TCCP cavity
Courtesy of Chiara Antuano, BE/ABP
TCPC parking position HL runs | TCCP parking position HL runs
595 W | 1.6 W
Design greatly reduces losses without use of a replacement chamber | 
TCCP operation position low intensity runs | TCCP operation position HL runs
<1W | ~100W
Design compatible with PoC settings Still not suitable for use in HL runs | 

## Slide 14: Design to requirement Motion assembly
Inner cavity beam tube
RF contacts
Metallic plate
Dielectric supports
Metallic plate to create contacts when crystal is in operational position

## Slide 15: Design to requirement Tank
Improvements
  Ease of manufacturing
  Separate linear systems support assembly
  Survey reference point support installed directly on the tank
Survey reference support

## Slide 16: Design to requirement General assembly
  Mounted on standard collimator support
  Counter-weight
  Lifting ears
  Optical heads orientation modified due to B1/B2 organisation
Counterweight
Lifting ears
B2
B1
Access from the corridor
Optical heads

## Slide 17: From design to operations Schedule
Design
Drawing redaction
Drawing verification, signature
Procurement
Assembly
Validation tests
Device installation
Currently
January 2024
February - May 2024
June - September 2024
YETS 24-25
October - November 2024

## Slide 18: Conclusion
New design inspired from existing TCPC
Initial simulation demonstrated the compatibility of design with impedance losses mitigation
3D design of equipment is complete
The equipment will be installed during YETS 24-25
The proposed design is adequate for TWOCRYST PoC but not for final experiment with HL protons

## Slide 19
Thank you for your attention!
Questions?