## Slide 1
rasha.abukeshek@ijclab.in2p3.fr
Lattice design and beam optics optimization of the PERLE facility
Assemblée Générale du Pôle Accélérateurs
December 2023
Presented by
Rasha ABUKESHEK
Under the direction of
Achille STOCCHI & Hadil ABUALROB

## Slide 2: Outline
Introduction
PERLE optics
Magnet design
  B-com magnet
  Quadrupole magnets
Preliminary study of PERLE lattice errors
  Misalignment errors
  Field errors
250 MeV PERLE machine

## Slide 3
Injector
Beam dump
Superconducting Linac
ERL Loop
acceleration
deceleration
Acceleration to the top energy
Beam used in IP
Kinetic energy of used beam recycled to re-excite cavities
New beam injected in ERL loop
The benefits:
Reduce accelerator power consumption
Dumping the beam at injection power
Multi-pass configuration: High average current carrying capability (no more RF power limit) + High average beam power in a compact machine
Acceleration:
RF power provided to cavities
The idea:
(1)
(2)
(3)
(4)
(1’)
ERL Loop
(2’)…
Deceleration:
180° RF Phase shift
Courtesy of Walid Kaabi
ERL (Energy Recovery Linac) concept

## Slide 4: PERLE: Powerful ERL for Experiments
Spreader/Recombiner
  Connect LINAC to arcs section.
  One common dipole magnet called the B-com magnet.
Dipole
Quadrupole
RF cavity
Top view
29 m
5.5 m
10 m
10 m
DE = 82.2 MeV
7 MeV
7 MeV
9 m
2 : 4 : 6
1 : 3 : 5
DE = 82.2 MeV
PERLE: first high-power multi-turn ERL, based on SRF technology, designed to operate at 10MW (20 mA, 500 MeV) power regime
ERL technology development for future energy and intensity frontier machines (same technological choices of LHeC).
Facility platform for nuclear applications (DESTIN).
LINAC
  Two cryomodules each of four 5-cell SRF cavities.
Arcs
  6 arcs for a three-turn configuration.
Staging with 250 MeV version
Demonstration of ERL with 6 passes at high current (with half of the power)
Three straight sections replacing spreader, recombiner, and 2nd Linac

## Slide 5: PERLE Optics
Courtesy to Alex Fomin
Name | Number |  | L, cm | ¦B¦, T |  | 
 | 250 MeV | 500 MeV |  | 250 MeV | 500 MeV | 
B-Com 3-lines | 2 | 4 | 33 | 0.451 | 0.866 | 0.866
B-Com 2-lines | 2 | 4 | 33 | 0.451 | 0.866 | 0.866
R-Bend 33cm | 8 | 16 | 33 | 0.451 | 0.873 | 0.873
S-Bend 33cm | 6 | 12 | 33 | 0.472 | 0.907 | 0.907
 | 18 |  |  | 0.472 | 1.342 | 1.342
S-Bend 66cm | 18 |  | 66 | 0.453 | 1.323 | 1.323
ERL Quads | 127 | 148 | 15 | Max ¦G¦, T/m |  | 
 |  |  |  | 23 |  | 55
 |  |  | 10 |  |  | 
Injector/Dump Quads | 15 |  | 5 | 1.2 |  | 
Total number of dipole (ERL only):
  60 dipoles for 250 MeV version
  78 dipoles for 500 MeV version
R-Bend 33 cm is used in the spreaders for Arcs 3, 4, 5, and 6.
S-Bend 33 cm is used in the spreader of Arcs 1, and 2 (vertical) and in Arcs 1, 2, and 3 (horizontal).

## Slide 6: B-com Magnet
This work is in collaboration with Jay Benesch from JLab.
Yoke material: standard steel (C content < 0.1%)
Tool: Opera 3D
Common between the three arcs.
Horizontal field magnet  Vertical beam split at three different energies.
30° bending angle.
Specification and design
Coil design

## Slide 7: B-com Magnet
Field calculations
A Pole blend radius of 8 mm with edge chamfer of 6 mm radius
Field uniformity within ±100 mm which is suitable for the 88 mm shift for the lowest energetic beam.
along the magnet length
for 0.34 m yoke length  B = 0.88 T

## Slide 8: B-com Magnet
Energy | b1 | b2 | b3 | b4 | b5 | 
171MeV | -2.90E+01 | -1.11E-02 | 3.06E-03 | 2.19E-04 | -4.99E-04 | 3.594E-04
336MeV | -2.81E+01 | 1.84E-03 | 1.14E-04 | 1.05E-04 | -4.69E-04 | 6.79E-05
500MeV | -2.79E+01 | 2.77E-03 | 3.85E-04 | -1.77E-06 | -2.49E-04 | 1.01E-04
Energy | b1 | b2 | b3 | b4 | b5 | 
171MeV | -2.90E+01 | -1.11E-02 | 3.06E-03 | 2.19E-04 | -4.99E-04 | 3.594E-04
336MeV | -2.81E+01 | 1.84E-03 | 1.14E-04 | 1.05E-04 | -4.69E-04 | 6.79E-05
500MeV | -2.79E+01 | 2.77E-03 | 3.85E-04 | -1.77E-06 | -2.49E-04 | 1.01E-04
Harmonic content
0.036% field homogeneity along the beam path.
Quadrupole and sextupole components can be dealt with in the lattice.
To ensure the quality of the field used to guide the electrons along a certain trajectory with a precise bending angle

## Slide 9: B-com Magnet
The cooling circuit parameters were calculated for different current values.
Goal: achieve the minimum possible current to power the magnet while ensuring adequate coil cooling.
Turbulent water flow must be achieved  Reynolds number > 4000
Coil and cooling circuit
is the minimum value possible.
Courtesy of Abdalrhman Marshoud – Internship student from An-Najah University
Excitation current calculated for B = 0.87 T
is
NI = 11520.263 A.turn

## Slide 10: Quadrupole Magnets
Arcs Section
Parameters | Arcs
Height | 250 mm
Yoke thickness | 35 mm
Length | 150 mm
Aperture radius | 20 mm
Pole width | 44 mm
NI per coil | 1750.7 A.turn
Current density J | 2.882 A/
Gradient | 34.15 T/m
Parameters | Arcs
Height | 250 mm
Yoke thickness | 35 mm
Length | 150 mm
Aperture radius | 20 mm
Pole width | 44 mm
NI per coil | 1750.7 A.turn
Current density J | 
Gradient | 34.15 T/m
Quadrupole series of 15 cm long was designed.
Merger Section
Maximum gradient of 1.2 T/m.
Available vertical space from the B-com magnet of around 33 cm.
Merger
100 mm
15 mm
50 mm
20 mm
17 mm
318.31 A.turn
2.62 A/
3 T/m
Merger
100 mm
15 mm
50 mm
20 mm
17 mm
318.31 A.turn
3 T/m
Max. gradient (250 MeV) = 23 T/m
Twice the required gradient

## Slide 11: Beam Optics
The lattice is tuned so that
The Dispersion function is Zero at the exit of each arc.
The Beta function is the same at the entrance and exit of each arc.
The Alfa function changes the sign between the arc entrance and exit.
Twiss functions through Arc1 for the first-order 500 MeV lattice with perfect elements on MADX.
The following work is for 500 MeV version
Effect of optics misalignment:
Lateral quadrupole misalignment is equivalent to an aligned quadrupole + small dipole
)
Additional deflection angle of the beam
Small offset

## Slide 12: Optics misalignments
Misalignments were introduced to all the quadrupoles in Arc1.
Transverse errors in the position of the quads the xy-plane: are only considered.
Simulations were done using MADX*
The errors are represented as a Gaussian distribution with standard deviation 𝜎=
* https://madx.web.cern.ch/madx/

## Slide 13: Optics misalignments
1000 simulations were performed.
Twiss functions were deduced at the exit of the arc.
Standard deviation
Standard deviation
Standard deviation
Standard deviation
Different values of the transverse alignment errors were introduced.
The standard deviation of DX at the exit of the Arc is extracted.
The error value affects linearly the dispersion

## Slide 14: Field errors
Relative field errors were introduced to the first B-com in the spreader and the B-com-R in the merger section.
The values of the first four higher relative harmonics () were considered.
An increase in the Beta function is noticed at the exit
 Additional quadrupole component change the beta function and possibly increase the beam size
Twiss | Perfect element
[m] | 0.00
[m] | 0.00
 | 0.00
 | 0.00
[m] | 8.63544
[m] | 8.63478
Twiss | Perfect element
 | 0.00
 | 0.00
 | 0.00
 | 0.00
 | 8.63544
 | 8.63478
Twiss functions at the exit of Arc1
With field errors
0.00
-0.00301
0.00
0.00059
8.70493
9.73175

## Slide 15: 250 MeV PERLE Lattice
No errors
With errors
Primary studies of lattice errors for the 250 MeV machine.
Quadrupole misalignments affected the dispersion function.
Studies will be carried out using BMAD instead of MADX.
The standard deviation of the dispersion showed an exaggerated value.

## Slide 16: Conclusion
The B-com magnet is designed to generate vertical field of 0.7 T and field integral of 0.88 T along the magnet length with harmonic content in the order of meeting the accepted tolerances of the beam dynamics.
Associated cooling circuit parameters were calculated for different coil configurations (conductor area, number of turns, different arrangements) to decrease the current from the power supply.
Quadrupole magnets of the Arcs and injector are designed. The coil circuit is under optimization.
The effect of transverse optics misalignments on the Twiss functions (, , , , , ) was studied.
The B-com field harmonics were introduced to the lattice, further investigation on its effect is undergoing.
Outlook
Focus the study on the 250 MeV version of PERLE using MADX/BMAD.
Complete the lattice error study to conclude the orbit stability and lattice acceptance.
Complete the design of the magnet elements: dipoles in arcs and spreader (ongoing), chicane magnets, and quadrupole families. (maybe sextupole if decided).

## Slide 17
Merci Beaucoup!

## Slide 18
Back-up Slides

## Slide 19: PERLE @ Orsay
PERLE is the first multi-turn, high current ERL based on SRF technology to operate at 10 MW power.
Same technological choices of LHeC  PERLE will be a demonstrator for the multi-turn ERL for the LHeC.
PERLE will also be a facility platform for nuclear applications (DESTIN).
Cryomodule with 82 MV accelerating gradient.
3 acceleration passes  maximum energy 500 MeV
Dump energy: 7 MeV.

## Slide 20
Initial design with 3 pancakes of 10 turns each using conductors.
To reduce the needed current, smaller conductors are needed : conductors were investigated.
Coil Parameters | 88 | 55
Excitation current NI | 11520.2625 A.turn | 
Number of turns/coil | 56 = 30 | 89 = 72
Current | 384 A | 166.67
Current density J | 8.69 A/ | 9.34 A/
Material | Copper | 
Coil Parameters |  | 
Excitation current NI | 11520.2625 A.turn | 
Number of turns/coil |  | 
Current | 384 A | 166.67
Current density J |  | 
Material | Copper | 
Coil and cooling circuit
B-com Magnet

## Slide 21: Quadrupole Magnet
Arcs Section
Parameters | Value
Height | 250 mm
Yoke thickness | 35 mm
Length | 150 mm
Aperture radius | 20 mm
Pole width | 44 mm
NI per coil | 1750.7 A.turn
Current density J | 2.882 A/
Parameters | Value
Height | 250 mm
Yoke thickness | 35 mm
Length | 150 mm
Aperture radius | 20 mm
Pole width | 44 mm
NI per coil | 1750.7 A.turn
Current density J | 
Quadrupole series of 15 cm long was designed.
G = 34.15 T/m

## Slide 22: Quadrupole Magnet
Merger Section
All merger quadrupoles are 5 cm long (in z).
Maximum gradient of 1.2 T/m.
Available vertical space from the B-com magnet of around 33 cm.
Pole tip field = 0.07 T
Gradient G = 3 T/m
Parameters | Value
Height | 100 mm
Yoke thickness | 15 mm
Length | 50 mm
Aperture radius | 20 mm
Pole width | 17 mm
NI per coil | 318.31 A.turn
Current density J | 2.62 A/
Pole tip field | 0.07 T
Gradient | 3 T/m
Parameters | Value
Height | 100 mm
Yoke thickness | 15 mm
Length | 50 mm
Aperture radius | 20 mm
Pole width | 17 mm
NI per coil | 318.31 A.turn
Current density J | 
Pole tip field | 0.07 T
Gradient | 3 T/m

## Slide 23: Introducing Errors (500 MeV)
Mean value = 0.2055 m
Standard deviation
Mean value = 0.622 m
Standard deviation
Field errors
1000 simulations using Gaussian distribution around the relative quadrupolar component.

## Slide 24
250 MeV PERLE Lattice
250 MeV lattice from Alex Fomin by MADX.
Injector optics are not included, only the chicane magnet  Using predefined initial Betas.
For misalignments, the simulation is done turn by turn.
Turn1 (89 MeV) consists of: Spr1, Arc1, Str1, Arc2, Mrg1.

## Slide 25: Transverse Misalignment to Turn 1 (250 MeV)
Dispersion Function
Mean value = 0.00
Standard deviation
Mean value = 0.00
Standard deviation

## Slide 26: Transverse Misalignment to Turn 1 (250 MeV)
Mean value = 0.00
Standard deviation
Mean value = 0.00
Standard deviation
Beta Function

## Slide 27: Outlook
Focus on the 250 MeV version of PERLE.
Complete the lattice error study to conclude the orbit stability and lattice acceptance.
  Longitudinal misalignments.
  Tilt (angular misalignments).
  Field errors for all magnetic elements.
Complete the design of the magnet elements: dipoles in Arcs and spreader, chicane magnets, and quadrupole families. (maybe sextupole if decided).